## Slide 1: OPTIMIZED TRANSFERS BETWEEN EARTH-MOON INVARIANT MANIFOLDS
Speaker: Laurent Beauregard laurent.beauregard@isae-supaero.fr
Co-authors: Emmanuel Blazquez
Dr. Stéphanie Lizy-Destrez

## Slide 2
Context
Lunar orbital platform-Gateway (LOP-G)
Successor to the International Space Station will be the LOP-G (2022)
Allow easy surface access
Constant communication with Earth, few eclipses
On a L2 southern Near Rectilinear Halo orbit
  Period: 6.56 days
  Periapsis: 1500 km
  Apoapsis: 70 000 km

## Slide 3
Circular restricted three body problem
x
y
z
Centrifugal acceleration
Coriolis acceleration
Earth’s gravity
Moon’s gravity
Center of mass
Only massive bodies
  Earth and Moon
Moon’s orbit is circular
Third body is masslesss

## Slide 4
Halo orbits
Fixed point of the CR3PB exists
  Lagrange points
Closed orbit of the CR3PB exists
Halo orbits are 3 dimensional trajectories

## Slide 5
Parametrization
Several parametrizations exist
  Amplitude of Halo
  Periapsis
  Velocity at

## Slide 6
Objective
Comparison of far approach rendez-vous methods
  Low thrust (Orbit hopping)
  Lambert arcs
  Manifold methods
  Orbit of the LOP-G

## Slide 7
Quasi-static method
Two body
Hohmann transfer
(Limit ∞ thrust)
Low thrust trajectory
(Limit 0 thrust)

## Slide 8
Orbit hopping ~ Low thrust trajectory
Gives an upper bound on the cost between any two Halo orbits
Each intermediate stage is a closed orbit
Up to an
Covering all NRHOs ~ 100 m/s
Quasi-static method
Orbit hopping

## Slide 9
Two impulse maneuvers
Minimize over
  Departure point
  Arrival point
  Time of flight
Lambert arcs

## Slide 10
Most Halo orbits are unstable
The eigenvalues of the differential of the Poincaré map encodes this information
Except for a narrow range of Halos
  Continuation direction:
  Unstable direction:
  Stable direction:
  Center:
Manifolds
Propagate
forward
Propagate
backward
Unstable direction: Diverges
Stable direction: Converges
Unstable direction: Converges
Stable direction: Diverges

## Slide 11
Manifolds generation
Eigenvector corresponding to the unstable direction
Apply a perturbation ,
Manifolds are parametrized by
Unstable trajectories

## Slide 12
Manifolds method
Departure orbit A
Unstable manifold of A
Stable manifold of
B
Arrival orbit B
Low
Low
Intersection +
Intersection of two surfaces: Find such that

## Slide 13
Manifolds method
Triangulation of

## Slide 14
Manifolds intersection
Intersections of two triangulated surface can be done efficiently
By linear interpolation and refinement, the states can be recovered
Find the intersection that has lowest

## Slide 15
Jacobi constant
The CR3PB has a conservation of “Energy”; the Jacobi constant
Halo orbits

## Slide 16
Cases considered
LOP-G
LOP-G
14 different cases considered
Close orbits
Far orbits, two directions
Same Jacobi constant
Stability

## Slide 17
Results
The three methods are compared
If the orbits are close, then the three methods cost the same (within 10%)
For far orbit, the manifold is better for regular halo, worse for NRHO
For orbits of same energy, saving of 25%-45% is observed compared to Lambert arc

## Slide 18
Results
The three methods are compared
If the orbits are close, then the three methods cost the same (within 10%)
For far orbit, the manifold is better for regular halo, worse for NRHO
For orbits of same energy, saving of 25%-45% is observed compared to Lambert arc

## Slide 19
Results
The three methods are compared
If the orbits are close, then the three methods cost the same (within 10%)
For far orbit, the manifold is better for regular halo, worse for NRHO
For orbits of same energy, saving of 25%-45% is observed compared to Lambert arc

## Slide 20
Example: Same energy, LOP-G -> Halo
Low thrust
  173.05 m/s
Lambert arc (Green)
  146.2 m/s
Manifold
  80.3 m/s

## Slide 21
Conclusion
For close orbits: No substantial savings
Manifold method can provide substantial saving in the for far orbits, especially for same energy level (up to 45%)
Next steps
  Increase the number of search variables
  Check the robustness of the trajectory in an ephemeris model

## Slide 22
Thank you
Thank you for your attention

## Slide 23
Bibliography
[1] “Lunar outpost sustaining human space exploration by utilizing in-situ resources with a focus on propellant production,” International Astronautical Congress 2018, IAC-18,A5,1,5,x46282.
[2] S. Lizy-Destrez, “Rendezvous optimization with an inhabited space station at EML2,” 25th International Symposium on Space Flight Dynamics, ISSFD, 2015.
[3] G. Gomez, A. Jorba, J. Masdemont, and C. Simo, “Study of the transfer from the earth to a halo orbit around the equilibrium pointl1,” Celestial Mechanics and Dynamical Astronomy, vol. 56, no. 4, pp. 541–562, Aug 1993.
[4] G. Gomez et al, “Connecting orbits and invariant manifolds in the spatial restricted three-body problem,” Caltech, 2004.
[5] V. Szebehely, “Theory of orbits. the restricted problem of three bodies,” Academic Press, New York, 1967.
[6] NASA, “General mission analysis tool (GMAT),” 2016.
[7] S. K. Wang et al., “Dynamical systems, the three-body problem and space mission design,” Caltech, 2000.
[8] Norman R. Lebovitz, “Ordinary differential equations, chapter 9 stability ii: maps and periodic orbits,” http://people.cs.uchicago.edu/ lebovitz/odes.html.
[9] D. Torre Sangra, E. Fantino, “Review of lambert’s problem,” 25th International Symposium on Space Flight Dynamics ISSFD, 2015.
[10] T. Moeller, “A fast triangle-triangle intersection test,” Stanford University, 1992.