## Slide 1: 25th SPINE workshop Mika Holmberg, Fabrice Cipriani, Grégoire Déprez, David Rodgers, Sebastien Hess, Thomas Nilsson ESA/TEC-EPS, ONERA, IRF 25/10/2018
Cassini plasma wake simulations compared to
Langmuir probe measurements

## Slide 2: Introduction – Studying the Enceladus plasma torus
The Cassini mission to Saturn, 2004-2017
New method to derive ion properties from LP sweeps
Plasma torus created from Enceladus’ subsurface ocean
Image credits: NASA/JPL-Caltech/AP/Space Science Institute
No correction for plasma wake effects
Small impact on statistical studies but, potentially, very important for case studies

## Slide 3: The Cassini model
Spacecraft model, excluding the lander Huygens
  Body h = 3.64 m, rmin = 1.00 m, rmax = 1.26 m
  High gain antenna h = 0.11 m, rmin = 1.08 m, rmax = 2.00 m
  MAG h = 0.56 m, l = 9.66 m
  CAPS/MIMI/INMS
  Search coil magnetometer and Langmuir probe (LP) (optional)
Cassini prior to launch
Image credits: NASA/JPL-Caltech
Blender model provided by Brian Kumanchik,
NASA/JPL-Caltech
Simplified model suitable for SPIS

## Slide 4: Simulation setup – Mesh and materials
Computational volume, egg-shaped 16 x 20 x 27 m
  100,281 tetrahedra
Materials
  Body BK2K, Black kapton
  High gain antenna PCBZ, White paint, assumed to be conductive
  MAG BK2K, Black kapton
  CAPS/MIMI/INMS BK2K, Black kapton
  Search coil mag. (optional) BK2K, Black kapton
  LP (optional) AU2K, Gold, actually TiN
All on one electrical node, except the LP
Material specifications of the multilayer insulation blankets from Stultz and Reeve 1995

## Slide 5: Simulation setup - The environment and the spacecraft
Time interval 2010-03-03 10:10 to 11:00
Inner to middle magnetosphere, inside the Enceladus plasma torus but outside the orbit of Enceladus at 3.95 RS
Close to cold plasma density maximum at 4.6 RS
X
Plasma flow in same direction as ring current (white arrow)
Gyroradii ion ~ 10 km and electron ~ 20 m
Debye length ~ 2 m

## Slide 6: Simulation setup – Global parameters
For time interval 2010-03-03 10:10 to 11:00
Parameter | Value | Reference
avPartNbPerCell | 50 | 
ne | 50 cm-3 | Holmberg et al. 2012, 2017
Te | 2 eV | Schippers et al. 2013
ne,h | 0.01 cm-3 | Schippers et al. 2008
Te,h | 500 eV | Schippers et al. 2008
ni | 50.01 cm-3 | Holmberg et al. 2012, 2017
Ti | 18 eV | Sittler et al. 2006, Thomsen et al. 2010
vi,θ | 28 km/s | Holmberg et al. 2012
Ion species | H2O+ | Young et al. 2005, Sittler et al. 2008
ZSun | 0.011 | 
vs/c,x, vs/c,y, vs/c,z | 0 – 13.2 km/s, -13.3 – 9.4 km/s, 8.2 – 8.7 km/s | The Cassini ephemeris tool from RPWS in Iowa
B | 100 nT | Estimated, assuming dipole field

## Slide 7: Simulation setup - The environment and the spacecraft
HGA pointing towards Earth and Sun, and spacecraft rolls
10:10 to 10:29 LP in undisturbed plasma flow
10:30 to 10:48 LP in region where the plasma flow is disturbed by the spacecraft, i.e., the ion wake
Plasma flow
*
Studied time interval, 2010-03-03
Relative flow direction (red), LP direction (blue), and the position of the s/c in Saturn Sun equatorial coordinates and over time
LP

## Slide 8: Simulation setup - The environment and the spacecraft
HGA pointing towards Earth and Sun, and spacecraft rolls
10:10 to 10:29 LP in undisturbed plasma flow
10:30 to 10:48 LP in region where the plasma flow is disturbed by the spacecraft, i.e., the ion wake
*
Studied time interval, 2010-03-03
Relative flow direction (red), LP direction (blue), and the position of the s/c in Saturn Sun equatorial coordinates and over time
Plasma flow
LP

## Slide 9: Simulation setup - The environment and the spacecraft
HGA pointing towards Earth and Sun, and spacecraft rolls
10:10 to 10:29 LP in undisturbed plasma flow
10:30 to 10:48 LP in region where the plasma flow is disturbed by the spacecraft, i.e., the ion wake
Plasma flow
*
Studied time interval, 2010-03-03
Relative flow direction (red), LP direction (blue), and the position of the s/c in Saturn Sun equatorial coordinates and over time
LP

## Slide 10: Simulation setup - The environment and the spacecraft
HGA pointing towards Earth and Sun, and spacecraft rolls
10:10 to 10:29 LP in undisturbed plasma flow
10:30 to 10:48 LP in region where the plasma flow is disturbed by the spacecraft, i.e., the ion wake
Plasma flow
*
Studied time interval, 2010-03-03
Relative flow direction (red), LP direction (blue), and the position of the s/c in Saturn Sun equatorial coordinates and over time
LP

## Slide 11: Simulation setup - The environment and the spacecraft
HGA pointing towards Earth and Sun, and spacecraft rolls
10:10 to 10:29 LP in undisturbed plasma flow
10:30 to 10:48 LP in region where the plasma flow is disturbed by the spacecraft, i.e., the ion wake
Plasma flow
*
Studied time interval, 2010-03-03
Relative flow direction (red), LP direction (blue), and the position of the s/c in Saturn Sun equatorial coordinates and over time
LP

## Slide 12: Results – Plasma wake structure
Ion density at the position of the probe
Studied time interval, 2010-03-03
Plasma flow
50
45
40
35
30
25
20
15
10
5
0
ni (cm-3)
d (m)
ni (cm-3)
ni (cm-3)
Vs/c
Plasma flow
Vs/c

## Slide 13: Results – Plasma wake structure
Ion density at the position of the probe
Studied time interval, 2010-03-03
Plasma flow
35
30
25
20
15
10
5
0
ni (cm-3)
d (m)
ni (cm-3)
ni (cm-3)
Vs/c
Plasma flow
Vs/c

## Slide 14: Results – Plasma wake structure
Ion density at the position of the probe
Studied time interval, 2010-03-03
Plasma flow
20.0
17.5
15.0
12.5
10.0
7.5
5.0
2.5
0.0
ni (cm-3)
d (m)
ni (cm-3)
ni (cm-3)
Vs/c
Plasma flow
Vs/c

## Slide 15: Results – Plasma wake structure
Ion density at the position of the probe
Studied time interval, 2010-03-03
Plasma flow
30
25
20
15
10
5
0
ni (cm-3)
d (m)
ni (cm-3)
ni (cm-3)
Vs/c
Plasma flow
Vs/c

## Slide 16: Results – Measured vs. simulated
Angle between probe and relative flow direction (red), measured ion density (blue), measurement uncertainty (light blue) and simulated ion density (black) for 2010-03-03.
Error of LP ni ~±10 cm-3

## Slide 17: Conclusion and future work
Simulated ion densities agrees well with ion densities measured with the Cassini/LP
  An excellent agreement can be obtained by varying Ti and v
  SPIS can be concluded to be very reliable for wake simulations in this plasma regime
Possible indication that Ti is lower than measured by CAPS
  i.e., in better agreement with LP Ti estimates
Additional simulations with smaller mesh size
Additional simulations that include the LP, but with larger mesh size
Additional simulation for larger radial distance, i.e. lower plasma density, to show why the wake is less important for statistical studies
Same kind of simulations are being set-up for JUICE, to prepare for future plasma measurements

## Slide 18: Mesh optimization
Cassini model without LP

## Slide 19: Potential and electron density
Cassini model without LP
Potential (not visibly affected by wake structure)
Electron density (not visibly affected by the wake structure)