## Slide 1: Charging of the PICASSO CubeSat
S. Ranvier1, A. Waets2, F. Cipriani2, J. De Keyser1 and J.P. Lebreton3
1 Royal Belgian Institute for Space Aeronomy (BIRA-IASB), Avenue Circulaire 3, 1180 Brussels, Belgium
2 ESA, TEC-EPS (Space Environment and Effects Section), Keplerlaan 1, Noordwijk 2200AG, The Netherlands
3 Laboratoire de Physique et Chimie de l’Environnement et de l’Espace (LPC2E), 3A, Avenue de la Recherche Scientifique, 45071 Orléans cedex 2, France
25th Spacecraft Plasma Interaction Network in Europe (SPINE) Workshop, 25-26 October 2018
ESTEC, Noordwijk, the Netherlands
Contact: sylvain.ranvier@aeronomie.be

## Slide 2: Outline
PICASSO mission
PICASSO platform
SLP: scientific objectives
SLP instrument
S/C charging due to the use of LP
S/C charging due to the plasma environment
Conclusions

## Slide 3: PICASSO mission
  ESA in-orbit demonstrator
  Quasi polar orbit, altitude: 500 - 600 km
  expected orbital lifetime: 1-2 years
  Launch in 2019
  2 scientific instruments:
  VISION: visible and near-infrared hyper-spectral imager
  Scientific objectives:
  Polar and mid-latitude stratospheric ozone vertical profile retrieval
  Upper atmosphere temperature profiling based on the Sun refractive flattening
  SLP: Sweeping Langmuir Probe

## Slide 4: PICASSO platform
Triple unit (34x10x10 cm, 1U for payload), four 2U deployable solar panels
Telecom: UHF/VHF + S-Band
Attitude control: magneto-torquers & dynamical wheels
Attitude: inertial flight, one face towards the Sun
Mass: 3.9 kg, power consumption: 8 W
Downlink: 40 MB/day, Uplink: 400 kB/day
Pointing accuracy: ~1° (knowledge: 0.2°)
  Star tracker & GPS

## Slide 5: SLP: scientific objectives
  In-situ study of:
  Ionosphere-plasmasphere coupling
  Subauroral ionosphere and corresponding magnetospheric features
  Aurora structures
  Turbulence (multi-scale behavior, spectral properties)
 | Minimum (> 95% probability) | Maximum (> 95% probability)
Plasma density (#/m³) | 108 (109) | 1013 (5x1012)
Electron temperature (K) | 600 (700) | 10 000 (5 000)
Expected plasma environment
Scientific objectives

## Slide 6: SLP instrument
Instrument overview
Four thin cylindrical probes whose electrical potentials are swept. From the electric current collected by each probe, the following parameters will be retrieved on ground:
  electron density and temperature
  ion density
  spacecraft potential
  Download raw data: I-V curves contain more information than only 3 parameters !
Key numbers:
  4 probes
  4 independent channels
  Probe diameter: 2 mm
  Probe length: 40 mm
  Boom length: 40 mm
  Sampling frequency: 10 KHz
  > 10 I-V curves/s => Ne, Te, Ni, VS/C
  Bias voltage: -5 V to 13 V wrt S/C GND

## Slide 7: SLP instrument
  Typical I-V mode:
  Apply bias, measure current
  On board plasma potential estimation => adaptive sweep
  Sweeps with different bias steps according to the region, e.g.:
  Ion saturation: 5 steps
  Electron retardation: 30 steps
  Electron saturation: 8 steps
  Fast Ne measurement:
  Acquire simultaneously with at least 2 probes the current when probes biased with different potential in the electron retardation region => retrieve Ne only
  5 KHz sampling rate => ~ 1,5 m resolution
  Floating potential:
  Measure the potential of the probes wrt the S/C GND

## Slide 8
Problem of using LP on board Pico-Satellite
Limited conducting area of the S/C with respect to the area of the probe
Spacecraft charging (e- saturation region)
  Drift of the instrument’s electrical ground during the measurement
  Unusable data
  Risk:
  Too low S/C potential: unable to sweep appropriate potentials (e- saturation region)
S/C charging due to the use of LP

## Slide 9
Particle-in-cell (PIC) modelling and simulations with SPIS
S/C charging due to the use of LP

## Slide 10
Example of sweeps in eclipse
Bias: from -5 V to + 13 V
S/C charging due to the use of LP
Ne = Ni = 1e8/m³ ; Te = Ti = 0,2 eV
Ne = Ni = 1e10/m³ ; Te = Ti = 0,2 eV

## Slide 11: S/C charging due to the use of LP
Proposed solution
Increase conducting surface of the S/C (at least 200 cm² on all sides of the S/C, incl. solar panels)
Measure the floating potential of one probe while measuring the I-V curve with another probe
=> The 2 probes that are in the same environment (light/shadow, wake)
Advantages
Robust: no filament
No risk of electron collection from e-gun
Disadvantage
Limited range in e- saturation region in very high density plasma

## Slide 12: S/C charging due to the use of LP
Test at ESTEC in July 2015 and February 2017
Functional test in plasma chamber (ESTEC Feb. 2017)
Red: I as function of bias (wrt to S/C GND)
Blue: I as function of bias (wrt to plasma pot.)
Floating pot. of one probe (wrt to S/C GND) as function of applied bias on other probe

## Slide 13: S/C charging due to the use of LP
Eclipse:
Max bias (wrt plasma): ~6 V
S/C charging effect: from ~3 V
Sunlight:
Max bias (wrt plasma): ~10 V
S/C charging effect: from ~8 V
Effect of photoemission
IV curves from LP sweeps in eclipse and sunlight.
Ne = Ni = 1e10/m³ ; Te = Ti = 0,2 eV
Bias: from -5 V to + 13 V

## Slide 14: S/C charging due to the use of LP
Maximum probe potential with respect to plasma potential
SPIS simulations for extreme cases
Most unfavorable case:
High Ne
Low Te
Eclipse (no photoelectron)
Floating potential:
-0.16 V for Te = 600 K
-1.9 V for Te = 6000 K
=> Always possible to reach electron saturation region
Probe potential for extreme cases (eclipse)

## Slide 15: S/C charging due to the plasma environment
Auroral environment: Maxwellian fit of the ECSS worst case distribution with Ne = 1.23E7/m³ and Te = 11keV
Background ion and e- populations: Ne = Ni = 1e8/m³, Te = Ti = 0.2 eV
After 10 seconds:
800V differential charging between epoxy and cover glass
550V differential charging between epoxy and gold (S/C GND)

## Slide 16: S/C charging due to the plasma environment
Background ion and e- populations: Ne = Ni = 1E9/m³, Te = Ti = 0.2 eV
After 10 seconds: 550V differential charging between cover glass and epoxy
Background ion and e- populations: Ne = Ni = 1E10/m³, Te = Ti = 0.2 eV
After 10 seconds: 165V differential charging between cover glass and epoxy

## Slide 17: Conclusions
  SLP (Sweeping Langmuir Probe) instrument to fly on board PICASSO in 2019
  Uses adaptive sweep => download raw data
  Can acquire > 10 I-V curves/s => Ne, Te, Ni, VS/C on ground
Problem of using LP on board pico-satellite:
Limited conducting area of the S/C with respect to the area of the probe
Spacecraft charging (e- saturation region)
  Drift of the instrument’s electrical ground during the measurement
  Unusable data
Proposed solution
Maximize conducting surface of the S/C
Measure the floating potential of one probe while measuring the I-V curve with another probe
Allows sweeping bias in e- saturation region even in the worst conditions of the PICASSO mission
Differential charging up to several 100 V might occur in auroral regions depending on background plasma density

## Slide 18
Thank you for your attention!