## Slide 1
G. L. Civardi, A. Brandonisio, M. Piccinin, M. Lavagna
ESA’s Clean Space Industry Days
20-24 September 2021
Multispectral imaging to support close proximity navigation and target mapping

## Slide 2: Outline
Context & motivation
Multispectral imaging
  TIR image rendering
  Navigation architecture
Testing campaign definition
Results
Conclusions & future work

## Slide 3: Context & Motivation
.
Objective
To investigate the feasibility of a multispectral imaging approach for optical navigation and mapping for uncooperative target inspection.
Multispectral Imaging: distinguished spectral bands  exploit their difference to increase robustness and flexibility of the navigation solution
The ESA e.Inspector mission:
12U Cubesat for debris imaging in preparation to active removal of VESPA.
On-board cameras operate in the VIS and TIR spectral bands
Responsible for the Phase A design.
Expected results:
Overcome challenging lightning conditions and relax operational constraints.
Enhance navigation robustness through data fusion.

## Slide 4: TIR image rendering
Parameter | VIS | TIR
Sensor size | 1024x1024 | 512x512
Field of View | 9.15°x9.15° | 9.15°x9.15°
Spectral band | 380 – 750 nm | 8 – 12 μm
Detectable temperature | - | 150 – 460 K
Environment model
Debris thermal model
Spacecraft trajectory
Image rendering
Traditional rendering with Blender
TIR camera model
Brightness enhancement + NETD

## Slide 5: Optical navigation architecture
Simultaneous Localization And Mapping (SLAM).
Same SLAM architecture adopted for processing in parallel VIS and TIR images.
No prior knowledge on the target is required.
ORB
features
Lucas-Kanade tracking
5-Point
Algorithm
Triangulation
Map
EPnP & MSAC
Motion
BA
Refined pose
Initialization only
Pose
Frames

## Slide 6: Testing campaign definition
Vespa: simple shape, smooth surfaces.
Envisat: Complex shape, rich in details.
Circular inspection orbit.
Two different illumination cases will be considered.
Targets selection:
Test case scenarios:

## Slide 7: Results: image rendering
Brightness of the visible image is enhanced according to the temperature profile.
Gaussian noise is added through Noise Equivalent Temperature Difference (NETD).
TIR
VIS

## Slide 8: Results: image processing
Surface smoothness negatively affects feature detection and feature tracking.
The resulting map is expected to be incomplete.

## Slide 9: Results: optical navigation
 | VIS |  | TIR | 
Case | [%] | [deg] | [%] | [deg]
VESPA - Low φ | 0.67 | 0.67 | 1.51 | 1.52
VESPA - Mid φ | 1.82 | 1.92 | 1.84 | 2.05
ENVISAT - Low φ | 0.49 | 0.52 | 0.58 | 0.67
ENVISAT - Mid φ | 0.97 | 1.05 | 1.23 | 1.15
 | VIS |  | TIR | 
Case |  |  |  | 
VESPA - Low φ | 0.67 | 0.67 | 1.51 | 1.52
VESPA - Mid φ | 1.82 | 1.92 | 1.84 | 2.05
ENVISAT - Low φ | 0.49 | 0.52 | 0.58 | 0.67
ENVISAT - Mid φ | 0.97 | 1.05 | 1.23 | 1.15
TIR exploitation is feasible.
VIS is more accurate than TIR for low φ.
For mid φ VIS and TIR results are comparable.
Results depend on the target’s geometrical features.
SLAM results in the low-phase angle case -Envisat

## Slide 10: Results: target mapping
Overall shape is well reconstructed. Size ratios are respected.
Smooth surfaces are not reconstructed due to lack of keypoints.
VIS/TIR mapping results are comparable.
Envisat 3D sparse map.
Vespa 3D sparse map.

## Slide 11: Natural target: asteroid Ryugu
Potentially Hazardous Asteroids characterization.
The on-board thermal imager is employed for GNC purposes.
Excellent generalizable properties of SLAM algorithm.
SLAM results.
Synthetic TIR images of asteroid Ryugu

## Slide 12: Conclusions & future works
Conclusions
SLAM algorithm numerically tested on VIS/TIR images for relevant application cases.
TIR-based navigation is feasible.
Flexibility of the navigation strategy is assessed with different targets.
Multispectral data fusion can be introduced to overcome the disadvantages of the distinguished spectral bands
Future work
Enhancement of TIR sensor model.
VIS-TIR images fusion algorithms exploitation.

## Slide 13
G. L. Civardi, A. Brandonisio, M. Piccinin, M. Lavagna
ESA’s Clean Space Industry Days
20-24 September 2021
Multispectral imaging to support close proximity navigation and target mapping