## Slide 1: Microthrusters and droplet dynamic modeling in SPIS : SPIS-µThrusters
17th SPINE
M. Villemant1, P. Sarrailh1, S. Hess1
1 ONERA, The French Aerospace Lab, 31055 Toulouse Cedex, France
19-20/02/2020

## Slide 2: Presentation plan
Presentation of SPIS-µThrusters problematic
SPIS-µThrusters new abilities presentation
Preliminary simulation of micro-thruster in LISA space environment
SPIS-µThrusters validation cases
Conclusion and further studies

## Slide 3
FEEP and colloids thruster technologies
3
Very high specific impulse
Specific impulse | 1600-8000 s
Thrust | 0.1-100 µN
Total thruster mass | 2.5 Kg
Total power supply | 13 W
Table 1 : In-FEEP thruster characteristics [1]
High compactness
Low mass
Low thrust
Droplets emission
Figure 1 : Example of FEEP thruster (NanoFEEP, NASA)
Figure 2 : Example of colloid thruster (NASA)
Interest of space agencies and private companies for FEEP and colloids technologies

## Slide 4
One of the main problems of FEEP and colloids : droplets emission
4
Satellite surface contamination by droplets
FEEP  use of liquid metal  satellite surface metallization (solar panels, optics, etc.)
Colloids  Complex organic molecules  Chimical reaction at satellite surface
Droplet behaviour around satellites body is a topic interest for space agencies and industrials
Need for simulation of droplet satellite body interaction
 SPIS software
Figure 4 : SPIS software interface
Figure 3 : Example of droplet emitted from a FEEP thruster

## Slide 5
Droplets evolution and interactions with spacecraft body and environment
5
Droplets
Evaporation
Ionization
Neutrals
Charge exchange ions
Surface charging
Surface erosion
Surface contamination
Droplets charging
Droplets splitting
Surface contamination
Surface contamination
Complex interaction between droplet populations, spacecraft body and environment
Interaction with the environment
Need to take these phenomena into account in satellites simulations

## Slide 6
Miscellaneous models implemented in SPIS-µThrusters
Micro-Thrusters emission models
Droplets thermal model
Droplets interactions with spacecraft surfaces
Mass fraction of the emitted species
Energy and angular distribution of the emitted species
Droplets mass, charge and radius distributions
Droplets temperature changes
Droplets evaporation
Droplets solidification
Outgassing
Droplets collection
Droplets erosion
Droplets rebounds
Droplets evaporation on surfaces
Spacecraft surfaces temperature taken into account

## Slide 7
SPIS-µThrusters software new abilities

## Slide 8
Setting of electrospray and FEEP thrusters
8

## Slide 9
Setting of micro-thrusters propellants
9
Definition of emitting surfaces materials properties:
For FEEP thruster:
Caesium
Indium
For colloids thruster:
EMI-BF4
EMI-TfN2

## Slide 10
Experimental data on propellant material
10
Parameter | EMI-BF4 | EMI-Tf2N | Indium | Caesium
SFTN: superficial tension [J/m²] | 0.0452 | 0.0349 | 0.56 | 0.06
dustRadiusDF: distribution of droplets [m] | - | - | - | -
SUBE: sublimation energy [MJ/kg] | 0.8 | 0.41 | 2.04 | 0. 53
VAPE: vaporization energy [MJ/kg] | 0.75 | 0.35 | 2.01 | 0. 51
FUSE: fusion energy [kJ/kg] | 48 | 58 | 28 | 16
MELT: fusion temperature [K] | 285.75 | 277.75 | 429.75 | 301.6
WORK: Work function [eV] | - | - | 4.12 | 1.95
THCO: thermal conductivity [W/M/K] | 0.2 | 0.130 | 81.6 | 35.9
HEAT: specific heat [J/kg/K] | 1281 | 1290 | 264 | 240
PREF: pressure reference [Pa] | 0.013 | 0.0062 | 1 | 1
TREF: temperature reference [K] | 300 | 441.7 | 1196 | 418
SOLA: sun light absorbance [-] | 0.1±0.05 | 0.1±0.05 | 0.1±0.05 | 0.1±0.05
RDC: relative dielectric permitivity | 12.9 | 12.2 | 1 | 1
BUC: electric bulk conductivity [S/m] | 1.4 | 0.88 | 11.6.106 | 4.89.106
MAD: material density [kg/m3] | 1294 | 1520 | 7310 | 1879
TEMI: thermal emissivity | 0.5? | 0.5? | 0.03 | 0.03
PEY: photo emission yield [A/m2/F0] | missing | missing | missing | missing
SRE: surface resistivity[W] | 1,4.109 | 1,8.109 | -1 (∞) | -1 (∞)

## Slide 11
Thruster information displayed

## Slide 12
Data output specific to droplets simulations
12
Droplets cloud of points:
Droplet flux on spacecraft surfaces
Droplet outgassing
Spacecraft surfaces temperature

## Slide 13
Example of contamination modelling on a spacecraft by FEEP and colloids thrusters

## Slide 14
Simulation initialization
14
Figure 5: Contamination test case simulation geometry
Environment plasma representative of LISA mission
1 AU from the sun
Solar wind electrons and protons:
  Density :
  Temperature :
Figure 6: Artist concept of LISA pathfinder satellite
Emitted droplets and plasma characteristics extracted from experimental data
Figure 7: Measured distribution of emitted droplet by the InFEEP thruster as a function of droplet radius

## Slide 15
Figure 8 : densities of cathode electrons (right), thruster ions (center) and droplets (right) in log(m-3).
FEEP simulation : Results analysis
In+
Electrons
Droplets
Ability of SPIS software to simulate droplets dynamic
Non negligible divergence of droplet flow from the thruster
  Spacecraft body contamination by FEEP droplets could be a real threat

## Slide 16
FEEP simulation : Erosion simulation due to In+ ions impact
Figure 10: In+ ion flux on the plate surface [log of ion.m-2.s-1]
Figure 11: eroded product flux, in log of molecule.m-2.s-1
SPIS ability to model spacecraft surface erosion and eroded product emission from spacecraft surface
Non-negligible erosion of spacecraft surface by FEEP thruster

## Slide 17
FEEP simulation : Spacecraft body contamination by droplets
Figure 12 : flux of droplet deposited on the plate [log of droplet.m-2.s-1]
Non-negligible contamination of spacecraft body by droplets

## Slide 18
Colloids simulation : emitted species densities
Figure 13 : From top to bottom : densities of (EMI-BF4)+, (EMI-BF4)2+, (EMI-BF4)3+, EMI-BF4 droplets and cathode electrons
Figure 13 : Densities of (EMI-BF4)+, (EMI-BF4)2+, (EMI-BF4)3+, EMI-BF4 droplets and cathode electrons
EMI-[BF4]+
EMI-[BF4]2+
EMI-[BF4]3+
Droplets
Electrons
SPIS ability to model the different species emitted by a colloid thruster
Similar densities in the volume for monomers, dimers and trimers

## Slide 19
Colloids simulation : droplets deposition on spacecraft body
Figure 13 : From top to bottom : densities of (EMI-BF4)+, (EMI-BF4)2+, (EMI-BF4)3+, EMI-BF4 droplets and cathode electrons
Figure 14 : flux of droplet deposited on the plate [log of droplet.m-2.s-1]
Non-negligible contamination of spacecraft body by droplets
Comparable contamination to Indium in FEEP thrusters

## Slide 20
SPIS-µThrusters validation cases

## Slide 21: LMIS FEEP thruster modelling
FEEP current measurement and comparison to FEEP model
Angular distribution of emitted current
Comparison between SPIS simulation and experimental data from ESA

## Slide 22: Geometry data on LMIS and justification on non-available data
Symbol | Definition | Value (mm)
 | Radius of FEEP case | 7,5
 | Length of FEEP case | 10
 | Radius of FEEP aperture | 5
 | Thickness of FEEP aperture | 1,5
 | Plates width | 1
 | Plates length | 5
 | Plates thickness | 0.3
 | Number of plates | 12
 | Distance between FEEP and plates | 40
 | Angle between plates | 15°
 | Radius of the vaccuum chamber | 50
 | Height of the vacuum chamber | 200
 | Gap between vacuum chamber and thruster | 30
Symbol | Definition | Value (mm)
 | Radius of FEEP case | 7,5
 | Length of FEEP case | 10
 | Radius of FEEP aperture | 5
 | Thickness of FEEP aperture | 1,5
 | Plates width | 1
 | Plates length | 5
 | Plates thickness | 0.3
 | Number of plates | 12
 | Distance between FEEP and plates | 40
 | Angle between plates | 15°
 | Radius of the vaccuum chamber | 50
 | Height of the vacuum chamber | 200
 | Gap between vacuum chamber and thruster | 30
: Data extracted from literature
: Data deduced from literature
: Data chosen arbitrary

## Slide 23: LMIS other data
All the nodes grounded
Thruster selected : Thruster : In-LMIS
Thruster Material : Indium Material Properties
No cathode
Simulations boundaries grounded and considered as perfectly absorbing for incident particles.
Chosen emission current :
  100 µA 
  250 µA 

## Slide 24: Results on LMIS ESA experiment

## Slide 25: Results on LMIS ESA experiment comparison with simulations: droplet massflow to the surface
Scale factor equal to : to compare with a ratio of
Good representativeness of droplet contamination modelling by SPIS-µThrusters

## Slide 26: Colloid ST7 thruster modelling
Comparison between SPIS simulation and experimental data from JPL
Colloid current measurement and comparison to Colloid model
Angular distribution of emitted current

## Slide 27: Geometry data on ST7 and justification on non-available data
Symbol | Definition | Value
 | Diameter of the electrospray vacuum chamber | 5 cm
 | Length of the electrospray vacuum chamber | 6 cm
 | Length of the main vacuum chamber | 130 cm
 | Diameter of the main vacuum chamber | 100 cm
 | Diameter of the electrospray aperture | 0.8 cm
 | Collector side length | 10 cm
 | Diameter of the electrospray | 1 cm
 | Length of the electrospray | 5 cm
 | Gap between the electrospray and the back of the vacuum chamber | 1 cm
 | Distance between the colector and the electrospray | 5 cm
Symbol | Definition | Value
 | Diameter of the electrospray vacuum chamber | 5 cm
 | Length of the electrospray vacuum chamber | 6 cm
 | Length of the main vacuum chamber | 130 cm
 | Diameter of the main vacuum chamber | 100 cm
 | Diameter of the electrospray aperture | 0.8 cm
 | Collector side length | 10 cm
 | Diameter of the electrospray | 1 cm
 | Length of the electrospray | 5 cm
 | Gap between the electrospray and the back of the vacuum chamber | 1 cm
 | Distance between the colector and the electrospray | 5 cm
: Data extracted from literature
: Data deduced from literature
: Data chosen arbitrary

## Slide 28: Geometry data on ST7 and justification on non-available data

## Slide 29: Conclusion and further studies
Preliminary simulations highlight the need to have realistic modelling of droplet emission and dynamic around spacecraft
SPIS-µThrusters is operational (end of code development)
The set of experimental data seems sufficient to carry out a relevant validation of SPIS-LISA
SPIS-µThrusters seems to simulate realistic order of magnitude for droplets angular dispersion
Get more relevant data on Electrospray thrusters
Compare results to in-flight data of satellites using micro-thrusters (LISA-Pathfinder, etc.)
One SNAPSHOT version of SPIS-µThrusters (with num core 6.0.4) will be released before the end of 2020  Feedbacks from the community will be much appreciated to improve this new version
Looking for new inflight data extracted from last European development in micro- and nano-satellites and micro-thrusters (e.g. Impulsion)

## Slide 30
Appendix

## Slide 31
[1] ‘Electrospray Thrusters Boost Efficiency, Precision’. [Online]. Available: https://spinoff.nasa.gov/Spinoff2016/ip_9.html. [Accessed: 17-Sep-2019].
[2] M. Fehringer, F. Rüdenauer and W. Steiger, “Ultra-Precise Indium Thruster - WP 2000: Droplet Emission,” Nordwijk, 2001
[3] ‘News | A Final Farewell to LISA Pathfinder’. [Online]. Available: https://www.jpl.nasa.gov/news/news.php?feature=6901. [Accessed: 17-Sep-2019].
References

## Slide 32
Droplet emission
Droplet display in simulation
Droplet temperature evolution
Droplet rebound

## Slide 33: Results on ST7 from JPL experiment

## Slide 34
Simulation of droplets rebounds on surfaces
34
Display of droplets cloud of points:

## Slide 35
Micro-Thrusters models

## Slide 36
Electrospray emission model
36
Beam current :
Droplet diameter :
Charge-mass ratio :
: Emitted massflow []
: Droplet charge [C]
: Droplet mass [kg]
: Droplet mass density
: Droplet electrical conductivity []
: Droplet surface tension [N/m²]
: Droplet relative electrical conductivity []

## Slide 37
FEEP emission model
37