## Slide 1
Internship presentation
MMOD modelling in an industrial context:
The use and application of MASTER
B. Zitouni, S. Gonzalez Garcia, R. Kast

## Slide 2: Overview:
Overview
MMOD Assessment process by OHB:
  Project needs
  General MMOD Analysis process
  Detailed MMOD Analysis methodology
MMOD Modelling
  Master use and comparison M2009 vs M8 outcome
  Connection to Systema (stenvi files)
Conclusion: open discussion
  MM models change? Why? [Results are weirder in new MASTER]
  New Stenvi file format?

## Slide 3: Project needs:
Modelling & Analysis Group
OHB variety of missions: LEO, MEO, GEO, Exploration. Needs to study several MMOD environment and not only one type
    LEO: 2 Observation satellites + CO2M
    MEO: Galileo first generation satellites
    GEO: Telecommunication satellites (H2SAT, Electra –orbit raising-) + Scientific (MTG)
    Exploration: Plato, HERA
LEO
GEO
Exploration
Lagrange L3 =>
  Project have specific needs for units or the whole satellite, to assess the PNF

## Slide 4: MMOD Analysis process:
Modelling & Analysis Group
Goal: check if the design is correct with regard of the studied subject
These types of environment analysis interact with several disciplines:
  Design
  Thermal
  Materials
  Mission definition (orbit + Environment)
Design: geometry STEP file
Thermal: simplified list
Materials: list with appropriate properties for the study
Mission definition:
  Orbit:
    altitude and latitude
    Local time and season
  Environment:
    MM models
    Manmade debris
    STENVI Files
Interactions in two directions:
  Defining the analysis
  Flowing the outputs to the impacted subsystems
  Loop if analysis show a design flow
Inputs
Implementation into model
Meshing
Mission and Environment definition
Numerical assessment
  Ray-tracing
  Surfaces orientation
Sufficient iterations for confidence in results
Analysis
Results
Results adapted to project needs
Comparison with requirements
Check if analysis too conservative
Identification of possible problems
New loops if necessary
PPT for intermediate results

## Slide 5: MMOD Analysis Methodology
Depending on the project state: PDR or CDR, we go more in details if needed
Simplified process at early satellites stages: « MASTER + EXCEL »
    Define Environnement with MASTER
    Load MASTER ouput file in our own Excel tool
    Make a first assessement for surfaces, for different BLEs, at different angles
    Provide a first PNP
  Detailed assessment at advanced stages: “MASTER + SYSTEMA”
    Defining the the meteoroids and orbital debris (M/OD) flux model from MASTER
    Simplifying the spacecraft geometry within Systema
    Computation of equipment vulnerability
      Identifying structures and elements within the model
      Defining the material parameters
      Choosing the correct equations
    Evaluating the Probability of No Penetration (PNP)
MMOD modelling in an industrial context (OHB)

## Slide 6: MMOD modelling: MASTER use and comparison
Target orbit
Performed for:
    MASTER 2009
    MASTER 8
      Grün model – Grün distribution
      Grün model – Taylor distribution
      Divine-Staubach model (Grün distribution)
      Divine-Staubach model (Taylor distribution)
MMOD modelling in an industrial context (OHB)
Comparison between M2009 and M8

## Slide 7
MMOD modelling in an industrial context (OHB)
Master 2009 | Master 8 Grün – Grün | Master 8 Divine-Staubach (Grün option)
First Comparison Analysis

## Slide 8
MMOD modelling in an industrial context (OHB)

## Slide 9
Master 8 Grün – Grün | Master 8 Grün – Taylor
MMOD modelling in an industrial context (OHB)
Suggestions of change from ESOC

## Slide 10
MMOD modelling in an industrial context (OHB)

## Slide 11
Master 2009 | Master 8 Grün – Taylor | Master 8 Divine-Staubach (Taylor option)
MMOD modelling in an industrial context (OHB)
Second Comparison Analysis

## Slide 12
MMOD modelling in an industrial context (OHB)

## Slide 13: Impact risk assessment
MMOD modelling in an industrial context (OHB)
Risk of failure assessed by using:
Spacecraft information (geometry, trajectory…)
Ballistic limit equations (stablishing the failure criteria)
Directional collision fluxes derived from MMOD models
Measure of risk : Poisson statistics relations
()
Link with MASTER?

## Slide 14: Link with MASTER: Stenvi files
MMOD modelling in an industrial context (OHB)
First difficulty: how to define the BIN?
#--------------------< Definition of the output spectrum >----------------------
# Bin Min Max
AZIMUTH 18 -180.0 180.0 Azimuth [deg]
ELEVATION 18 -90.0 90.0 Elevation [deg]
VELOCITY 2 0.5 20.5 Velocity [km/s]
DIAMETER 40 0.1E-04 0.1E+02 Diameter [m]
LATITUDE 1 0.0 360.0 Argument of True Latitude [deg]
DENSITY 200 0.0 5.0 Density [g/cm^3]
How the link with the “different years scenarios” is performed?
Stenvi only provides Lower border and Uppers Borders, averaged in time
Some information are lost afterwards in the simulation (exact distribution according to the particles sizes)

## Slide 15: Conclusion: open discussions
MMOD modelling in an industrial context (OHB)
Micrometeoroids and Debris assessment
The use of MASTER 2009 is recommended until the MASTER 8 Divine-Staubach model patch is released and a more exhaustive investigation on the Grün model has been performed
    An exchange with ESA/ESOC about the MASTER new version investigation was performed
    The use of Grün model with Taylor distribution is recommended
  Why change of the MM models? Not stable in new MASTER
  Use of new orbits such as Lagrange Points, exploration… How reliable is the tool? Limitations?
Link with Systema: STENVI files, open for discussions
Some questions remains open: different years scenarios, averaged values, information lost later