## Slide 1: NIRCA MkII IR Image Sensor Readout and Controller ASIC
AMICSA 2022, Madrid, Spain
Custom cell-, circuit- and system- design of ICs for space applications
Torbjørn Østmoe, torbjorn.ostmoe@ideas.no
Integrated Detector Electronics AS (IDEAS), Oslo, Norway
Copernicus Sentinel-2A, Courtesy of Airbus
NIRCA MkII

## Slide 2
NIRCA MkII provides A/D conversion and control for IR sensors using a single IC

## Slide 3: IR system using NIRCA MkII
Flex cable
  HgCdTe/InGaAs
  Microbolometer array
Sensor: FPA + ROIC
NIRCA MkII
Master Controller (FPGA)
Sensor examples

## Slide 4: NIRCA MkII Applications
Earth observation
Astrophysics
Terrestrial

## Slide 5: Benefits of NIRCA MkII
Reduce SWaP
  NIRCA MkII bare die area: 1 cm2
  Power consumption < 2 W
  This reduces costs
Withstands harsh environments
  Radiation hardness (SEE/TID)
  Operating temperature -40oC to +85oC
1 cm
1 cm

## Slide 6: Example: NIRCA MkII in system
Ethernet / CameraLink
IDEAS RX IP
FPGA
Pixel array
Analog out
Sensor
SPI / Serial
Store images
SPI
Control (RST, INT,…)
Status (FV, LV, ERR)
Sensor clock
Supply/References
AIN
NIRCA MkII ASIC
DIN
DOUT
AOUT
Adjustable frequency/delay/duty
Direct connection
7 pF input capacitance
Fully-/pseudo-differential
Adjustable sample point
Wide common-mode range
Flexible waveforms
Debug (internal sig)
Std. SPI modes
Shift register
Read status/serial
React to status
Low noise
Programmable voltage
Proximity sensor
SPI
PIRQ
IRQ
TX
Control
ASIC configuration
ASIC control
ASIC state/status read
Sequencer programming
Signal about ASIC/sensor states
React to interrupts
AC or DC coupling
Source synchronous
With/without TX clock
Multiple frame types
Many data sources (ADC, DIN, REGs)
Stream capability
CRC
IDEAS provides RX IP (VHDL)
Clock
Clock
≤ 15 MHz from FPGA or other source

## Slide 7: NIRCA MkII Block Diagram and Features
17 ADCs digitizing sensor data at 12 Msps
8 adjustable voltage references (0 – 3 V)
I/O interface for sensor control, monitoring and sample time adjustment
Programmable sequencer
Instruction RAM with single error correction, double error detection (SECDED)
ACQ capable of a wide variety of acquisition modes
9 LVDS links TX<0:8> with 8b/10b encoding exporting data to the FPGA at 480 Mbps/link double rate
SPI interface for communication
Radiation hardened against SEE and TID
16
16

## Slide 8: Analog front-end
Preamp + pipeline ADC architecture
Supports fully- and pseudo differential mode
16 Video ADCs + 1 Auxiliary ADC
  16-bit ADCs with 12 Msps
  14-bit if frame/line valid are sent upstream
Programmable offset and gain
  Gain: x1, x1.14, x1.33, x1.6, x2, x2.67, x4, and x8
  Range: V V
Automatic calibration of capacitor mismatch
Parameter | Measured
Equivalent input noise (ENI) | 3.0 LSBrms
Differential non-linearity (DNL) | (-0.32, +0.35) LSB
Integral non-linearity (INL) | (-2.4, +1.5) LSB
Typical values with gain x1 and 16-bit ADC mode.
16
16

## Slide 9: Sequencer
Automating the control sequences
Microcontroller-like instruction set
21 instructions:
  Control: CALL, JUMP, LOOP, …
  Data management: LOAD, LDTEMP, MOVTEMP, …
  Data flow: TXVAL, TXBR, …
  State management: WAIT (COMPARE / IRQ)
  Can be used in combination with flags as SYNC and ACQUIRE
Handling of IRQ inputs and outputs

## Slide 10: Using the NIRCA MkII sequencer
Simple NIRCA program generating a waveform using functions, instructions and the ACQUIRE-flag
@start:
NOOP 0
LOAD DOR 0b00000001
LOAD NLC 5 # Call next function 5+1 times
CALL @f_func1
LOAD DOR 0b00000000
WAIT 2 # Stops: wait for unused condition
LOOP @start
@f_func1:
A LOAD DOR 0b00000011
LOAD DOR 0b00000111
LOOPR @f_func1 # LC = LC - 1
NM2 assembly program
ACQ triggered by sequencer (A-flag in @f_func1) VADC_0 enabled sample sent on TX
Configuration

## Slide 11: Example use case: Sensor with Frame and Data valid
WAIT for line-valid
Line valid low
1. Reset & integration phase
2. Frame and data/line-valid sequence
Sends frame/
line valid=1 to DIN
Line valid high
Resets sensor
Integration time
Start of frame
Sensor
Data sent on TX
End of frame
NIRCA MkII
Software

## Slide 12: Radiation testing
SEL tolerance up to LET = 71.1 MeVcm2/mg
No SEU in configuration registers below LET < 16.1 MeVcm2/mg, few SEUs above
SECDED implementation of the RAM works
27 krad (low dose rate) + 85 krad (high dose rate)
No TID induced drift on DNL, INL, noise, offset/gain errors and max frequency
Drift in voltage references/ODACs about -0.5 %
SEE
TID

## Slide 13: NIRCA – Roadmap
NIRCA MkII is validated, radiation tested and packaged
  Samples are available
Funding for further development is secured from ESA
NIRCA MkII Further development
2015 2017 2020 2023
NIRCA MkII
NIRCA MkII Design iteration & Qualification
NIRCA 1
NIRCA 1.1

## Slide 14: NIRCA – Next steps
Make qualification platform Q4 2022
NIRCA MkII design iteration available Q2 2023
Space qualified packaging Q2 2023
Procure engineering models Q2 2023
  Available for customers too
Radiation testing for qualification Q3 2023
Space qualification Q1 2024
  Flight models will be available
Collaborate with users!

## Slide 15: Contact
Project Manager - Amir Hasanbegovic: amir.hasanbegovic@ideas.no
Presenter - Torbjørn Østmoe: torbjorn.ostmoe@ideas.no
Special Apps/Ops/Env
Radiation Detectors
Image Sensors
IC Designer/Supplier