## Slide 1: Radiation Hardened Versatile 14-bit SAR adc
Laurent Berti

## Slide 2: Outline
  Original ADC
  Analog mux 8:2
  Comparator improvement (offset, speed and input equivalent noise)
  ADC core improvement
  Conclusion

## Slide 3: Original ADC
10-bit SAR ADC single ended
  Silicon proven
  Single capacitor bank, no split capacitor architecture
    1024 unit-capacitors of 25 fF (min. value comes from the PCell of the PDK)
    Low enough sampling noise (kT/C) for 16-bit resolution
    DAC matching equivalent to a 14-bit DNL
Goal
  Transform the original ADC into a 14-bit versatile ADC without losing the benefit of the silicon proven
Implementation strategy
  The root architecture and design must be kept

## Slide 4: Outline
  Original ADC
  Analog mux 8:2
  Comparator improvement (offset, speed and input equivalent noise)
  ADC core improvement
  Conclusion

## Slide 5: Analog mux 8:2
Analog MUX 8:2 added in front of ADC
  Useful for low frequency sensor application: 1 ADC to monitor till up to 8 sensors in single ended mode or 4 in differential mode
  Possibility to isolate the input from the sampling capacitor (25pF)
    Zin > 24 kOhms
  Possibility to amplify the signal up to 12dB

## Slide 6: Analog mux 8:2
Bypass possible
Switches 1, 3, 4 and 6: no DC current
Switches 2 and 5: DC current but not in ADC signal path
  Sizing of the switches driven only by settling time consideration and SA (i.e. min. size)
  No gain error
  No distortion
No secondary ESD protection needed for the amplifying path => no gain error due to ESD resistor

## Slide 7: Outline
  Original ADC
  Analog mux 8:2
  Comparator improvement (offset, speed and input equivalent noise)
  ADC core improvement
  Conclusion

## Slide 8: Comparator improvement
Architecture maintained, only resizing
Auto-zeroing
  During tracking phase
  Use switched Miller compensation
  Min. retention offset correction: 30 µs
  Max. settling time 14-bit: 600ns
  PM > 60º
Max delay FS to 1 LSB for 14-bit: 100ns
Max input-referred noise at 125ºC: 35µVrms
SET filter
Auto zeroing cap

## Slide 9: Outline
  Original ADC
  Analog mux 8:2
  Comparator improvement (offset, speed and input equivalent noise)
  ADC core improvement
  Conclusion

## Slide 10: ADC core improvement
Added 4 items
  Internal voltage reference (Bypass possible)
  Second DAC for the differential mode
  1-bit to the FSM
  Extra DAC in parallel with the original DAC to extend the resolution
Original ADC

## Slide 11: ADC core improvement
Goal of the extra DAC: increase the resolution from 11-bit to 14-bit
  The DAC uses the charge sharing principle between the different capacitor
    Sampling: QC_S = (VIN-AGND) * 2048 * C where C is the unit capacitor of the DAC
    End of conversion: QC_E = QC_S => VIN_comp = [(AGND-VIN) * 2048 * C + 1024 * C * VREFP/N + 512 * C * VREFP/N ....]/(2048*C) QC_LSB = (VREFP – VREFN) * C
C
C
2C
4C
1024C
512C
256C
VIN
Comparator
AGND = (VREFP-VREFN)/2
AGND

## Slide 12: ADC core improvement
Adding 3 bits resolution means dividing the LSB charge (QC_LSB) by 8
  Add a capacitor of C/2, C/4 and C/8.... not possible
    The unit cap C is already at minimum value (MiM cap of 12.5 fF)
    Use of MoM cap is not suitable for matching (MoM can’t match with MiM)
    Arranging unit capacitor in series is not suitable due to floating node or leaky path
  Add a unit capacitor and divide the reference in 8 intervals of (VREFP-VREFN)/8
    It means QC_LSB become C * (VrefP-VrefN)/8
    Easy to implement thanks to a resistive divider. High resistor value is possible because the sampling frequency is low and the capacitor is small (1 unit cap)

## Slide 13: ADC core improvement
Add 2 capacitors of 2 C and of 4 C in the extra DACs
  Added for dithering purpose
    Input signal is sampled on the bottom plate of all the capacitors connected to the mid-range reference
    A first conversion where the 2 extra capacitors stay connected to the mid-reference
    Input signal is sampled on the bottom plate of all the capacitors connected to the mid-range reference
    A second conversion (with the same sampled value) where the 2 extra capacitors are connected to VREFP. Equivalent to add an offset of 6*(VREFP-VREFN)/2048
    A third conversion (on the same sampled value) where the 2 extra capacitors are connected to VREFN. Equivalent to substract an offset of 6*(VREFP-VREFN)/2048
    Use the averaged value of the 3 conversions for the output code....

## Slide 14: ADC core improvement

## Slide 15: Outline
  Original ADC
  Analog mux 8:2
  Comparator improvement (offset, speed and input equivalent noise)
  ADC core improvement
  Conclusion

## Slide 16: Conclusion
Starting from silicon proven 10-bit ADC:
  Add 3 optional bit
  Add analog MUX
  Add internal reference
  All these improvements can be bypassed