## Slide 1: Space Qualified European Ethernet PHY 100Mb/1Gb
Aerospace & Defense
June 2022
AMICSA
Solution Provider for Deterministic Networks and Modular Avionics
Notes: My thoughts are to tell a story…
  Climate change concerns driving electrification
  Electrification driving investment by traditional players and VC/ Startups
  Our CEM’s don’t have bandwidth to get to the new startups - need your help
  We have anchor products ideally positioned to help customer pivot to support this megatrend
  Example products – block diagrams
  Call to action
Mike Sorrentino set up the Sockeye meeting with CACI in the metro area and our CEM in Eastern Canada is setting up a meeting for me with Barry Devine to work out a coverage plan for A&D he does not have the bandwidth for.
Things are already different…

## Slide 2: Microchip ADG France
Aerospace and Defense Product Line
Committed to High Reliability and Long-Term Supply
  Delivering aerospace ICs for more than 30 years
  Strong flight heritage in space and avionics applications
  Leverage from automotive solutions for “new space” challenges: volume, cost and time to market
Major Product Focus
  ASICs
  Processors and microcontrollers
  Communication interfaces and memories
Long-term Cooperation with European Agencies:
  ESA, CNES, DGA, DLR …
Internal Qualified Supply Chain
  DLA/ESCC: Wafer lot to qualified parts (France)
  DLA: Assembly line (Thailand)
Microchip Nantes - France
Microchip MMT - Thailand
Foundry
Probe
Assembly
Design
Test
Microchip MMT - Thailand
Microchip Nantes - France
Microchip Rousset - France

## Slide 3: Microchip Space Portfolio
Communication Interface & memories
SpaceWire, Ethernet, CAN
SRAM
NVM memories
MPUs and MCUs
8-bit AVR
32-bit SPARC V8 and arm M3 & M7
GNSS SoC
FPGAs
RT PolarFire
RTG4 RT ProASIC3
RTAX, RTSX-SU
Mixed Signal Integrated Circuits
Telemetry and Motor Control Space System Managers
Power Supply protection
Timing solutions & Oscillators
Ovenized Quartz Oscillators
Hybrid Voltage Controlled & Temperature Compensated Crystal Oscillators
Cesium Clocks
Chip Scale Atomic Clock (CSAC)
Power Solutions
Rad-hard JANS Diodes, Bi-Polar Small Signal Transistors
Rad-hard Isolated DC-DC Converter Modules
Custom Power Supplies 2 W to > 5 KW
Point of Load Hybrid Solutions
Electromechanical Relays
RF Products
Packaged and Chip Si and GaAs RF Diodes,
SAW filters,
Packaged and bare die GaN and GaAs MMICs
GaN on SiC HEMT transistors.

## Slide 4
TTTech Group - Truly Global
Global Reach: 2300+ employees
20 locations/sites in 14 countries
headquartered in Austria
Off-Highway
Automotive
Aerospace & Space
Android & Services
Industrial & IoT

## Slide 5: TTEthernet Products
TTETesting Systems
TTETestbed
TTEDevelopment Systems
TTE Equipment
TTE Components
TTE Software (tools & embedded) - Building Blocks
TTE Development, Testing & Integration - Building Blocks
              TTEController HiRel (PBGA400, AEC-Q100)
              TTEController Space (CQFP352, QML-V)
              TTETools Development Suite
              TTEVerify and TTEAnalyze Verification Tools
              TTEDevelopment Systems Linux / VxWorks 653
              TTETesting Systems
              TTETestbed
TTEPlan
TTEAnalyze
TTEVerify
TTEBuild
              TTEEnd System Space 3U cPCI (EDU, PROTO, FLIGHT)
              TTESwitch Space 3U cPCI (EDU, PROTO, FLIGHT)

## Slide 6: Ethernet for Avionics Networks
Ethernet is becoming a more common standard in modern spacecrafts
Most used technology for local networks
Used in automotive, industrial control and aircraft avionics
Flexible, plug & play
High data rates
Open cross-industry standard (IEEE 802.3) with multiple providers
Connectivity: works with any commercial laptop
Enabler of more Ethernet in Space – component qualification

## Slide 7: TTEthernet for Spacecraft Network Systems
TTEthernet for high-reliable deterministic Ethernet for safety-critical systems
Protocol on top of standard Ethernet
Network devices synchronized autonomously via dedicated sync frames
Redundancy, network fault management, diagnostics data reporting - abstracted fully by the network
Used on Ariane 6 and as Gateway backbone

## Slide 8: What is Ethernet PHY ?
MAC layer builds the Ethernet packets transmitted to the PHY.
PHY includes the PCS and PMA (Physical Medium Attachment) sublayers.
  ENCRYPT and DECRYPT modules perform the format preserving encryption/decryption of 8b/10b symbols at the PCS sublayer.
  P/S and S/P modules are Parallel to Serial and Serial to Parallel modules, that transmit and receive the bitstream from the optical link.
BASE-T / BASE-TX
BASE-X / BASE-FX
Copper
Fiber
&

## Slide 9: VSC8541RT
Rad Tolerant Fast/Gigabit Ethernet PHY
Samples & Flight Models available
ESCC Detail Specification No. 9405/020
10/100/1000BASE-T Ethernet copper transceiver (IEEE 802.3ab compliant)
RGMII/GMII/MII/RMII MAC interface
Synchronous Ethernet and IEEE 1588 Start of Frame identification
Patented line driver with low EMI voltage mode
Wake-on-LAN
Supports clocking from 25 MHz crystal or 25/50/125 MHz oscillator
Host-free configurability through hardware strapping
Best-in-Class power consumption
Extended temperature range -55°C to 125°C
CQFP68 and VQFN68 packages
Radiation
TID 100krad(Si) SEL immune up to 78MeV.cm2/mg
Ceramic CQFP68
Plastic QFN68

## Slide 10: COTS to Radiation Tolerant devices
Start from industrial/automotive products |  | 
Same mask set Same functionality Same development tools | Easy access via commercial eval kit Free tool chain & libraries Same pin out as commercial device | Easy access via commercial eval kit Free tool chain & libraries Same pin out as commercial device
Hardening of critical parameters |  | 
Process tuning for no Single Event Latch-up at least up to 62 MeV.cm²/mg @ Tmax Total Ionizing Dose – Specific screening & Lot selection (>50Krad) Radiation report including SEU full characterization |  | 
Scalable solutions |  | 
Space Grade Ceramic: QML qualification & screening equivalent Minimum Ordering Quantity of 5 units |  | Hirel Plastic (HP): 3-Temp screening + Ext. Visual Inspection Minimum Ordering Quantity > 200 units

## Slide 11: VSC8541RT Radiation Results
Tests supported by CNES (Centre National d’Etudes Spatiales)
Single Event Latchup – SEL
  Performed under worst case conditions (Vccmax & 125°C)
  In accordance with ESCC25100 and MIL STD 883/Mil PRF 38535 standards
  Single Event Latch-Up LET threshold is higher than 78 MeV.cm²/mg
Single Event Upset – SEU
  SEFI conditions as well as Hard and Soft reset occurrence characterized
  Weibull curves and MTBF tables available for the different SEFI conditions
  No Power Off/On sequence was needed to restart the device after a link loss
Total Ionizing Dose – TID
  Performed according to MIL STD 883 TM1019 & ESCC22900 standards
  27 parts remained inside the specification limits after test read-out at 100krad(Si) on parametrical parameters and no functional deviation was observed
Radiation report available upon request

## Slide 12: VSC8541RT Qualification Results
Goal is to demonstrate high reliability and ability to withstand user environmental constraints
Qualification is based on:
  Technology Qualification
  Product Qualification for space applications
Technology Qualification
  Qualified with projected lifetime at 110°C higher than 15 years
Product Qualification for Space applications
  Successfully qualified on 3 successive assembly lots
  All tests passed successfully : HBM & CDM ESD, Electrical latch Up, Life test, Assembly/Packaging reliability tests, Construction analysis and Irradiation tests
VSC8541RT fully qualified and Qualification Package available upon request
Part of European Preferred Part List => ESCC Detail Specification No. 9405/020

## Slide 13: SoC w Embedded Ethernet for Space
Rad Hardened processor
ARM Cortex M7 SoC w TCM/MPU & DSP capabilities
>200DMIPS, 1MB SRAM w ECC, 128KB Flash w ECC
Spw, 1553, CAN FD, 100Mbit Ethernet gPTP/1AS TSN
Ready for Spacewire to Ethernet Gateway
Rad Tolerant µC
Radiations
TID 150krad (Flash limited to 20krad) SEL immune up to 62 MeV SEU LET >20Mev.cm2/mg (Xsection <10-9 cm2/word)
Radiations
TID 30krad SEL immune up to 62.5 MeV
SpaceWire
SpaceWire
CQFP256
BGA625

## Slide 14: Ethernet for Space - Looking forward
Supporting European space industry & agencies towards more Ethernet solutions
Targeting new RT/RHBD Ethernet devices for Space
  Ethernet PHY
    SGMII, FX & 10Gbit
  Ethernet Switch
    1 to 10Gbit (w/wo TSN)
  Ethernet SoC
    Gbit ARM MCU & MPU
    Gbit embedded IP for FPGA

## Slide 15: TTEthernet® Equipment for Gateway as Reference Design with VSC8541RT
Switch or network interface card (SONIC)
TTESwitch: interconnection of several nodes
TTEEnd System: ability for host computer to connect to TTEthernet
Main components
  TTEController: Main functional block for TTEthernet, contributing to all high-level functions
  VSC8541RT PHY: Translation of MII to MDI signals (100/1000 BASE-T) to provide connectivity to the function of the TTEController
SONIC-End System (Baseboard)
SONIC-Switch (Baseboard and Mezzanine)
TTEController (ceramic)
PHY (ceramic)
PHY (plastic)
PHY (ceramic)
PHY (plastic)
Internal I/F Connection
External I/F Connector
SONIC Elegant Bread Board (EBB) used for development tests

## Slide 16: SONIC Architecture and Main Functions
Modular design concept to provide flexibility, easy integration and maintenance for different use cases
SONIC supports multiple network lanes for fault-tolerant computer architectures
Main Functions
TTEEnd System Use-Case
Networking (BE, RC, TT)
Synchronization
Monitoring + commanding
Testing and debugging
SONIC-ES Board
PBA incl. TTE-Controller, PHYs, Peripherals
Frame
End System firmware
Driver
Networking (BE, RC, TT)
Synchronization
Monitoring + commanding
Testing and debugging
SONIC-SW Board
PBA incl. TTE-Controller, PHYs, Peripherals
Frame
Switch firmware
Network configuration
TTESwitch Use-Case
Main Functions
SONIC Switch (12 Ports)
SONIC End System (3 ports)

## Slide 17: VSC8541RT Performance Validation
Objective
Functional validation and performance measurements as a part of component qualification
Link speed: 1Gbit/s
Tests performed on Development Model (DM) and Elegant Bread Board (EBB)
Test Setup
Ports 2-3 daisy chained
Performance test script (PTP) running on Host CPU
Throughput measured via Wireshark and recorded via the test script (log-file)
Dropped frames counted and recorded (log-file)
SONIC Switch performance test setup with reduced daisy chain
Switch ID | SONIC Switch Model | TTE-Controller | PHYs (Baseboard) | PHYs (Mezzanine)
SW1 | DM | plastic | plastic | plastic
SW2 | EBB | ceramic | plastic | plastic
SW3 | EBB | ceramic | ceramic | plastic
Overview of SONIC Switch models used for performance tests

## Slide 18: VSC8541RT Performance Validation
Throughput, kBit/s
SW2 (EBB)
Data: Wireshark
Data: Log-File (Script)
Details
Chart: Time, s
| 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4000000000000001 | 1.6 | 1.7999999999999998 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8000000000000003 | 3 | 3.2 | 3.4000000000000004 | 3.5999999999999996 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.6000000000000005 | 4.8 | 5 | 5.2 | 5.4 | 5.6000000000000005 | 5.8 | 6 | 6.2 | 6.4 | 6.6000000000000005 | 6.8000000000000007 | 7 | 7.1999999999999993 | 7.4 | 7.6 | 7.8000000000000007 | 8 | 8.1999999999999993 | 8.4 | 8.6 | 8.8000000000000007 | 9 | 9.2000000000000011 | 9.3999999999999986 | 9.6
 | 984402 | 984499 | 984342 | 984427 | 984451 | 984402 | 984330 | 984427 | 984378 | 984463 | 984414 | 984414 | 984414 | 984390 | 984475 | 984451 | 984414 | 984414 | 984390 | 984390 | 984427 | 984451 | 984414 | 984390 | 984475 | 984390 | 984390 | 984269 | 984451 | 984414 | 984414 | 984439 | 984475 | 984366 | 984427 | 984378 | 984427 | 984427 | 984463 | 984439 | 984342 | 984439 | 984427 | 984402 | 984402 | 984451 | 984402 | 984451
100kBit/s
Data: Log-File (Script)
Chart: Time, s
| 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4000000000000001 | 1.6 | 1.7999999999999998 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8000000000000003 | 3 | 3.2 | 3.4000000000000004 | 3.5999999999999996 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.6000000000000005 | 4.8 | 5 | 5.2 | 5.4 | 5.6000000000000005 | 5.8 | 6 | 6.2 | 6.4 | 6.6000000000000005 | 6.8000000000000007 | 7 | 7.1999999999999993 | 7.4 | 7.6 | 7.8000000000000007 | 8 | 8.1999999999999993 | 8.4 | 8.6 | 8.8000000000000007 | 9 | 9.2000000000000011 | 9.3999999999999986 | 9.6
 | 984402 | 984499 | 984342 | 984427 | 984451 | 984402 | 984330 | 984427 | 984378 | 984463 | 984414 | 984414 | 984414 | 984390 | 984475 | 984451 | 984414 | 984414 | 984390 | 984390 | 984427 | 984451 | 984414 | 984390 | 984475 | 984390 | 984390 | 984269 | 984451 | 984414 | 984414 | 984439 | 984475 | 984366 | 984427 | 984378 | 984427 | 984427 | 984463 | 984439 | 984342 | 984439 | 984427 | 984402 | 984402 | 984451 | 984402 | 984451
SW3 (EBB)
Test Results
Successful tests for
  Different SONIC Models (DM/EBB)
  TTE-Controller and PHY configurations (plastic/ceramic)
1Gbit/s throughput successfully demonstrated
No dropped frames
Throughput results for different SONIC Switch configurations
2
4
6
8
10
0
Throughput, kBit/s
SW1 (DM)
1,00∙106
Time, s
0,75∙106
0,50∙106
0,25∙106
1,25∙106
1,00∙106
0,75∙106
0,50∙106
0,25∙106
1,25∙106
2
4
6
8
10
0
Time, s
Data: Wireshark
0
0

## Slide 19: Conclusion
Ethernet PHY successfully qualified
TTE-Controller (TTTech) and VSC8541RT (Microchip) – key components for high-speed deterministic Ethernet avionics networks for future spacecrafts
Reference design based on high-profile human space flight Gateway equipment
Thank you & please visit us at our exhibition booths to learn more about chip and board-level solutions for dependable avionics

## Slide 20: Thank You

## Slide 21: VSC8541RT ordering codes
VSC8541 Evaluation Kit
VSC8541RT Part Numbering
TID wafer lot data available for QML-V eq. under specific request
Tool | Part Number
VSC8541 Evaluation Board | VSC8541EV
Part Number | Package | Interface | Ethernet Bandwidth | Quality Flow
VSC8541WZBRT-E | CQFP68 | GMII / RGMII / MII / RMII | 10/100/1000Mbps | Engineering Sample
VSC8541WZBRT-MQ |  |  |  | QML-Q Equivalent
 |  |  |  | QML-V Equivalent
VSC8541WZBRT-SV |  | GMII / RGMII / MII / RMII | 10/100/1000Mbps | QML-V Equivalent
VSC8541XMVRT-HP | VQFN68 | GMII / RGMII / MII / RMII | 10/100/1000Mbps | Hirel Plastic (HP)

## Slide 22: VSC8541RT Reference Clocks
App Note AN3503: Reference Clocks from Vectron for VSC8541RT Radiation Tolerant Ethernet Transceiver
Microchip Part Number | Quality Level | REF Clock Frequency (MHz) | Oscillator Specification | Oscillator Model Number | Oscillator Supply Voltage(V) | TID (krad)
VSC8541WZBRT-E | Prototype (-E) | 25 | OS-68338/PX-709 | PX-709-0025-25M0000000 | 3.3 | 100
VSC8541WZBRT-MQ | QML_Q | 25 | OS-68338/PX-709 | PX-709-0026-25M0000000 | 3.3 | 100
VSC8541WZBRT-SV | QML_V | 25 | OS-68338/PX-709 | PX-709-0027-25M0000000 | 3.3 | 100
VSC8541XMVRT-HP | Hirel Plastic (-HP) | 25 | OS-68338/PX-709 | PX-709-0028-25M0000000 | 3.3 | 100
VSC8541WZBRT-E | Prototype (-E) | 50 | OS-68338/PX-709 | PX-709-0029-50M0000000 | 3.3 | 100
VSC8541WZBRT-MQ | QML_Q | 50 | OS-68338/PX-709 | PX-709-0309-50M0000000 | 3.3 | 100
VSC8541WZBRT-SV | QML_V | 50 | OS-68338/PX-709 | PX-709-0031-50M0000000 | 3.3 | 100
VSC8541XMVRT-HP | Hirel Plastic (-HP) | 50 | OS-68338/PX-709 | PX-709-0032-50M0000000 | 3.3 | 100
VSC8541WZBRT-E | Prototype (-E) | 125 | DOC204900 | 1403D125M0000CX | 2.5 | 100
VSC8541WZBRT-MQ | QML_Q | 125 | DOC204900 | 1403B125M0000CE | 2.5 | 100
VSC8541WZBRT-SV | QML_V | 125 | DOC204900 | 1403R125M0000CS | 2.5 | 100
VSC8541XMVRT-HP | Hirel Plastic (-HP) | 125 | DOC204900 | 1403C125M0000CB | 2.5 | 100
1403