## Slide 1: DESIGN OF A SPATIALLY RESOLVED VUV SPECTROSCOPY SYSTEM FOR SHOCK TUBE FLOWS
Maïlys Buquet, Alex Glenn, Peter Collen, Benjamin Williams, Matthew McGilvray and Tobias Hermann
University of Oxford
Tuesday 13 – Sept – 2022
RHTG Conference

## Slide 2: What? Shock Layer and Radiative Heating
Fig 1: Schematic of the high-temperature regions
in an entry-body flowfield [1]
Through shock
    Temperature increase
        Ionization & dissociation
          Chemical reactions induce radiation
→ Radiation causes additional heating
[1] Hypersonic and High Temperature Gas Dynamics, John D. Anderson Jr
Notes: Schematic of a typical entry case, which a shock layer in grey, which presents a complicated aerothermal environment
With total temperatures around 10000K. High temperatures cause ionization and dissociation of species, and these chemical
Reactions lead to additional heating to the surface

## Slide 3: What? Shock Layer and Radiative Heating
[2] Characterization of Stagnation-Point Heat Flux for Earth Entry, A. M. Brandis and C. O. Johnston, 45th AIAA Plasmadynamics and Lasers Conference, 2014
Fig.2: Share of radiative and convective heat fluxes at stagnation point for different velocities and nose radii. LAURA/HARA simulations, earth atmosphere. [2]
Through shock
    Temperature increase
        Ionization & dissociation
          Chemical reactions induce radiation
→ Radiation causes additional heating
At speeds > 10 km.s-1 :
Radiation becomes substantial / main source of heat load
→ non-equilibrium region
→ high energy transition in the vacuum ultra-violet (VUV) can
become dominant
(up to 85% of the total post-shock radiance for high enthalpy shock tube tests [3])
[3] Air Radiation in Superorbital Expanding Flow, Han Wei, Thesis
Large
uncertainties
→
Largest source of
uncertainties
→
Due to complexity of measuring rad. in this wavelength – fully absorbed by atmosphere
Notes: At speeds characteristic of re-entry, radiation can actually become the main source of heat load, which we can see on these simulations. The contribution of convective and radiative heat flux to total heat flux at stagnation point is shown for 2 vehicles of radii 1 and 5m, for speeds ranging from 10 to 15km.s.
We can see that in both cases, the contribution from radiative heat flux shown in red quickly becomes dominant, and even represents up to 90% of the total heat flux for a 5m radius vehicle at 15km.s.
Within this radiative heat flux, a large portion can arise from the non-eq region, in which the chemical reactions are not in equilibrium with their backwards reactions, as well as from high energy transitions in the VUV region of the spectrum which were experimentally found to represent up to 80% of the total post-shock radiance.
Despite being a substantial part of the temperature challenge, the models currently in use suffer from large uncertainties, mainly due to the complexity of measurement data in this region of the spectrum.

## Slide 4: What? Shock Layer and Radiative Heating
[2] Characterization of Stagnation-Point Heat Flux for Earth Entry, A. M. Brandis and C. O. Johnston, 45th AIAA Plasmadynamics and Lasers Conference, 2014
Radiation becomes substantial / main source of heat load
→ non-equilibrium region
→ high energy transition in the vacuum ultra-violet (VUV) can
become dominant
Large
uncertainties
→
Largest source of
uncertainties
→
→ Overdesign of thermal protection systems
Reduced travel distance / useful load
Increased cost / waste
Better understanding → better model → more sensible design
Obtain spectra and absolute radiance from VUV:
very valuable
→ species number densities
→ temperature
Fig.2: Share of radiative and convective heat fluxes at stagnation point for different velocities and nose radii. LAURA/HARA simulations, earth atmosphere. [2]
Notes: These uncertainties directly reflect on the overdesign of thermal protective systems, leading to reduced travel distances and increased costs and wastes.
Being able to better understand the reentry environment would allow us to obtain better models and design more sensibly.
Motivation behind obtaining spectra and measurements of absolute radiance in the VUV, as these would allow us to obtain valuable info about flowfield the vehicle is interacting with

## Slide 5: How? Shock tube to recreate conditions
[1] Hypersonic and High Temperature Gas Dynamics, John D. Anderson Jr
Fig 1: Schematic of the high-temperature regions
in an entry-body flowfield [1]
≡
Fig 4: T6 shock tube schematic, modified from [4]
[4] High Enthalpy Effects in Transpiration Cooled System, S. D. Subiah
T6 shock tube mode
High speed, high enthalpy facility
Notes: How are we planning on doing that? Through shock tube experiments, in the Oxford T6 shock tube, which is a high-speed, high enthalpy flow type of facility.
Shock tube experiments allow us to create a partial simulation of a re-entry flow, by assuming that the stagnation streamline in the slug of gas between the shock and the vehicle is equivalent to the slug of gas following a normal shock in the tunnel.

## Slide 6: How? Spectroscopy to investigate the flow
Andor iStar sCMOS
Vacuum chambers
containing mirrors
Spectrometer
Intensified
camera
[5] Measurements of Radiating Hypervelocity Air Shock Layers in the T6 Free-piston Driven Shock Tube, P. L. Collen, L. J. Doherty, M. McGilvray
Fig 5: Example spectra (T6s52, 10.18 km.s−1) red spectrum [5]
Species
Temperature
Species number
densities
Tunnel
axis
Shock direction
Shock
Notes: When the conditions are (hopefully) reached, the flow can then be investigated through spectroscopy. And this is where I spent my last year, designing a VUV spectroscopy system for our T6 wind tunnel.
The light emitted by the radiation in the test section (here shown in purple) is received by a bunch of mirrors contained in vacuum chambers.
The mirrors collimate, focus and redirect the light information on our spectrometer which divide the light by its wavelength components.
An intensified camera allows us to visualize the spatially resolved spectra, where we can see the radiation intensity behind the shock for different wavelength.
By integrating this signal, the spectral radiance can be obtained. It acts as a footprint of the chemical reactions in the gas.
From these, we can infer species present, their densities, and therefore temperature.

## Slide 7: How? Spectroscopy set-up on T6
→ Allows to keep
system under
vacuum during
tunnel turn-around
Spectrograph
Vacuum chambers
Camera
Shock
tube
Turbopump
Test section
Notes: To be able to obtain signal in the VUV, the light path has to be fully evacuated to avoid absorption.
Additionally to the spectrometer and the camera, the volume to be pumped down consists of two vacuum chambers containing the mirrors.
The whole system connects to the tunnel via a window insert, which slides into the side of the test section.
The biggest chamber, which connect to the tunnel, is mounted on a set of rails (in blue) which allows to extract the spectroscopy system during tunnel turn-around, while keeping the whole system under vacuum, up to the window.
A set of bellows connects the two chambers, such that the spectrometer and camera can stay in place during this procedure.

## Slide 8: How? Spectroscopy set-up on T6
→ Can perform calibration during turn-around using a deuterium lamp
Notes: In the meantime, during turn-around, a calibration box can be mounted on the system, approximately at the tunnel’s axis location, to perform calibration in conditions as close to the experiment as possible. The deuterium source used for calibration is mounted on a plate which can slide to mimic the different shock locations.

## Slide 9: How? Optical system design
[6] Collection Optics for Imaging Spectroscopy of an Electric Arc Shock Tube, Greenberg, Reid, Cruden, Brett, Grinstead, Jay, Yeung, Dickson
Shock
Tunnel
axis
Blur
θ
Chief rays from all object points
perpendicular to shock tube
Blurring effects due to
non-telecentricity [6]
Notes: The optics inside the chambers were designed as a telecentric system, as it was shown that telescopic systems can lead to blurring effects. Keeping the chief rays from all object points perpendicular to the shock tube allows to obtain a better spatial resolution. To achieve this, a few geometrical constraints have to be followed.

## Slide 10: How? Optical system design
Bunch of constraints
Optical
Magnification
Matching F#
Focal lengths
90deg turn for camera
Minimum number of mirrors, smallest angles possible…
Geometrical
Must fit in boxes
Must not be on optical path
Tilting mirror makes it harder to make them fit
Optimisation approach with a code
Position and geometry of mirrors
Ray-tracing simulation using OPTOMETRIKA [7]
[7] Optometrika (https://github.com/caiuspetronius/Optometrika), Yury, 2002
Tunnel axis
Spec.
slit
Notes: As the vacuum chambers already existed, this lead to a bunch of optical but also geometrical constraints. These were used as inputs for an optimization code, to obtain the position and geometry of the mirrors. These were then used to run so ray-tracing simulations.

## Slide 11: How? Optical system characterisation
Cylindrical mirror
Helps rays lying in perpendicular planes on the optical axis to focus at different distance
Strategy used for the VUV
spectroscopy set-up in EAST [6]
[6] Collection Optics for Imaging Spectroscopy of an Electric Arc Shock Tube, Greenberg, Reid, Cruden, Brett, Grinstead, Jay, Yeung, Dickson
Notes: On top of confirming collimation, the simulations could be used to characterise the system. By placing a virtual screen (basically a virtual sensor with size and resolution of the camera’s sensor which allows us to plot the intensity received by each pixel), we found that the system suffered from astigmatism, a uni-directional aberrations where rays lying in perpendicular planes on the optical axis focus at different distances, and this could be corrected by introducing a cylindrical mirror instead of a flat turning mirror between the two powered mirrors. This same strategy was used for the VUV spectroscopy set-up in EAST. We can see that axisymmetric signal of satisfying intensity is recovered.

## Slide 12: How? Optical system characterisation
θ > 40deg
θ = 30deg
Magnification:
M = 10.5 → M = 7.2
Notes: Originally, the intensity of the signal was also affected by the large angle between the cylindrical and focusing mirror. An additional constraint was added to the code such that the angle would not go above 30deg. This forced a comprise on the magnification of the system, which went from 10.5 to 7.2, still allowing a view of 150 along the tunnel’s axis.

## Slide 13: How? Calibration
→ Some effects obtained from simulations
SPACE
→
LSF
SRF
Notes: The system was then calibrated to quantify its resolution and limits. Although the spec/cam/deut lamp were in place, the focusing optics were still missing so simulations were used to approximate the spatial smearing function.
The first function, the Line Spread Function, which corresponds to the optics and camera resolution blurring, was obtained by generating a step emission at axis of shock tube (i.e a white square of light with sharp edge). This signal is then ran through the simulated optical system to record what would be imaged at spec slit, and the derivative of the signal is then fit to a sqrt of voigt. In an ideal system, this would correspond to a Dirac impulse, but in practice we obtain some thickness due to imperfect optical system, blurring spatially our shock.
The second function corresponds to the depth of field effect, and is obtained by obtaining the angle at which the chief rays emanating from the center of the tunnel hit the window. The blurring induced is approximated by a triangular function of the same angle.
Finally, the effect of the shock motion during exposure time is expressed as a square function of width equal to the product of the shock speed and the gating time.
-> convolve for 3 for total spatial smearing function, which can be applied to ideal simulation to recreate what we would be getting out of our system during experiments. The real radiance distribution is dotted line, but red is what we’d be able to obtain through experiments, showing limit of system to what we can spatially resolve.

## Slide 14: How? Calibration
SPACE
WAVELENGTH –
– INTENSITY
→ Some effects obtained experimentally
Mercury lamp spectra
Deuterium lamp spectra
Notes: The wavelength and intensity calibration curve could be obtained experimentally
The wavelength to pixel distribution was obtained by placing a mercury lamp in front of the spectrometer slit and recording its spectra. These thin lines could then be fitted to the wavelength they correspond to to obtain a wavelength to pixel location relation.
The intensity calibration was obtained using a deuterium lamp mounted of the spectrometer. The spectral radiance measured was then fitted to the radiance curve given by the manufacturer to obtain a value of radiance per count.

## Slide 15: What’s to come… hopefully
→ Calibration applied to Poshax [8] and NEQAIR [9] simulations
→ Simulations ran to select wind-tunnel conditions
→ EAST conditions - gave good VUV data
→ Fire II re-entry datapoint
→ Data point from previous T6 campaign
[8] Eilmer 4.0 flow simulation program. P. A. Jacobs and R. J. Gollan, 2022.
[9] NEQAIR - Nonequilibrium Radiative Transport and Spectra Program, NASA
P∞ = 26.66 Pa
u∞ = 10.66 km.s-1
P∞ = 2.08 Pa
u∞ = 11.36 km.s-1
P∞ = 6.66 Pa
u∞ = 11.38 km.s-1
Notes: Finally, these smearing functions were used on simulations ran to select possible conditions of interest for T6 experiments. Applying the smearing functions to ‘ideal’ simulations allows us to visualize more accurately what our set-up would be able to collect from the wind tunnel tests.
Three conditions were selected, one to recreate a shot by EAST giving good VUV data, one to simulate a Fire-II entry point which was simulated in a few papers, and one to recreate conditions from a previous T6 shock.
Simulation of shock tube chemistry with poshax, and of non-equilibrium radiative transport were performed using Poshax and Neqair, to obtain EAST style plots to visualize for each case the radiance intensity as a function of distance from the shock, as well as the spectrally resolved radiance. From these, we can select conditions which seem interesting to us.
The first one, as a conditions tried by NASA and known for giving high levels of spectral radiance behind the shock, can help us to characterize the resolution of our system.
The second point, despite giving lower levels of spectral radiance, showed nicely defined region of non-equilibrium.
And the last point, which corresponds to a conditions previously tested in our tunnel, on top of giving us further information for data we already have, shows levels of spectral radiance comparable to the EAST test.

## Slide 16: Summary
So far…
→ Mechanical system designed,
almost fully assembled
→ Optics designed and characterised
→ Couple of test conditions selected
To come…
→ Characterised rest of optics (mirrors)
→ Pump down full volume
→ T6 test campaign to obtain spectra

## Slide 17: Thank you for listening!