## Slide 1: MAVERIC
Speaker: Antonio Rotondi, Riccardo Moro
Moving To Mars Workshop

## Slide 2
SEEDS XIV: OUR TEAM

## Slide 3: Mission Statement
Mars
VEhicle
forR
Interplanetary
Cruise
“To safely transfer the crew from Earth on a roundtrip mission to Mars, cooperating with international infrastructure to pave the way to human exploration of Mars.”

## Slide 4: Design Reference Mission
Mars Capture
4
Interplanetary trajectory to Mars
Interplanetary trajectory to the Moon
Moon capture
Transfer to Moon PO
1
2
3
6
7
Launch
Assembly in Lunar orbit
5
Transfer to MPO
8
Total ΔV
7.1 km/s
Assumption
Mars Ascent and Descent Vehicle
Earth Ascent and Descent Vehicle
space tugs
Infrastructure with supply

## Slide 5: Trajectory
250 days
381 days
265 days
Departure from the Moon 13th of October 2039
Arrival on Mars 19th of June 2040
Departure from Mars 5th of July 2041
Arrival on the Earth 27th of March 2042
TOTAL TIME: 896 days

## Slide 6: Overall view of the spacecraft
Nuclear reactors
Radiators
Radiators
Antenna
Tanks
Truss structure
Habitat
Bryton generator
Dimensions
Length ∼ 60 m
Diameter ∼ 22 m
Mass ∼ 420 tons

## Slide 7: Structures
Truss Structure
Pressurized Module
The Truss structure have to sustain the loads during the orbital manoeuvres while habitable modules have to sustain the mechanical stress caused by the internal pressure

## Slide 8: Electric Power System
Bimodal Nuclear PG
Brayton Engine
Li-ion batteries
Autonomy 18 h
Safe mode = 45.9 kW
Nominal mode = 58.8 kW

## Slide 9: Propulsion
33 kN
925 s
x3 engines
8 radial tanks
12m x ⌀ 6.8m
24.7 t capacity
2 inline tanks
10m x ⌀ 4.5m
8.9 t capacity
Total capacity: 215 t of LH2
Credit: BWX Technologies
Nuclear Reactors

## Slide 10: Thermal Control System
Fluid Loops
Radiators
60 Layer MLI
25 Layer MLI
Cryocooler
40 layer MLI
25 Layer MLI

## Slide 11: Attitude and Orbital Control System
Sensors
Actuators
Inertial Measurement Unit
Sun sensors
Star trackers
Navigation Camera
Space sextant
Control moment gyros
Radius: 0.4 m
Mass: 109 kg
Angular momentum: 6000 Nm
1
Reaction control system
Trust: 219 N
Propellant mass: 449 kg
Arm lever: 20 m
2

## Slide 12: Communication strategy
Deep Space Network
L4/L5 Relay
MAVERIC High Gain Antenna x2
5 m diameter
X Band
S Band
Ka Band
*S Band
Mars Relay
MAVERIC
HGA

## Slide 13: Environmental Control System
Remove CO2: 4.0 kg/day
Provide O2: 3.3 kg/day
Crew metabolic heat: 440 Wth
Pressure: 97 - 103 kPa
Temperature: 18 - 27 °C
Humidity: 40 - 70%
Mass budget | 2640 kg
Nominal power | 8.23 kW
Safe mode | 4.15 kW
Subsystem margin | 10%
Temperature Humidity Control
Air
Revitalisation System
OGA = Oxygen Generation Unit (Water Electrolyser) CCA = Carbon Concentration Assembly (4BMS)
CRA = Carbon Removal Assembly (Sabatier Reactor) MPA = Methane Processing Assembly
Fire
Detection
Suppression
Atmosphere
Control
Supply
Notes: To support the crew The environmental control system provide O2 and remove CO2 from the internal atmosphere. A oxygen generator unit create oxygen from water electrolysis while a corbon removal assembly based on a sabbatier reactor will process the (Comon Cambin Assembly) and Methan Processing Assenbly (MPA)

## Slide 14: Life Support
Supply
1,8 kg/CM/day
Total of 8500 kg
Greenhouse
Surface: 11.8 m2
Mass: 1200 kg
Volume: 12 m3
Power: 6.5 kW
Water Processor
Assembly
Urine Processor
Assembly
Heat Melt Compactor
Sabatier cycle
Brine Processor
Assembly
Recover water
Reduce volume of trash
Reduce biological activity
Stabilize processed trash
Tiles used as radiation shields
FOOD
13.02 kg/CM/day
η = 97.6%
Total water onboard 1940 kg
WATER
WASTE
Notes: The food resources are composed by a supply of 8500 kg that cam ensure 1.8 kg per CM per Dauwe also implement a grwwnhouse to provide about 2% of the crew needed but most important it can provide fresh food.

## Slide 15: Spare Management
Reduction | 
37% | Volume
37% | Mass
From ground
Mass: 2495.48 kg
Volume: 8.25 m3
Foam
From ground
Waste on board
Printing
Raw material

## Slide 16: Zero-G countermeasures
Short Arm Centrifuge
Combination of a centrifuge with
a cycle ergometer
1
Suits
Lower body negative suits and gravity suits
2
Pneg
F
Exercises Equipment
Treadmill and resistive exercise machine
3
Drugs
Promethazine, Amoxicillin, Bisphosphonates
4

## Slide 17: Radiation Protection
Hydrogen tank
Cargo
Polyethylene + Waste tiles
Water
External reactor shielding
(180mm Be, 20mm W, 50mm LiH)
Internal Reactor shielding
Waste tiles (50mm)
Polyethylene (50mm)
Al structure
BNNT (20% H2) (2mm)
BNNT (20% H2)

## Slide 18: Habitable Module Configuration
The habitable volume is designed to host 4 astronauts.
21 m
Internal habitable volume 25 m3 per astronaut
Divided in 3 segments to optimize launch
4.2 m
Cargo
Habitable 1
Habitable 2
The length of the modules is 21 m
2.2 m
Internal Dimensions

## Slide 19: Habitable Module description
Medical Area
Positioned to reduce passages in case a crew member is ill
Cargo
Medical area
Living Room
Leisure activities and institutional meetings
Galley and
Living room
Green House
A small greenhouse is present to produce part of the food needed
Greenhouse
Workspace
Workspace
Payload and 3D printer
Crew quarters
Waste and Hygiene
Waste and Hygiene
Area devoted to water recycling and waste management (tiles production)
Physical Exercise
Short arm centrifuge and training machines
Water Tanks
Clear water tanks and brine tanks
Water tanks
Physical
exercise
Racks Contents
ECLSS
Stowage
Surgery Table
Shower

## Slide 20: Mass Budget Costs
Chart: 
| Structures | AOCS | EPS | TCS | Propulsion | TT&C | OBDH | Payload | ECLSS | Harness
 | 28.2677 | 0.56206 | 10.24 | 12.622 | 50.4 | 0.48934 | 0.6868 | 0.38 | 27.9219 | 6.5785
TOTAL MASS: 420 tons
Advanced Missions Cost Model*
66.65 B€*
Ref : «Comparing NASA and ESA Cost Estimating Methods for Human Missions to Mars» / ISS Operation cost / Colombus cost analysis
*Neglecting inflaction in 2040
Launch
Manufacturing
Operation
Development

## Slide 21
2nd Level Specialising Master’s Programme
SPACE EXPLORATION AND DEVELOPMENT SYSTEMS
bit.ly/SEEDSMaster22
Enrolment Deadline: November 25th 2022

## Slide 22
key partners and sponsors

## Slide 23
Moro Riccardo s305160@studenti.polito.it
Rotondi Antonio s305112@studenti.polito.it