## Slide 1
Feasibility of vehicle-based propellant production on Mars using the Sabatier reaction
UBC Mars Colony
University of British Columbia
Engineering Design Team
Moving to Mars 2022
4:10 pm, 17 Novembre 2022,
Concordia University
Francis Desilets-Mayer

## Slide 2
Introduction
Francis Desilets-Mayer, P. Eng,
  MASc. (UBC), BSc. (UofC)
UBC Mars Colony (ubcmarscolony.com)
  University of British Columbia, (UBC) Canada
  ≈20 members
  Multiyear research project

## Slide 3: Project background
SpaceX 2016 mission architecture1
  Refuel a Starship Rocket on Mars
  1200 tons of Methalox in 26 month
Sabatier reaction2
  Martian air (95% CO2), H2O ice (trace HClO4)
Sabatier reactor project
  Benchtop reactor sub-project3
  Sabatier plant design sub-project

## Slide 4: Methodology
Process flow simulation
  Give you flowrate and duty (kW)
  DWSIM (dwsim.org)
Equipment sizing
  Use flow rate and duty kW to get size
  Fitting equipment chart
Chart: 
| 22.371000000000002 | 5.5927500000000006 | 11.185500000000001 | 3.7285000000000004 | 37.285000000000004
 | 1.5682 | 0.62291 | 1.1217 | 0.35789 | 1.7081

## Slide 5: Process flow diagram
0.006 atm
-63 °C
0.0117 kg/s
0.030 atm
-53 °C
0.0092 kg/s
1.000 atm
-161 °C
0.0037 kg/s
1.000 atm
-183 °C
0.0153 kg/s
252 tons CH4; 1051 tons O2 in 26 months
Notes: Fuel ratio 3.764065
Leftover oxygen 102.5175 tons

## Slide 6: Reactor and Electrolysis Loop4
Power: 335 kW, Size: 3.9 m3
Electrolyser energy efficiency 83%
Overall energy efficiency 7.1%

## Slide 7: Atmosphere Acquisition and Cooling
Cooling6
  Air flow: 16.4 kg/s
  Power: 78 kW,
  Size: 1.1 m3
Atmosphere capture5
  5 kW input gives 1 kW cooling
  Power: 42 kW, Size: 4.5 m3

## Slide 8: Gas Treatment and Liquefaction
Gas liquefaction7
  Power: 194 kW, Size: 10.4 m3
  Energy efficiency: 5.2%
Gas conditionning8
  Power: 23 kW, Size: 6.3 m3
  Energy efficiency: 3.4%

## Slide 9: Result Size and Energy
Overall energy efficiency: 7.1%
Total Size: 25.2 m3
Total Power: 598 kW
Chart: 
| Atm. Capture | Electrolysis | Sabatier | Liquefaction | Gas Cleanup
Size(m3) | 4.5366 | 2.5249 | 1.3805 | 10.4196 | 6.31
Chart: 
| Atm. Capture | Electrolysis | Sabatier | Liquefaction | Gas Cleanup
Energy (kW) | 47.035 | 304.4951 | 30.8065 | 193.5436 | 22.5423
SpaceX’s Starship cargo space 9 : 1000 m3

## Slide 10: Conclusion
Key takeaway
  The propellant plant fits in the rocket
  Even if energy efficiency is low
  Sabatier reactor is a minute contributor
  Liquefaction and electrolysis are important
Recommendation
  Sabatier reaction: not the best choice
  Less complex system are possible
  Always propose full plant
Chart: 
| Blower | Compressor | Electrolyser | Heater and Pump
Energy (kW) | 78.2021 | 195.2071 | 274.688 | 50.3253
Total Power: 598 kW

## Slide 11: Acknowledgements

## Slide 12: Reference
1. Musk, E. Elon Musk Unveils SpaceX’s Mars Interplanplanetery Transport System Architecture AT IAC 2016. www.youtube.com/watch?v=SPblvBnEDk (2016).
2. Franco, C., Devor, R. W., Snyder, S. J., Petersen, E. & Hintze, P. E. Study of Sabatier Catalyst Performance for a Mars ISRU Propellant Production Plant. 1–12 (2019).
3. Schoen, D. Design and Validation of a Lab-scale Methalox Fuel Plant for In-situ Propellant Production on Mars Dagan Schoen. in Congress, International Astronautical 18–22 (2022).
4. Falbo, L. et al. Kinetics of CO2 methanation on a Ru-based catalyst at process conditions relevant for Power-to-Gas applications. Appl. Catal. B Environ. 225, 354–363 (2018).
5. Clark, D. L., Payne, K. S. & Trevathan, J. R. Carbon dioxide collection and purification system for mars. AIAA Sp. 2001 Conf. Expo. 1–5 (2001) doi:10.2514/6.2001-4660.
6. Colgan, N., Nellis, G. & Anderson, M. Forced Convection Heat Rejection System for Mars Surface Applications. in 1–13 (2021).
7. Naik, M. Y. 4-Stage Refrigeration Process with Propylene , Ethylene , Methane and Nitrogen.
8. Vaidya, S. Sweetening of Natural Gas Followed By Manufacturing of LPG.
9. Paul, R. A., Lamontagne, M. & Senna, B. Proposed ITS pressurized cargo modules to initiate a chemical industry on mars. AIAA Sp. Astronaut. Forum Expo. Sp. 2017 (2017) doi:10.2514/6.2017-5335.

## Slide 13
Q&A
Francis Desilets-Mayer,
fdmayer@student.ubc.ca
UBC Mars Colony
ubcmarscolony.com
Contact us
for simulation file and details