## Slide 1: Verification of a CCSDS121-based data compression IP core through fuzzing
Antonio J. Sánchez**
Joan Bartrina-Rapesta*, Yúbal Barrios**, Roberto Sarmiento**, Ian Blanes*, Miguel Hernández-Cabronero*, Joan Serra-Sagrista*
14th March 2023
*UAB: Autonomous University of Barcelona
** IUMA/University of Las Palmas de Gran Canaria

## Slide 2: Outline
Introduction
Conclusions
Fuzzer for hardware designs
Test campaign and results
Fuzzing background

## Slide 3: Introduction
IP cores commonly used in system-level design.
  Costs and development time savings.
Classical IP core verification: Test campaign with predefined cases.
  Hierarchical verification: blocks, modules, system.
  Verify functionality based on directed test-cases.
  Maximize code coverage.
  Easy link with IP requirements: coverage matrix.
  “Ease of documentation”.
With more complex IP cores, is this still enough?
Alternative approaches:
  Formal verification
  UVM, standard with support from multiple vendors
  Fuzzing: random generation of test vectors

## Slide 4: Outline
Introduction
Fuzzing background
Fuzzer for hardware designs
Test campaign and results
Conclusions

## Slide 5: Fuzzing background
Real tested program
Glue code - reads and adapts input
Fuzzing harness
Fuzzing flow for software testing:
  Mutation-based
Fuzzer: generates inputs and manages execution of program under test.

## Slide 6: Fuzzing background
Coverage-guided fuzzing:
  Original test vector
  Mutated test vector
  Same coverage  discard
  Mutated test vector
  New coverage  add to test set

## Slide 7: Outline
Introduction
Conclusions
Fuzzer for hardware designs
Test campaign and results
Fuzzing background

## Slide 8: Fuzzing for hardware designs
Recent efforts towards fuzzing of hardware designs:
  Rfuzz[1]:
    “Fuzzing hardware as software”
    MUXES are treated like software branches.
    Fuzzing of DUT + logic simulator.
  HW-Fuzzing[2]:
    SW model generated from RTL description.
    Fuzzing of DUT only.
    Relies on SystemVerilog assertions.
[1] K. Laeufer, J. Koenig, D. Kim, J. Bachrach, and K. Sen, “Rfuzz: Coverage-directed fuzz testing of RTL on FPGAs”, in AsianHOST 2017.
[2] T. Trippel, K. G. Shin, A. Chernyakhovsky, G. Kelly, D. Rizzo, and M. Hicks, “Fuzzing hardware like software”, https://arxiv.org, 2021.

## Slide 9: Proposed fuzzer architecture
Requirements:
  Fuzzer.
    American Fuzzy Loop.
  SW golden reference for coverage-guided fuzzing.
  Design under test:
    Hardware description for logic simulation, or
    Implementation for on-board testing.
HW simulation much slower. Strategies:
  Precompiled sources (except test configuration).
  Test vectors filtered, based on code coverage.
  Multiple hardware simulator instances running in parallel.

## Slide 10: Proposed fuzzer architecture
UDP Socket
TCP/IP Socket
TCP/IP Socket
TCP/IP Socket
IP Core Fuzzer
Reference Software
Code coverage
expected output
Fuzzer Harness
input raw
Fuzzer
input raw
return code
configuration
input raw
Agent 1
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration
Orchestrator
Extract configuration
Task Collector
Output
expected output
input raw
configuration
IP Core output
input raw
expected output
return code
expected output
IP Core return code
VHDL configuration
configuration
input raw
Agent 2
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration
configuration
input raw
Agent n
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration

## Slide 11: Proposed fuzzer architecture
IP Core Fuzzer
Reference Software
Code coverage
expected output
Fuzzer Harness
input raw
Fuzzer
input raw
return code
IP core fuzzer:
  Encapsulates fuzzer, reference software and fuzzing harness.
  Generates input test vectors.
  Test vectors are fed to reference software to:
    Compute expected output.
    Gather coverage metrics for fuzzing.
  Fuzzer harness collects test vectors and expected outputs and filters them for orchestrator.

## Slide 12: Proposed fuzzer architecture
Orchestrator
Extract configuration
Task Collector
Output
expected output
input raw
configuration
IP Core output
input raw
expected output
return code
expected output
IP Core return code
VHDL configuration
Orchestrator:
  Receives input test vector and expected output from IP core fuzzer.
  Extracts IP configuration from expected output header.
  Selects an agent to run the test and provides all relevant data.
  Collects IP core output and compares it with expected output.
  Stores all simulation data for crash debugging, hardware coverage analysis, …

## Slide 13: Proposed fuzzer architecture
configuration
input raw
Agent 1
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration
configuration
input raw
Agent 2
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration
configuration
input raw
Agent n
IP Core output
VHDL Simulator
IP Core return code
expected output
VHDL configuration
Pool of agents:
  Agents implemented in virtual machines.
  Each agent receives input test vectors, IP configurations and expected outputs from orchestrator.
  Performs hardware simulation.
  Simulation outputs are sent back to orchestrator.

## Slide 14: Outline
Introduction
Conclusions
Fuzzer for hardware designs
Test campaign and results
Fuzzing background

## Slide 15: Case study
Case study: CCSDS121 compression IP
  Lightweight universal lossless compressor.
  CCSDS 121.0-B-3 standard compliant.
  2 functional blocks:
(optional)
Block-adaptive
Unit-delay predictor
  Previous sample is used as an estimator of the current one.
  Periodic insertion of reference samples
  Based on Rice codes.
  Input grouped in blocks of J size.
  Shortest code is selected for each block.

## Slide 16: Case study
Case study: CCSDS121 compression IP
  Fully tested with traditional methodology.
  Functional verification based on direct test-cases.
    IP verification plan included:
      More than 30 images of different sizes, dynamic ranges, and sample distribution.
      32 sets of configuration parameters (both compile-time and run-time).
    Verification test campaign: around 100 tests
      Verification includes basic sanity tests and additional test cases to improve coverage.
  Results:
    All tests passed.
    Achieved code coverage: 100%

## Slide 17: Experimental setup
Case study: CCSDS121 compression IP
  CCSDS 121.0-B-3 reference software by CNES.
  Fuzzing for data input and IP configuration (runtime configurable).
  Workstation used for tests:
    AMD Ryzen 9 3900X 12-Core Processor.
    48 GB RAM DDR4.
    SSD 1TB.
  Pool of 20 agents.
  +1 000 000 test vectors
  Throughput: 1.5 tests/s

## Slide 18: Experimental results
Case study: CCSDS121 compression IP fuzzing results
  18 unnoticed bugs found:
    Wrong header generation for specific IP configurations.
    Reference sample insertion with zero-block option.
    Zero-block encoding at end-of-segment.
    Reference sample interval R=1.
    Dynamic range D<4 and restricted codeset.
    Encoding of last block under certain conditions.
    Wrong computation of second-extension option length.
    Output packing errors.
    …

## Slide 19: Experimental results
Case study: CCSDS121 compression IP Implementation results:
  Target board: Kintex UltraScale XCKU040.
  IP configuration:
    D = 16
    W_BUFFER = 64
    J = 64
    R = 4096
  Synthesis with Synplify Premier P-2019.09-SP1
Implementation | LUTs | FFs | DSPs | BRAMs | Freq (MHz)
Before debugging | 8463 | 2368 | 6 | 5 | 142.8
After debugging | 9116 | 2542 | 8 | 3 | 147.6

## Slide 20: Outline
Introduction
Conclusions
Fuzzer for hardware designs
Test campaign and results
Fuzzing background

## Slide 21: Conclusions
IP cores growing in complexity:
  Classical IP verification may not reach all corner cases.
  Other verification approaches: fuzzing.
HW verification through fuzzing:
  Able to find hidden corner cases.
  Networked fuzzer architecture proposed.
    Applicable to any soft IP core.
    Scalable via LAN.
  Requires a SW golden reference.
  Test vectors stored, can be used for code coverage.
Case study: compression IP CCSDS121-based.
  +1 000 000 test vectors  18 bugs found.
Fuzzing complements classical verification.

## Slide 22
Questions?
Antonio J. Sánchez
E-mail: ajsanchez@iuma.ulpgc.es