## Slide 1: Open-source reconfigurable processing system for novel high-performance space applications
Álvaro Ortega1, Alfonso Rodríguez2, Eduardo de la Torre2, Juan Antonio Ortega1
1AIRBUS CRISA 2Universidad Politécnica de Madrid

## Slide 2: A bit of spam…
Center of Industrial Electronics (CEI-UPM)
  Reseach center at Universidad Politécnica de Madrid, Spain
  Research lines: Digital Embedded Systems, Power Electronics
  Strong relationship with companies (e.g., Industrial Council)
Digital Embedded Systems @ CEI-UPM
  7 full-time professors (1 on temporary leave) + 6 full-time PhD students
  Research lines: IoT systems, post-quantum cryptography, Edge AI/ML, Reconfigurable HW and FPGAs, adaptive RISC-V processors
  Strong presence in competitive project calls (e.g., H2020, KDT JU)

## Slide 3: Context and Motivation
NewSpace scenarios
  Space missions treated as a commercial industry
  Higher computational requirements → better devices and processors
  Higher competition → reduction in costs, reusability
Run-time reconfigurable COTS SRAM-based FPGA devices
  Support for time-multiplexed HW resources (same FPGA, larger accelerators)
  Support for OTA HW updates (increased system lifetime)
  Less tolerant to radiation-related effects (additional fault detection, mitigation and recovery techniques are required)
Open-source standards, computing architectures and tools

## Slide 4: Main Issues in FPGA-Based Systems
D. Göhringer, “Reconfigurable Multiprocessor Systems: Handling Hydras Heads – A Survey”, in SIGARCH Comput. Archit. News, vol. 42, no. 4, p. 39–44, Dec. 2014.
Lack of proper hardware architectures to deal with highly dynamic scenarios
Lack of adequate design tools to isolate developers from low-level technology details
Lack of user-friendly runtime environments to manage application execution
Computing Performance
Energy Efficiency
Fault Tolerance
Automated DPR Flows
High-Level Accelerator Descriptions
Parallel Execution
Computation Offloading
DPR Management

## Slide 5: The ARTICo3 Framework
FPGA-Based High-Performance Embedded Computing Platform
Processing
Architecture
Design-Time
Support
Run-Time
Support
https://github.com/des-cei/artico3

## Slide 6: ARTICo3 Architecture
Hardware Acceleration
Hierarchical Memory Model
Global Memory
Bus-Based DMA-Enabled Communication
Embedded Monitoring Infrastructure
Power Monitor
Configurable Datapath

## Slide 7: ARTICo3: Configurable Datapath
Configurable voter unit
  Bypass (Simplex)
  Comparator (DMR)
  Majority voter (TMR)
Reduction engine
  ADD, MAX, MIN
AXI-P2P bridge

## Slide 8: ARTICo3: Operation Modes
Parallel
  kernel instances
  Send: DMA transfer with data
  Receive: DMA transfer with data
Redundant
  kernel instances
  Send: DMA transfer with data
  Receive: DMA transfer with data
Reduction-oriented
  kernel instances
  Send: DMA transfer with data
  Receive: 1 datum (AXI4-Lite control bus)

## Slide 9: ARTICo3: Accelerator Virtualization
Memory-mapped virtualization
  Virtual address subranges for each kernel ID
  Isolation between kernel functionality and FPGA location
  Multicast commands in control bus
    Write operations: kernel reset
    Read operations: reduction operation code

## Slide 10: ARTICo3: Hardware Generation
entity <kernel_name> is
port (
-- Port list
);
end <kernel_name>;
A3_KERNEL(a3reg_t <reg_i>, (...),
a3const_t <mem_j>, (...),
a3in_t <mem_k>, (...),
a3inout_t <mem_l>, (...),
a3out_t <mem_m>, (...)) {
a3reg_init(<reg_i>);
(...)
}

## Slide 11: ARTICo3 Toolchain (Hardware + Software Generation)

## Slide 12: ARTICo3 Runtime and C API
1 Acc.
1 Acc.
2 Accs.
1 Acc.
2 Accs.
4 Accs.
Type | Function
System | artico3_init
 | artico3_exit
Slot | artico3_load
 | artico3_unload
Memory | artico3_alloc
 | artico3_free
Kernel | artico3_kernel_create
 | artico3_kernel_release
 | artico3_kernel_execute
 | artico3_kernel_wait
 | artico3_kernel_reset
 | artico3_kernel_wcfg
 | artico3_kernel_rcfg
Monitor | artico3_hw_get_pmc_<type>
Helper | ftoa3
 | a3tof
Full Reconf.
DPR
Accelerator Management

## Slide 13: Run-Time Solution Space Exploration with ARTICo3
XC7K325T-2FFG900C FPGA @ 100 MHz
Accelerators | Iterations | Theor. Throughput Msamples/s | Actual Throughput Msamples/s | Energy Efficiency mW/(Msamples/s)
1 | 4096 | 7.72 | 6.92 | 378.18
2 | 2048 | 15.45 | 13.28 | 197.1
4 | 1024 | 30.9 | 24.52 | 106.73
8 | 512 | 61.81 | 42.48 | 61.61
16 | 256 | 123.62 | 67.04 | 39.1
ARTICo3-enabled CCSDS 123 compressor (HyLoC)
Input Image: AVIRIS (calibrated) 512 samples, 512 lines, 224 bands
9.69x
XC7Z100-2FFG900 ARM @666.67 MHz FPGA @ 100 MHz

## Slide 14: Hardening ARTICo3 MPSoCs for Space Applications
H2020-ECSEL-2015-2-IA-two-stage (grant ID 692455)
On-board processor for space applications on reconfigurable, non-rad-hard, SRAM-based COTS FPGA
Single platform that unifies System Under Test (SUT) and Test System (TS)
RTEMS ported to Zynq US+ (locked-step execution on Cortex-R5)

## Slide 15: Hardening ARTICo3 MPSoCs for Space Applications
Passive fault-tolerance techniques
  Modular redundancy in ARTICo3 accelerators
  Locked-step execution on Cortex-R5 processors
Adaptive-rate active fault-tolerance techniques
  [HW] ECC/CRC scrubber (SEMIP)
  [SW] Configuration-aware scrubber
  [SW] Blind scrubber
Performance, error and power consumption monitors (i.e., PMCs)
On-board fault injection support for V&V
Safe, secure and predictable reconfiguration mechanisms (i.e., firewall)

## Slide 16: Going full Open Source
Implementation on reference NOEL-V design on KC705 (Kintex-7) board
Integration of ARTICo3 on NOEL-V subsystem w/ AHB2AXI bridges
Integration of HWICAP on NOEL-V subsystem to support reconfiguration
Integration of scrubber and fault injection mechanisms (SEMIP + SW)
Development of low-level drivers (HWICAP, SEMIP and DMA engine)
HW
HW
HW
HW SW
SW
https://www.gaisler.com/index.php/downloads/leongrlib
Arbitration HW/SW
Migration from ARM Cortex-R5 processors to NOEL-V (RISC-V)

## Slide 17: Experimental Results (I)
ARTICo3 block-based matrix multiplication demo
Reconfiguration time ~250 ms/acc
Limited speedup due to bus bandwidth

## Slide 18: Experimental Results (II)
CCSDS 121 data compression algorithm
Reconfiguration time ~250 ms/acc
8-bit data
16-bit data
Limited speedup due to bus bandwidth

## Slide 19: Experimental Results (III)
Application | #Accs | Abitration (ms) | Repair (ms) | Reset (ms) | Blind scrubber (ms)
Matmul | 1 | 63.88 | 209.42 | 70.56 | 269.34
 | 2 | 62.64 | 218.69 | 77.38 | 539.28
 | 4 | 64.48 | 219.84 | 78.76 | 1097.27
 | 8 | 62.78 | 224.57 | 75.13 | 2199.61
CCSDS 121 | 1 | 62.21 | 214.37 | 76.4 | 229.11
 | 2 | 63.26 | 214.74 | 78.94 | 476.31
 | 3 | 63.29 | 226.36 | 77.53 | 782.42
 | 4 | 64.63 | 232.98 | 77.86 | 1047.70
Fault tolerance metrics for HW- and SW-based scrubbers
Initialization time (reset) in datasheet for ECC repair: 71 ms
Blind scrubbing overheads dependent on the #accelerators

## Slide 20: Conclusions
User-accessible HW-accelerated framework
Transparent FPGA reconfiguration support
Hierarchical mixed HW/SW fault detection, recovery and mitigation
Full open-source computing stack for space applications
  NOEL-V processor
  RTEMS operating system
  ARTICo3 acceleration infrastructure

## Slide 21: Future Activities (and Wishlist)
Finish the migration of the scrubber stack (i.e., reconfiguration-aware)
Evaluation of multi-FPGA setups
  Supervisor device: NOEL-V + RTEMS + SW-based support stack
  High-performance device: DPR-capable computing substrate
Evaluation of alternative acceleration approaches (e.g., ISA extensions)
Migration to space-grade reconfigurable FPGA families (NanoXplore)

## Slide 22: THANK YOU FOR YOUR ATTENTION
alfonso.rodriguezm@upm.es