## Slide 1
EDA Tools for the analysis and mitigation of radiation effects on FPGAs
Eleonora Vacca
Sarah Azimi
Corrado De Sio
Andrea Portaluri
Daniele Rizzieri
Luca Sterpone

## Slide 2: Goal
Enhance state-of-the-art techniques for the reliability analysis and mitigation of radiation effects on FPGAs
Development of Electronic Design Automation (EDA) tool set
  Analysis of SEU / SET effects impact on FPGA circuit reliability
    Capability of evaluating redundancy architecture such as TMR
  Accurate error rate estimation
  Mitigation of SEU / SET effects at the FPGA place and route level
  Compatibility with commercial tools
    AMD Xilinx
    Microchip
    NanoXplore

## Slide 3: Back-end EDA tools
Physical Design Description (PDD) converters
  A set of netlist conversion tool for FPGA logic and routing resources generation, storage and management
PDD Place
  A resource balanced and timing-driven placement software tool for any FPGA architecture
PDD Routing
  A FPGA-oriented routing algorithm for any FPGA architecture
PyXEL
  An integrated environment for the correlation of PDD and FPGA configuration memory

## Slide 4: Back-end tool flow
Synthesis
Mapping
Place and Route
Bitstream Generation
PDD Convs
PDD Place
Design Entry
Bitstream
Netlist
Architecture & Bitstream Structure
PDD format
Resource Bitmap
PyXEL
PDD Annotated
PDD Routing
PDD Convs
PDD
File
Standard
Implementation Flow
Back-end tool set
Exchange Files for
Front-end tools
Island or Channel Style
FPGA
Logic And Routing
Area
I/O
Pins
Block RAM and DSPs
Embedded Cores
Configurable Parameters

## Slide 5: Back-end tool flow
Synthesis
Mapping
Place and Route
Bitstream Generation
PDD Convs
PDD Place
Design Entry
Bitstream
Netlist
Architecture & Bitstream Structure
PDD format
Resource Bitmap
PyXEL
PDD Annotated
PDD Routing
PDD Convs
PDD
File
Standard
Implementation Flow
Back-end tool set
Exchange Files for
Front-end tools
Island or Channel Style
FPGA
Logic And Routing
Area
I/O
Pins
Block RAM and DSPs
Embedded Cores
Configurable Parameters

## Slide 6: Physical Design Description
The PDD is a graph description of the FPGA mapped circuit
The model is characterized by
  Nodes: mimic resources such a LUTs, hardwired cores, BRAMs, …
  Edges: mimic routing resources such as drivers, PIPs, segments, …
The annotated PDD includes delay and configuration data
49
clock/redundant_clock_toggling
C NOR2B
75
N_49_i
C INV
85
Clock_pad/U0/U0
C IOPAD_TRI
…
…
…

## Slide 7: Back-end tool flow
Synthesis
Mapping
Place and Route
Bitstream Generation
PDD Convs
PDD Place
Design Entry
Bitstream
Netlist
Architecture & Bitstream Structure
PDD format
Resource Bitmap
PyXEL
PDD Annotated
PDD Routing
PDD Convs
PDD
File
Standard
Implementation Flow
Back-end tool set
Exchange Files for
Front-end tools
Island or Channel Style
FPGA
Logic And Routing
Area
I/O
Pins
Block RAM and DSPs
Embedded Cores
Configurable Parameters

## Slide 8: PDD Converters
The netlist converter tools are a fundamental part of the framework since they guarantee the compatibility of the model with existing FPGAs
Python Extract DB to PDD
AMD Xilinx Vivado
SDC, PIP and Bitlevel constraints
Microchip
Flattened Netlist to PDD
PDC Constraints
NanoXplore
Driver HDL to PDD
Cluster Constraints

## Slide 9: Back-end tool flow
Synthesis
Mapping
Place and Route
Bitstream Generation
PDD Convs
PDD Place
Design Entry
Bitstream
Netlist
Architecture & Bitstream Structure
PDD format
Resource Bitmap
PyXEL
PDD Annotated
PDD Routing
PDD Convs
PDD
File
Standard
Implementation Flow
Back-end tool set
Exchange Files for
Front-end tools
Island or Channel Style
FPGA
Logic And Routing
Area
I/O
Pins
Block RAM and DSPs
Embedded Cores
Configurable Parameters

## Slide 10
Bitstream formats are proprietary and FPGAs vendors do not disclose information about them
Electrical and logical behaviours of routing segments are not known and are architecture dependant
The mapping between bitstream bits and FPGA resources is a hard topic

## Slide 11
PyXEL generates bitmaps to relate resources and bitstream bits
Bitmaps are binary files that are used to enable or disable resources

## Slide 12
Extract Device Information
Create Tile-Encoding pairs
Understand
Implemented designs
Bitstream Structure
Device Architecture
Tiles Architecture
(Bitmap, Tile configuration) Pairs
- pip_x, pip_y, pip_z…
- pip_a, pip_b, pip_x, pip_y…
Bit Resource
Configuration
Bits DB
Bit/Resources Correlation
Active High/Active Low filtering
Fake PIP filtering
…
Configuration Bits DB

## Slide 13
Bitstream Parsing, Manipulation, Visualization
Tiles-to-bits mapper
Supported Devices: Series7, US, US+ Families
  Case of Study: Z7000 - KU040 - KU060 – ZU1CG
Bitstream Analysis and Visualization

## Slide 14: Configuration Memory Models
FPGA
Architecture
PyXEL
Bitmap

## Slide 15: Back-end tool flow
Synthesis
Mapping
Place and Route
Bitstream Generation
PDD Convs
PDD Place
Design Entry
Bitstream
Netlist
Architecture & Bitstream Structure
PDD format
Resource Bitmap
PyXEL
PDD Annotated
PDD Routing
PDD Convs
PDD
File
Standard
Implementation Flow
Back-end tool set
Exchange Files for
Front-end tools
Island or Channel Style
FPGA
Logic And Routing
Area
I/O
Pins
Block RAM and DSPs
Embedded Cores
Configurable Parameters

## Slide 16: Front-end - EDA tools
VERI-Place (aka VERI-Py)
  VERIfication and Placement tool for the analysis and mitigation of SEU effects in FPGA configuration
  Reliability calculation
SETA (aka PySETA)
  Single Event Transient Analysis tool for the analysis of SET effects including Propagation Induced Pulse Broadening (PIPB) effect
PySELFI
  SELective Filtering of SET for any FPGA architecture
  Fundaments of the tools are included in ECSS-Q-HB-60-02A – Techniques for radiation effects mitigation in ASICs and FPGAs handbook

## Slide 17: SEUs on SRAM-based FPGAs - Background
SEUs may cause structural changes in the circuit implemented on the FPGA
TMR techniques suffer cross-domain failure induced by single and multiple bitflips within the configuration memory

## Slide 18: VERI-Py: A Reliability Prediction Tool
Synthesis
Mapping
Place and Route
Bitstream Generation
Net2VCRAM
Bitflip CRAM
Design Entry
Bitstream
Netlist
XC7Z020 Bitstream
AMD Xilinx Implementation Flow
1
3
Virtual CRAM
PDD_arch
CRAM2PDD
2
MBU_arch
Propagation
Classification
4
Reliability Plot
Configuration coding
Architectural map
SEU insertion, propagation and classification
Cumulative effect and reliability results

## Slide 19: VERI-Py: A Reliability Prediction Tool
Real
Bitstream
Configuration
Bitstream
MonteCarlo
Single Modification
On Configuration
Conf0
SEU1
Conf0
SEU2
Confi
SEUj
PDD
Configuration i
Extraction of
Architectural map j
Architectural Mapj
Configuration SEUj j = 12030
“pip INT_L_X42Y57 SL1END1 -> ER1BEG2;”
Propagation
Architectural Mapj
Net 1 “….sub_alu_k/result_o[17];”
Net 2 “….channel_0/ar_cmd_fsm_0_n_26;”
Bitstream
DB
net “….sub_alu_k/result_o[17] ;”

## Slide 20: VERI-Py Main Achievement
Accurate identification of TMR single point of failures
0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
M0
M1
M2
VOTER

## Slide 21: PySETA
Single Event Transient Analysis of circuit sensitive nodes
G1
G2
G3
G4
FFA
FFB
Physical Design Description
(PDD)
Terminal nodes are the destination points of SET propagation
Injection [#] | Source SET [ns] | SET reach to FF [ns]
(1) | 0.35 | 0.40
(2) | 0.35 | 0.42
(3) | 0.35 | 0.30
… | … | …

## Slide 22: PySELFI
FFB
FFA
G1
G2
G3
G4
G5
Selective Filtering logic structure insertion at the netlist level

## Slide 23: PySELFI
Selective Filtering logic structure insertion at the netlist level
FFB
FFA
G1
G2
G3
G4
G5

## Slide 24: PySELFI
Calculation of SET filtering delay with respect to max SET pulse reported by PySETA
PySETA is compatible with ProASIC3, SmartFusion-II, PolarFire and RTG4
Filtering insertion is at Verilog level or integrated in FPGA tools
FFB
FFA
G1
G2
G3
G4
G5

## Slide 25: Experimental Results
TMR design | LUT [#] | PIP [#]
(a) Original | 11,572 | 13,590
(b) Isolated Domains | 11,578 | 14,642
(c) Resource Sharing | 11,572 | 24,948
AMD-Xilinx Zynq XC7Z020 28nm CMOS SRAM-based FPGAs
The developed tool has been applied to a TMR benchmark
Three different alternative layouts

## Slide 26: The Placement Tool – Design Interface
Redundant modules are automatically recognized and reorganized in the FPGA area
  Adopting a per-domain isolation policy, not requiring user intervention
The customization of other modules is left to the preference of the user
  User will indicate the name of the module, choosing from a list, and coordinates (xmin, xmax, ymin, ymax) of the new region of the device in which to confine it
Provides a preview of the placement solution realized

## Slide 27: Routing Tool
Customized SEU-aware Routing Path
Original Vivado Routing Path

## Slide 28: Experimental results
Energies ranging from 50.80 MeV up to 150 MeV
Average flux 4.134 107 proton.cm-2s-1
Default
TMR isolated
Resource Sharing

## Slide 29: Predicted vs Measured Reliability
Radiation Test Mitigatef TMR
Radiation Test Default TMR
Radiation Test Resource sharing TMR
Predicted Mitigated TMR
Predicted Default TMR
Predicted Resource sharing TMR

## Slide 30: Experimental Analysis on AI
Network architecture: AlexNet CNN and Torchvision
Multichannel Convolutional Layer
Compared with 10,000 SEU injection of VERI-Py bitstream coordinates

## Slide 31: SET analysis and mitigation
Analysis and mitigation of ZFNet CNN on RT4G150 Microchip Rad-Hard Flash-based FPGA
Resource | Available | Utilization | 
 |  | [#] | [%]
4LUT | 151,824 | 120,904 | 85.9
DFF | 151,824 | 123,084 | 81.1
Math 18x18 | 462 | 382 | 82.7
LSRAM 18K | 209 | 202 | 96.7

## Slide 32: SET analysis and mitigation
Application of PySELFI versus Commercial Solution and Filtering at 600ps

## Slide 33: Conclusions
EDA tools are compatible with state-of-the-art FPGA used in space domain
  A viable solution for implementing resilient FPGA circuits for space
Reliability evaluation includes a wide spectra of hardware faults

## Slide 34: Future works
Propose a comprehensive analysis involving more complex hardware cores such as AI accelerators
  layers, network architectures and fault models would be extended
Reliability comparison of different hardware (e.g., HW accelerators on FPGAs) exploiting the developed platform
Continue to expand our approach with the results from emulation-based fault injection and radiation tests

## Slide 35: Thank you
luca.sterpone@polito.it

## Slide 36: Routing Switch architectural model
The model is based on the routing organization of AMD-Xilinx SRAM-based FPGAs
  Connection clusters towards nearby resources
  2 - short lines
  4 - longitudinal and diagonal lines
  6 - long lines
  12 - hex lines

## Slide 37: Reliability Prediction Tool
Monte Carlo analysis with a limit up to 100,000 iterations per SEU combination
Bit Classification criterias
  Accumulated: bitflips accumulated in the virtual configuration memory
  Miss: number of upsets that did not hit any programmed resources
  Error: bitflips causing an error propagated to the output
  Filtered: bitflips that, even if there are related to a used resource, they did not propagate the error until an output cell