## Slide 1: SpaceFibre and SpaceWire IP Cores for the Next Generation of Radiation-Tolerant FPGAs Marti Farras Casas, Alberto Gonzalez Villafranca, Albert Ferrer Florit – STAR-Barcelona Chris McClements, Andrew MacLennan, Steve Parkes – STAR-Dundee www.star-dundee.com @STAR_Dundee
20 Years of Spacecraft Networking Innovation

## Slide 2: Contents
SpaceWire and SpaceFibre technology
  SpaceFibre
  STAR-Dundee test equipment and STAR-System
SpaceFibre IP cores on current and next generation FPGAs
The STAR-Tiger SpaceFibre Routing Switch

## Slide 3: SpaceWire Technology and IP cores
Spacecraft onboard data-handling network technology
Connects together instruments, data compressor, data processors, data storage, downlink transmitter and control computer on-board a spacecraft
  Low to medium bit rates up to 400 Mbit/s, typical 200 Mbit/s maximum
SpaceWire standard
  Written by Steve Parkes, STAR-Dundee’s Chief Technical Office
  With inputs from international spacecraft engineers
  Recently updated to Rev.1
SpaceWire technology
  Being used or designed into well over 100 spacecraft
STAR-Dundee SpaceWire IP cores used extensively in USA, Europe, Japan
  Available for NanoXplore, Xilinx and Microchip FPGAs
  SpaceWire Interface, Routing switch, RMAP protocol handling, DMA, AXI slave bridge
  Updated for ECSS-E-ST-50-12C Rev.1

## Slide 4: SpaceWire Technology and IP cores
NG-Medium Test
PolarFire test
RTG4 test
Kintex Ultrascale Test
Zynq (including PS PL bridge)

## Slide 5
Very high performance
  6.25 Gbit/s per lane and higher depending on SerDes
Multi-lane capability
  Increases link bandwidth - Quad lane link at 6.25 Gbit/s per lane gives 25 Gbit/s
  Arbitrary number of lanes with graceful degradation when a lane fails
In-built Quality of Service
  Bandwidth reservation, priority and scheduling
Fault detection, isolation and recovery capabilities
  At the link level enabling rapid error recovery (a few microseconds)
  Provides data integrity and reliable data delivery
SpaceFibre for payload data-handling

## Slide 6: SpaceFibre for payload data-handling
Low-latency broadcast messages
  For time distribution, synchronisation, event signalling, error notification, etc.
Runs over electrical or optical cables
  Few metres electrical, 100 metre Fibre optic
Small implementation footprint
  Taking a few percent of a recent radiation tolerant FPGA
Added as both data & control planes in SpaceVPX Vita 78 recently released

## Slide 7: STAR-System and Test Devices
STAR-System is the software stack used for all STAR-Dundee’s test and development equipment
  Software suite:
    Device drivers, GUI applications, C, C++, APIs
    Version 5.00 introduced a Python API and RMAP Initiator Application
  Packet Libraries:
    RMAP, CCSDS Space Packet Protocol, CCSDS Transfer Frames
Test equipment for both SpaceWire and SpaceFibre EGSE
Brick Mk4 (USB to SpaceWire)
PCIe Mk2
(PCIe Gen3 x1 to SpaceWire)
STAR-Ultra PCIe
(PCI Gen3 x8 to SpaceFibre)

## Slide 8: New Generation FPGAs for Space
NanoXplore BRAVE family (NG-Large / NG-Ultra)
  65 / 28 nm FD-SOI
  SRAM-based – Volatile
  Radiation-hardened by design
  4x SerDes @ 6 Gbit/s / 32x SerDes @ 12.5 Gbit/s
Microchip RTG4
  65 nm
  Flash-based – Non-volatile
  Radiation-hardened by design
  24x SerDes @ 3.125 Gbit/s
Xilinx Kintex UltraScale
  20 nm
  SRAM-based – Volatile
  Radiation-tolerant
  32x SerDes @ 12.5 Gbit/s
Microchip PolarFire
  28 nm
  SONOS-based – Non-volatile
  Radiation-tolerant
  24x SerDes @ 10 Gbit/s
Xilinx Versal
  7 nm FinFET
  SRAM-based – Volatile
  Radiation-tolerant
  44x SerDes @ 25 Gbit/s

## Slide 9: SpaceFibre IP Core
SERDES
SERDES
SpaceFibre Interface
IP Core
Broadcast
APB / AXI4-Lite Signals
SERDES
Serial Data
8B/10B Encoding
8B/10B Decoding
Optional
Virtual Channel AXI4-Stream
Management
APB / AXI4-Lite Signals
User Interfaces
HSSL Interface
Use of an APB / AXI4-Lite with registers
Number of virtual channels
Type of SerDes interface:
RTG4, PolarFire, Xilinx, BRAVE, TLK2711, Parallel
Depth of internal buffering
Technology independent RTL with optimisations for specific FPGAs
Independent clock for each AXI interface
Number of lanes, Tx/Rx unidirectional lanes,
hot/warm redundancy
Lane 3
Lane 4
Lane 3
Lane 4
Unidirectional lane
Inactive unidirectional lane
Lane 1
Lane 2
Lane 1
Lane 2
Bidirectional lane
Unidirectional lane

## Slide 10: SpaceFibre IP Cores General Features
Use of EDAC protection in memories
Guaranteed, straightforward timing closure
  Lane rate only limited by Serdes (e.g. up to 3.125 Gbps on RTG4)
  For the whole temperature and voltage range (i.e. fast & slow corners)
  With EDAC and SET filters
  Does not require specific placement or timing constraints.
  Even with more than 80% FPGA utilisation
    Low latency
      Less than 400 ns for Broadcasts (including 250 ns due to SerDes latency)
      Streaming frame sending option
Compact design

## Slide 11: SpaceFibre IP Core General Features
Configurable
  Number of lanes, virtual channels, ports
High performance
      Optimised for radiation hardened FPGAs
Easy to use
  AXI4-Stream interface for each Virtual Channel
  Reference designs for RTG4, PolarFire, KUS, Versal, BRAVE...
Safe
  Extensive verification and validation
  Tested in radiation environment

## Slide 12: SpaceFibre Single-Lane Interface IP Resources
 | RTG4 |  |  | XQRKU060 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
1 VC | 2.2% | 1.6% | 1.9% | 0.5% | 0.4% | 0.4%
2 VCs | 2.6% | 1.9% | 2.9% | 0.7% | 0.4% | 0.6%
4 VCs | 3.5% | 2.7% | 4.8% | 0.9% | 0.6% | 0.9%
 | RTPF500T * |  |  | XQRVC1902 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
1 VC | 0.6% | 0.5% | 0.5% | 0.2% | 0.1% | 0.2%
2 VCs | 0.7% | 0.6% | 0.8% | 0.2% | 0.2% | 0.3%
4 VCs | 1.0% | 0.8% | 1.3% | 0.3% | 0.2% | 0.5%
RTG4 and
Kintex Ultrascale
PolarFire and
Versal

## Slide 13: SpaceFibre Single-Lane Interface IP Resources
TMR in PolarFire
  DFF ~ x 2.8
  LUT ~ x 2
RTPF500T
XQRVC1902

## Slide 14: SpaceFibre Single-Lane Interface IP Resources
NG family share the same type of fabric resources
  IP implementation expected to use the same resources in NG-Large and NG-Ultra
In terms of % of resource usage for the SpFi IP Core
  NG-Large is equivalent to the RTG4
  NG-Ultra is equivalent to the PolarFire
 | NG-Large |  |  | NG-Ultra |  | 
 | LUT | DFF | RAM | LUT | DFF | RAM
1 VC | 2.0% | 1.9% | 4.2% | 0.5% | 0.5% | 1.2%
2 VCs | 2.4% | 2.4% | 6.3% | 0.6% | 0.6% | 1.8%
4 VCs | 3.2% | 3.3% | 10.4% | 0.8% | 0.8% | 3.0%

## Slide 15: SpaceFibre Multi-Lane Interface IP Core
Multi-Lane is an optional capability of the SpFi standard
Allows several physical lanes to behave as a single logical link
  Higher throughput
  Redundancy
    Hot (< 3 µs) & Warm (< 80 µs)
Lanes can be operated independently
  Any number of lanes supported
  Unidirectional lanes supported

## Slide 16: SpaceFibre Multi-Lane Interface IP Resources
Values for different configurations available at https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/89Gonzalez.pdf
RTPF500T
XQRVC1902

## Slide 17: SpaceFibre IP on NanoXplore FPGA
Successful link connection established with STAR-Fire unit
  2 Gbps setup
  Correct data transmission without any data errors
Retry events periodically appear
Currently debugging this problem in collaboration with NanoXplore
  The final validation of the IP to be completed soon
  Reference design with SerDes configuration, clock scheme details, memory instantiation (EDAC), etc. provided with IP
STAR Fire
eSATA
FMC Mk3
SpW/SpFi
NG-Large
Evaluation
Kit
FMC
NanoXplore NG-Large Evaluation Kit

## Slide 18: Demonstration - SpaceFibre Multi-lane Interface IP Implementation
SpaceFibre Multi-lane on
RTG4
Test Equipment
STAR Fire
SpaceFibre Multi-lane on
Kintex Ultrascale

## Slide 19: Demonstration - SpaceFibre Multi-Lane Interface IP Implementation
Microchip PolarFire MPF300 development kit
3.125 Gbit/s demonstration
Xilinx Versal VCK190
6.25 Gbit/s demonstration
FMC SpW/SpFi
eSATA to SFP
STAR-Ultra
MPF300
QSFP to SFP
QSFP to SFP
FMC
to
QSFP
VCK190

## Slide 20: SpaceFibre Routing Switch IP Core
Full non-blocking switch matrix
Deterministic low-latency switching
Supports path, logical addressing and group adaptive routing
Fully configurable
  Port types
    SpaceFibre  Number of lanes, VCs
    AXI4-Stream Internal  Number of VCs
    SpaceWire
  Target technology

## Slide 21: SpaceFibre Routing Switch IP Core
Supports virtual networks that can be static or dynamically configured
  Up to 64 virtual networks
Configuration port with RMAP protocol
Isolates each virtual network using priority, scheduling and bandwidth reservation QoS
Within the same virtual network:
  Packet by packet round robin arbitration for packets going to the same output port
  Automatic packet spill on timeout
  Additional timeout timers to detect a babling node

## Slide 22: SpaceFibre Routing Switch IP Core

## Slide 23: SpaceFibre Single-Lane Routing Switch IP Resources
SpFi Interface IP Cores are included
  Additional Configuration port and RMAP target is also included
  Port count includes 1x internal AXI4-Stream (2 VCs) and 1x SpW ports
 | RTG4 |  |  | XQRKU060 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
6 Port 2 VCs | 20.9% | 18.0% | 22.5% | 5.4% | 4.2% | 4.4%
10 Port 4 VCs | 64.9% | 50.1% | 60.8% | 16.9% | 11.8% | 11.9%
 | RTPF500T * |  |  | XQRVC1902 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
6 Port 2 VCs | 6.2% | 5.6% | 6.1% | 1.9% | 1.5% | 5.0%
10 Port 4 VCs | 19.4% | 15.8% | 16.6% | 6.0% | 4.2% | 13.2%
RTG4 and
Kintex Ultrascale
PolarFire and
Versal

## Slide 24: SpaceFibre Multi-Lane Routing Switch IP Resources
SpFi Multi-lane Interface IP Cores are included
  Additional Configuration port and RMAP target is also included
  Port count includes 1x internal AXI4-Stream (2 VCs) and 1x SpW ports
 | RTG4 |  |  | XQRKU060 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
2 Lane 6 Port 2 VCs | 31.6% | 29.3% | 28.2% | 8.6% | 6.5% | 3.1%
2 Lane 10 Port 4 VCs | 92% | 76.7% | 81.2% | 24.9% | 16.5% | 9.4%
4 Lane 6 Port 2 VCs | 50.9% | 45.6% | 56.0% | 14.1% | 9.9% | 5.7%
4 Lane 10 Port 4 VCs |  |  |  | 38.8% | 23.9% | 17.2%
2 Lanes
4 Lanes

## Slide 25: SpaceFibre Multi-Lane Routing Switch IP Resources
PolarFire and Versal FPGA utilisation
 | RTPF500T |  |  | XQRVC1902 * |  | 
 | LUT | DFF | LSRAM | LUT | DFF | RAMB36
2 Lane 6 Port 2 VCs | 9.8% | 9.3% | 4.4% | 2.9% | 2.4% | 3.5%
2 Lane 10 Port 4 VCs | 28.2% | 24.4% | 13.4% | 6.8% | 6.1% | 10.5%
4 Lane 6 Port 2 VCs | 15.8% | 14.5% | 8.1% | 4.8% | 3.6% | 6.4%
4 Lane 10 Port 4 VCs | 44.2% | 36.2% | 24.4% | 13.4% | 8.8% | 19.2%
2 Lanes
4 Lanes

## Slide 26: STAR-Tiger SpaceFibre Routing Switch
Primary element of the payload data-handling network for the Hi-SIDE project
  10 port multi-lane SpaceFibre Routing Switch
Spaceflight TRL5 level design
  Radiation tolerant EM flight parts or industrial/commercial equivalents
Power consumption: 14.2W
  Typical at 20 °C, all links running with lanes speeds of 6.25 Gbit/s
Conduction cooled
  -25°C to +55 °C
Size: 108 x 108 x 68mm
Mass: 1.32 kg
European Space Forum Innovation in Space Award won by Hi-SIDE Team: https://www.hi-side.space/

## Slide 27: STAR-Tiger SpaceFibre Routing Switch
Power supply board
  Texas Instruments radiation tolerant components are used
  Primary and redundant power supplies
FPGA board
  KU060 industrial grade FPGA
  The FPGA is surrounded by six Elara connectors
  Each connector provides four lanes of SpaceFibre
Configuration board
  FPGA and flash programming
  FPGA scrubbing routines
Configuration Board
FPGA Board
TI Power
Supply Board

## Slide 28: STAR-Tiger SpaceFibre Routing Switch
Aggregate throughput 200 Gbit/s
  10 SpaceFibre ports
  Two quad-lane ports
  Eight dual-lane ports
  Lane speeds up to 6.25 Gbit/s
Port data rate
  9.6 Gbit/s dual-lane port
  19.2 Gbit/s quad-lane port
2 SpaceWire interfaces
  Flash memory or FPGA can be programmed over SpaceWire

## Slide 29: Hi-SIDE Demonstration System Block Diagram

## Slide 30: Summary
STAR-Dundee provides both SpaceWire and SpaceFibre IP cores
  SpaceWire Interface and Routing Switch IP cores
  SpaceFibre Interface and Routing Switch IP cores
  Supporting IP cores
    RMAP Initiator and Target IP cores
    DMA and AXI bridge
The IPs have been designed specifically for space applications
  Designed for the highest performance in RTG4 and other rad-had FPGAs
  Exhaustive verification and validation, including radiation testing
IP Core can be used without knowledge of the internals of the SpaceFibre protocol
Reference designs available that show how to interconnect to different SerDes/Transceivers

## Slide 31: Demonstration and References
Demonstration setup
  PolarFire MPF300T and Versal VCK190 – SpaceFibre Multi-lane
  STAR-Ultra PCIe
Reference Material
  A. Gonzalez Villafranca, et. al., “SpaceFibre IP Cores for the Next Generation of Radiation-Tolerant FPGAs”, ISC 2022
    https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/89Gonzalez.pdf
  A. Ferrer Florit et. al., “SpaceFibre Multi-Lane Routing Switch IP”, ISC 2022
    https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/88Ferrer.pdf
  A. Gonzalez Villafranca, et. al., “Mitigation and Recovery of Single Event Effects in RTG4 FPGA Transceiver Links Using SpaceFibre”, RADECS 2022
    https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/2022_RADECS_RTG4_Rad_Test-ver_2.pdf
  S. Parkes , et. al., “SpaceFibre Payload Data-Handling Network”, ISC 2022
    https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/87-Parkes.pdf
  D Gibson, et. al., “Hi-SIDE: Monitoring, Control and Test Software in a SpaceFibre Network”, ISC 2022
    https://www.star-dundee.com/wp-content/star_uploads/conference_papers/spacefibre/78Gibson.pdf