## Slide 1
CNES Activities on NanoXplore Chips
SEFUW Presentation
14/03/2023
_
DTN/TVO/ET

## Slide 2: Contents
SEFUW: CNES activites on Nx chips
FPGA IPs
  DDR2
  ESIStream
  RISC-V
Designs
  R5 Reference design
  PhotoBooth
  Cipher Design
COMODO Boards

## Slide 3
IPs : DDR2, ESIStream, Risc-V

## Slide 4: IP DDR2
DDR2 developed by LGMi for NG-MEDIUM through R&T
Tested on evalkit NX1H35-EK with DDR2 module memory
NG-LARGE is ongoing (end foreseen mid 2023)
Two interfaces:
  user interface (UI)
  AXI
SEFUW: CNES activites on Nx chips

## Slide 5: IP DDR2
SEFUW: CNES activites on Nx chips
DDR2- NG-MEDIUM UI mode
DDR2- NG-MEDIUM AXI mode

## Slide 6: IP DDR2 : next steps
SEFUW: CNES activites on Nx chips
4 bugs have been corrected on NG-MEDIUM, see Gitlab figure:
Currently 4 bugs on NG-LARGE development, see Gitlab figure:

## Slide 7: ESISTREAM : Protocol Brief
ESIStream stand for Efficient Serial Interface Stream.
14B/16B encoding.
Open source and license-free. (https://www.esistream.com/protocol)
Clock recovered from the data.
High speed serial interface.
Can be used with any system requiring a serial interface
Already well implemented on Xilinx chips
SEFUW: CNES activites on Nx chips

## Slide 8: ESISTREAM On Nx Chips
HSSL Lanes have part of ESIStream protocol (coder and decoder) in silicium
Tx Lane encoder:
  LFSR generator.
  Scrambler + Clock bit generator.
  ESIStream Synchronization Sequence generator.
  Disparity bit module.
Rx Lane decoder:
  Frame alignement module.
  LFSR module.
  Decoder module (descrambler and disparity).
  Output buffer.
SEFUW: CNES activites on Nx chips

## Slide 9: ESISTREAM : R&T Steps
R&T developed by NanoXplore
Support of Teledyne E2V
Protocol RTL Simulation
NG-ULTRA
OnBoard Loopback
NG-LARGE
DAC DD700
NG-ULTRA
ADC AQ600
Ongoing:
RTL Simulation of ESIStream
sources
Step 2:
NG-ULTRA DevKit + HSSL FMC Board
Step 3:
COMODO-L
(see next slides)
+ FMC board DD700
Step 4:
COMODO-U
(see next slides)
+ FMC board AQ600
SEFUW: CNES activites on Nx chips

## Slide 10: Soft Core RISC-V
all-in-one package: CPU + SoC + Software Framework & Tooling
completely described in behavioral, platform-independent VHDL - no platform-specific primitives, macros, attributes, etc.
Open source and license-free. (https://github.com/stnolting/neorv32)
Continuous integration thanks to Linty services
SEFUW: CNES activites on Nx chips

## Slide 11: Neorv32 performances (V1.5.7 – june 2021)
SEFUW: CNES activites on Nx chips
Rv32iv0 minimale
Rv32imcv1 intermédiaire
Rv32imcv0 performance

## Slide 12
R5 reference design on NG-LARGE

## Slide 13: Project General description (architecture)
Implemented on NgLarge evalboard
SEFUW: CNES activites on Nx chips
Notes: Generic SOC design with axi bridge and peripheral
It is not a huge design 8% of the FPGA . Expected performances are downgraded (we want to assess the design flow and the result on board) see next slide

## Slide 14: R5 Reference Design and XNG implementation
SEFUW: CNES activites on Nx chips
R5 Reference design will be implemented on COMODO-L (see next slides)
XNG has been implemented on NG-LARGE R5 processor thanks to the R5 Reference design
  Currently working with BRAM memories (for software)
Qualification is ongoing, waiting for DDR2 memory
  The design has been adapted for XNG : Specific timer with software breakpoint management, DDR controller…
XNG on NG-ULTRA (R52) is ongoing (H2020 HERMES contract)
LVCUGEN (generic flight software using XNG) development on NG-ULTRA will start soon

## Slide 15
PHOTOBOOTH DESIGN

## Slide 16: PHOTOBOOTH : General Description
How to show CASPEX and NanoXplore technology to everyone?
SEFUW: CNES activites on Nx chips

## Slide 17: PHOTOBOOTH : FPGA Design
IP SPW : OpenCore  switch to NX SPW Codec
IP COMBLOCK 5401 and 5402 from AXI4Stream to GMII/RGMII Interface
Global Photobooth entity to manage each block  could be a Risc-V core, R5
SEFUW: CNES activites on Nx chips

## Slide 18
CIPHER DESIGN

## Slide 19: Cipher Design : Context
SEFUW: CNES activites on Nx chips

## Slide 20: IP Architecture
SEFUW: CNES activites on Nx chips

## Slide 21: IP Features
AXI4-Stream Interface for key input for 128 and 256 bits key length
Internal Key Expansion processing
AXI4-Stream Interface for IV inputIV input of 96 bits length
AXI4-Stream Interface for Data input (AAD and PlainText)
Supports only GMAC messages or GMAC and PlainText or only PlainTextSupports data input of 8bits granularitySupports AAD data masking for tag computation
AXI4-Stream Interface for Data output (AAD, CipherText and Tag)
Simple, fully synchronous and reusable design in all architectures (no target dependency)
Implemented according to the National Institute of Standards and Technology (NIST) Special Publication 800-38D
Fully validated with NIST CAVP "Cryptographic Algorithm Validation Program" tests vectors
Data Rate 55 Mbps with a 100MHz clock. (~Freq/2 bps)
AES-GCM 256b mode with Key expansion:
SEFUW: CNES activites on Nx chips
IP Resources
CHIP | LUT | FF | BRAM
ZYNQ7x | 1250 | 2500 | 1.5
NG-LARGE | 2400 | 2540 | 6

## Slide 22: IP Validation on DevKit NG-LARGE & Briquette (Zynq US+)
SEFUW: CNES activites on Nx chips

## Slide 23: Validation : coverage and NIST Test Vectors
Coverage : 9 scenariis
SEFUW: CNES activites on Nx chips

## Slide 24
COMODO BOARDS

## Slide 25: COMODO
SEFUW: CNES activites on Nx chips
COMODO-L
EM (Available)
COMODO-L
Flight (End of 2023
R&T developed by STEEL Electronique
COMODO Versal is also ongoing
COMODO-U
Fabrication ongoing
COMODO-U
First tests

## Slide 26
THANK YOU ! QUESTIONS?