## Slide 1: An Exploration of Metrics for Orbital Capacity Modeling Darren McKnight, Erin Dale, Mohin Patel, and Chris Kunstadter Space capacity allocation for the sustainability of space activities workshop, Milan, June 2023

## Slide 2: Modeling Orbital Capacity
3 different models, 3 different metrics
Models span reductive to reflective
  Focusing on the now – that is hard enough!
All highlight the deleterious effects of massive derelicts, the importance of persistence, and the criticality of responsible constellation operators
Concept of an orbit being “full” is controversial and fraught with cognitive danger
  Often does not consider benefit of enhanced conjunction assessment services
Model | Aggregate Derelict Collision Risk | Aggregate Operational Payload Collision Risk | Orbital Lifetime
Risk Mapping |  |  | 
Simple Regulatory |  |  | 
Collision Risk Balance: Posed, Abated, and Persistence |  |  | 

## Slide 3: Empirical Risk Mapping
Risk = probability of collision (PC) x consequence
  Uses LeoLabs “representative” conjunction data messages (CDMs) from 1 Jan 2022 to 15 May 2023
    One high-PC conjunction per minute on average
  Distinguishes Space Debris Management from Space Traffic Management
Visualizes stochastic encounter variability in “bad neighborhoods” and the increase where large constellations reside
Aggregating historical risk
Constellation Data Disclaimer!

## Slide 4: Simple Regulatory Models
Suggested to FCC as first part of a challenge to simplify mitigation metrics
  First model (i.e., object-years) based only on number of derelict objects times orbital lifetime
Metric and threshold are both important
  Object-years threshold of 100 object-years was provided only as an example to show the math…
  FCC imposed on Starlink Gen2
Introducing Object-Years and Object-Metric Ton-Years

## Slide 5: Simple Regulatory Models
Mass is critically important
  Drives consequences directly and collision probability indirectly
Brings Clusters at ~840 km and ~975 km closer to ~1,450 km band
Introducing Object-Years and Object-Metric Ton-Years

## Slide 6: Collision Risk Balance
More reflective, but still simplified, model to depict current operations
Risk posed x Risk abated x Persistence
Adding a behavior layer
Risk Burden Posed (RBP)
Collision risk the object poses to others
Size (now)
Mass (future catalog and LNT)
Risk Burden Abated (RBA)
Ability to reduce collision risk
Attitude control (‘duck’)
Propulsion system (move & remove)
PC threshold for maneuver
PC abate goal
Persistence/Altitude Adjustment (AA)
Objects persist at higher altitudes
Atmospheric drag

## Slide 7: Collision Risk Balance
Orbital Capacity =
Σ [RBP * {10-RBA} * AA]
  See paper for algorithm details
Major spikes across LEO not due to constellations
Risk posed x Risk abated x Persistence

## Slide 8: Synthesis
Just as important to remediate an orbital regime as individual objects
All models depict high debris-generating potential at 840km and 975km
  When considering persistence, 1,400 to 1,500km becomes third priority
Responsible constellation operations imperative to maintaining space safety as launches continue
  Further enabled by enhanced conjunction assessment services provided by LeoLabs’ global network of radars
Active Debris Remediation and Other Implications
Remove top 6 SL-16s
Aggregate Risk by Altitude