## Slide 1
Definition of Sustainable Development Goals based indices for the Earth observation missions assessment
Marco Nugnes, Camilla Colombo, Chiara Zuliani, Valerio Santoro
Politecnico di Milano
Space Capacity allocation for the sustainability of space activities Workshop, Milan, 6-8 June 2023

## Slide 2: Agenda
1. Introduction
  Background overview
  Sustainable Development Goals 2030
  Earth observation services
2. Modelling
3. Results
4. Conclusions and future developments

## Slide 3: Introduction
Background overview
Chart: Space VS Global economies average growths[3]
| 2005 | 2010 | 2015
Space economy | 0 | 33.5 | 67
Global economy | 0 | 17.5 | 35
[1] https://www.mise.gov.it/images/stories/documenti/all_6_Piano_Strategico_Space_Economy_master_130520 16_regioni_final.pdf
[2] https://www.oecd.org/
[3] https://www.eib.org/attachments/thematic/future_of_european_space_sector_en.pdf
[4] https://www.wwf.eu/?uNewsID=875891
Space Economy: entire value chain that, starting from research, development and manufacturing of enabling space infrastructures (upstream) goes up to the production of innovative enabled services (downstream)[1]
Wellbeing Economy: capacity to create a virtuous circle in which citizens’ well-being drives economic prosperity, stability and resilience […] [2]
Wellbeing Economy infographic. Courtesy of World Wide Fund [4].
Notes: - Sottolineare che si sta sviluppando un indice che valuta l’effetto di una missione spaziale in termini di benefits alla società basato sugli SDGs.
As you can.. Growing double rate
Let me now intro.. Newborn.. Endorsed by Council of EU and embraced by Iceland, Scotland, Finland and New Zeland joining WEGo network
Infographic – GDP growth persp – societal thriving – wellb of citizens and the planet. SDGs can guide decision making

## Slide 4: Introduction
Sustainable Development Goals 2030
[4] https://www.un.org/sustainabledevelopment/news/communications-material/
The 17 Goals were adopted by all UN Member States in 2015, as part of the 2030 Agenda for Sustainable Development which set out a 15-year plan to achieve the Goals
Courtesy of the United Nations [4].

## Slide 5: Introduction
Earth observation services
Questa foto di Autore sconosciuto è concesso in licenza da CC BY-SA-NC
Agriculture (Agr)
Built-up land (Blt)
Wild nature (Wild)
Geology (Geo)
Limnology (Limn)
Meteorology (Meteo)
Oceanography (Ocean)
Air Quality Monitoring
(AQM)
Hazards monitoring (Haz)

## Slide 6: Agenda
1. Introduction
2. Modelling
  Performance indices
  Mission and sensors analysed
  Flowchart
  Spatial resolution index
  Temporal resolution index
  Spectral efficiency index
  Earth coverage index
3. Results
4. Conclusions and future developments

## Slide 7: Modelling
Performance indices
How well?
What?
How frequently?
Where?
The core of the modelling is made of the four performance indices focusing on the payload and orbit main characterizing factors.
Spectral efficiency index ISpectr (0-100)
Spatial resolution index ISR (0-100)
Earth coverage index ICov (0-100)
Temporal resolution index ITR (0-100)

## Slide 8: Modelling
Union of Concerned Scientists database lists 2787 operational satellites around the Earth. 28% (785 satellites) are for Earth observation (EO), of which more than 93% lie on Low Earth Orbits (LEO)
Missions and sensors analysed
Orbits considered: Sun-synchronous orbits (73% of LEO EO missions). All have eccentricity values < 0.01, hence the assumption of circular orbits. Finally, assumption of repeat ground track orbits
Sensors considered: passive (whiskbroom, pushbroom) and active (Synthetic Aperture Radars)
Synthetic Aperture Radar (SAR)
Whiskbroom
Pushbroom
Courtesy of Moreira [5]
[5] A. Moreira. “A tutorial on Synthetic Aperture Radar”, IEEE Geoscience and Remote Sensing Magazine, 2013

## Slide 9: Modelling
Flowchart
Notes: - Starting from EO mission data (orb and sens tech par) and from the ident of sev services

## Slide 10: Modelling
Spatial resolution index
Ground Sample Distance (GSD): the pixel size on the ground surface measured by the instrument
Computed GSD | Literature GSD | Error
250.00 m | 250 m | 0%
GSD model validation for MODIS sensor on-board Terra
Computed GSD | Literature GSD | Error
20.00 m | 20 m | 0%
GSD model validation for HRVIR sensor on-board SPOT-4
Variable | Computed | Literature | Error
Range resolution | 17.33 m | 18 m | 3.72%
Azimuth resolution | 5.95 m | 6 m | 0.83%
Spatial resolution model validation for SAR on-board JERS-1
Whiskbroom sensor
Pushbroom sensor
SAR sensor
Index definition
Requirements
Model
Model validation

## Slide 11: Modelling
Temporal resolution index
ReVisit Time (RVT): time elapsed between two successive observations of the same ground point on the surface of the Earth
Variable | Computed | Literature | Error
S’width | 735.35 km | 735.43 km | ~ 0%
RVT | 4 | 4 | 0%
RVTmin | 1 | 1 | 0%
Variable | Computed | Literature | Error
S’width | 823.76 km | 830.17 km | 0.77%
RVT | 5 | 5 | 0%
RVTmin | 1 | 1 | 0%
RVT model validation for HJ-1A satellite
RVT model validation for IRS–P6 satellite
Index definition
Requirements
Model
Model validation

## Slide 12: Modelling
Spectral efficiency index for passive sensors
Spectral signatures based on
reflectance in the VIS-SWIR domain (0.37 – 2.5 µm)
emissivity in the TIR domain (3 – 5, 8 – 14 µm)
Services spectral signatures
Index definition
Final index obtained through a proportional-to-bandwidth average between ISpectr,VISSWIR and ISpectr,TIR
Flowchart
Area-proportional evaluation
Index application

## Slide 13: Modelling
Earth coverage index
The index is based on the service visibility in a repeat cycle with respect to the total service visibility
4320 x 8640 pixels services layers
Population density
Crops
Pastures
In-land water
Oceans
WWF biomes
Earthquakes hazard
Index definition
Datasets

## Slide 14: Modelling
Services indices
Services indices: the mean among the four aforementioned indices
E.g.
If

## Slide 15: Agenda
1. Introduction
2. Modelling
3. Results
  Earth observation for the Sustainable Development Goals 2030
  Earth observation services contribution to the SDGs and SDG indices
  Copernicus program evaluation
5. Conclusions and future developments

## Slide 16: Results
0: The service cannot support at all the Activity
1: The service is marginal for the achievement of the Activity
2: The service can poorly support the Activity
3: The service can moderately support the Activity
4: The service can strongly support the Activity
5: The service is fundamental for the Activity achievement
Earth observation for the Sustainable Development Goals 2030
Identification of the role of each service to support the SDGs through several Activities, readjusted from the possibilities listed by UNOOSA and bearing in mind all previous works to support the Agenda
Goal | Activity | Blt | Agr | Wild | Geo | Limn | Ocean | Meteo | AQM | Haz | Activity weight (0-1)
1. No Poverty | Natural disaster forecast and management | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0,3
 | Optimising sustainable utilisation of natural resources | 0 | 3 | 4 | 1 | 3 | 0 | 0 | 0 | 0 | 0,3
 | Mapping populated areas and their access to basic services | 5 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0,4
7,5 |  | 2,3 | 0,9 | 1,2 | 0,3 | 1,3 | 0 | 0 | 0 | 1,5 | 
2. Zero Hunger | Crop productivity optimisation | 0 | 5 | 0 | 0 | 3 | 0 | 3 | 1 | 0 | 0,5
 | Livestock management optimisation | 0 | 5 | 2 | 0 | 2 | 0 | 0 | 0 | 0 | 0,5
10,5 |  | 0 | 5 | 1 | 0 | 2,5 | 0 | 1,5 | 0,5 | 0 | 
Total score of each service with the weighted sum of the scores of such service for each activity
SDG total score
E.g. SDG #1: the total is 7.5, given by 2.3 + 0.9 + 1.2 + 0.3 + 1.3 + 0 + 0 + 0 + 1.5

## Slide 17: Results
Earth observation services contribution to the SDGs and SDG indices
EO majorly contributes to Goal 13 (Climate Action), followed by Goal 15 (Life on Land) and Goal 12 (Responsible Consumption and Production)
Major contributions from Built-up land and Limnology services
Two sets of indices:
    Relative indices: contribution of a mission to the SDGs with respect to given service maximum capability
    Absolute indices: it considers the maximum value among all the services capability

## Slide 18: Results
Copernicus program evaluation
Service indices of Copernicus program
Relative indices of Copernicus program
Absolute indices
Notes: Copernicus: EO program of ESA, able to evaluate 5 out of 6 missions
S1 radar mission, other passive sensors
Left spider dgrm  Service indices

## Slide 19: Agenda
1. Introduction
2. Modelling
3. Results
4. Conclusions and future developments

## Slide 20: Conclusions and future developments
Conclusions
The complete derivation of a tool for the evaluation of the social value assessment of EO missions is achieved
Missions technical parameters
Service indices
Social rating
ISR , ITR , ISpectr , ICov
EO4SDG
Including other types of perturbation, such as the atmospheric drag
Extending evaluable orbits types, such as geostationary and elliptical orbits, and evaluable sensors types, such as lidars, radar altimeters and microwave radiometers.
Improving services classification, by creating sub-services and including new services
Including other missions’ features, such as their footprint in terms of orbit crowding and space debris, the orbit maintenance requirements, readiness from the acquisition and open-source availability of data, international cooperation fostering
Extending the analysis to Navigation and Telecommunication applications, but also to other space missions' classes, such as Exploration and Safety and Security

## Slide 21: Thank you for your attention!
Marco Nugnes, Camilla Colombo, Chiara Zuliani, Valerio Santoro,
marco.nugnes@polimi.it
camilla.colombo@polimi.it
@COMPASS_ERC
www.compass.polimi.it
This project has received funding from the European Research Council (ERC) under the European Union’s Horizon 2020 research and innovation programme (grant agreement No 679086 – COMPASS)

## Slide 22: Introduction
Scalera et al. “Social value rating of Earth remote sensing missions through the United Nations Sustainable Development Goals 2030”
Programs and agencies working to define the socio-economic value of space missions
Socio-economic value of space missions and state of the art
Group on Earth Observations
Committee on Earth Observation Satellites
European Space Agency
United Nations Committee of Experts on Global Geospatial Information Management (UN-GGIM)
United Nations Office for Outer Space Affairs
Qualitative social benefits evaluation
Quantitative social benefits evaluation
Notes: Many space..
However, only qualitative
Scalera

## Slide 23: Introduction
Thesis aim and novelty of the work
Scope: to give a quantitative indication of the contribution an Earth observation mission can make to the achievement of the Sustainable Development Goals (SDGs) set by the UN, in a perspective of sustainability
With respect to other works:
    quantitative evaluation rather than qualitative
With respect to Scalera:
    Air Quality Monitoring service added
    Novel technique for the Temporal resolution index
    New methodology for the Spectral efficiency index of SAR sensors
    Earth coverage index developed through several world data layers
    Cloud coverage considered
    Possibility of analysing also hyper-spectral sensors and satellite constellations
    Quantitative link between services and SDGs

## Slide 24: Agenda
1. Introduction
2. Thesis groundwork
  Sustainable Development Goals 2030
  Earth observation services
  Performance indices
  Missions and sensors analysed
  Thesis structure
3. Modelling
4. Results
5. Conclusions and future developments

## Slide 25: Modelling
Spatial resolution index 1
Flowchart
Model validation
Ground Sample Distance (GSD): the pixel size on the ground surface measured by the instrument
Computed GSD | Literature GSD | Error
250.00 m | 250 m | 0%
GSD model validation for MODIS sensor on-board Terra
Computed GSD | Literature GSD | Error
20.00 m | 20 m | 0%
GSD model validation for HRVIR sensor on-board SPOT-4
Variable | Computed | Literature | Error
Range resolution | 17.33 m | 18 m | 3.72%
Azimuth resolution | 5.95 m | 6 m | 0.83%
Spatial resolution model validation for SAR on-board JERS-1
Whiskbroom sensor
Pushbroom sensor
SAR sensor

## Slide 26: Modelling
Spatial resolution index 2
SR service requirements
Index computation
Index application

## Slide 27: Modelling
Temporal resolution index 1
Flowchart
Model validation
ReVisit Time (RVT): time elapsed between two successive observations of the same ground point on the surface of the Earth
Variable | Computed | Literature | Error
S’width | 735.35 km | 735.43 km | ~ 0%
RVT | 4 | 4 | 0%
RVTmin | 1 | 1 | 0%
Variable | Computed | Literature | Error
S’width | 823.76 km | 830.17 km | 0.77%
RVT | 5 | 5 | 0%
RVTmin | 1 | 1 | 0%
RVT model validation for HJ-1A satellite
RVT model validation for IRS–P6 satellite

## Slide 28: Modelling
Temporal resolution index 2
TR service requirements
Index computation
Index application

## Slide 29: Modelling
Spectral efficiency index for passive sensors – Air Quality Monitoring
Index definition
Based on gases detection bands in the UV (0.1 – 0.37 µm), VIS-SWIR (0.37 – 2.5 µm) and TIR (3 – 5, 8 – 14 µm) domains
Index based on a boolean evaluation
Index application
Mission | Ispectr,AQM
AIRS | 50
MODIS | 16.67
CERES | 100
Ispectr,AQM of AIRS, MODIS and CERES sensors
Flowchart
Gases detection bands

## Slide 30: Modelling
Spectral efficiency index for SAR sensors
 | Ku | X | C | S | L | P
Blt |  |  |  |  |  | 
Agr |  |  |  |  |  | 
Wild |  |  |  |  |  | 
Geo |  |  |  |  |  | 
Limn |  |  |  |  |  | 
Ocean |  |  |  |  |  | 
Haz |  |  |  |  |  | 
Based on sensor operative band (Ku, X, C, etc..) and signal polarisation (HH, HV, VH, VV)
Relative scattering strength by polarisation | 
Rough surface | VV > HH > HV or VH
Double bounce | HH > VV > HV or VH
Volume | HV or VH > > HH or VV
 | Rough surface | Double bounce | Volume
Blt | 1 | 2 | 0
Agr | 2 | 0 | 1
Wild | 2 | 1 | 2
Geo | 2 | 1 | 0
Limn | 2 | 2 | 0
Ocean | 2 | 0 | 0
Haz | 2 | 2 | 2
Link : ‘’pctpol’’
Index definition:
Courtesy of Meyer [5]
[5] “The SAR Handbook: Comprehensive Methodologies for Forest Monitoring and Biomass Estimation”.
SARs operative bands common applications
Services type of scattering (0-2)

## Slide 31: Modelling
Flowchart
Earth coverage index 1
The index is based on the service visibility in a repeat cycle with respect to the total service visibility
Datasets
4320 x 8640 pixels services layers
Population density
Crops
Pastures
In-land water
Oceans
WWF biomes
Earthquakes hazard

## Slide 32: Modelling
Ground track computation and identification of the pixels seen by the sensor
Earth coverage index 2
Index computation
Passive sensors
Active sensors
Index application

## Slide 33: Results
Pléiades and PRISMA – passive sensor missions
Notes: Passive sensors
Pleiades, very high resolution mission  french space agency, PRISMA, hyperspectral mission  ASI

## Slide 34: Results
COSMO-SkyMed SG and Biomass – SAR missions
Notes: COSMO-SkyMed sar mission of ASI X band fully pol, Biomass  Earth explorer mission of the ESA, P band, fully polarimetric
COSMO even if limited to certain services, provide significant social performances

## Slide 35: Conclusions and future developments
High versatility in terms of services supply
Hyper-spectral sensors are filling the gap of passive instruments in terms of spectral efficiency
Support the SDGs more effectively
Conclusions
Passive instruments
Synthetic Aperture Radars
Limited number of services according to their operative band
Higher services indices, especially in full-polarimetric modes
Support less effectively the SDGs (higher indices but less Goals)
Next future of EO still characterised by a combination of these two imaging technologies complementarity of the attainable data
The complete derivation of a tool for the evaluation of the social value assessment of EO missions is achieved
MMissions technical parameters
SService indices
SSocial rating
ISR , ITR , ISpectr , ICov
EO4SDG

## Slide 36: Conclusions and future developments
Including other missions’ features, such as their footprint in terms of orbit crowding and space debris, the orbit maintenance requirements, readiness from the acquisition and open-source availability of data, international cooperation fostering
Criticalities and future developments
Criticalities:
    Intrinsic difficulty in quantifying something not directly measurable like social benefits
    The boundaries lability of service requirements, on which the four technical indices are based
    Arithmetic average of the four performance indices may results in a loss of information
    Modelling the flexibility of the sensors imaging modes
    Validity of the assigned quantities of EO4SDG table need to consolidate also employing surveys and/or stakeholders’ advice
Including other types of perturbation, such as the atmospheric drag
Extending evaluable orbits types, such as geostationary and elliptical orbits,
and evaluable sensors types, such as lidars, radar altimeters and microwave radiometers.
Extending the analysis to Navigation and Telecommunication applications, but also to other space missions' classes, such as Exploration and Safety and Security
Improving services classification, by creating sub-services and including new services
Future developments