## Slide 1: Implementation of Rapidly-Scanned, Infrared Laser Absorption Diagnostics in NASA Electric Arc Shock Tube Experiments
Efaine Chang, Dylan Drescher, Jesse Streicher,
Christopher Strand, Prof. Ronald K. Hanson
Andrea Fagnani, Brett Cruden
High Temperature Gasdynamics Laboratory
Stanford University
Outline:
1
10th International Workshop on Radiation of High Temperature Gases for Space Missions Oxford, September 10, 2024
Theory
Results
Conclusions
Background

## Slide 2: Motivation
2
Incident Shock Tube (e.g., EAST/T6)
Reflected Shock Tube (e.g., Stanford)
Shock Tunnels (e.g., T5/T6)
  Stagnated test gas provides high time resolution
  Integration of multiple UV laser diagnostics
  Low enthalpy conditions and limited test time
  High-velocity incident shocks reproduce relevant conditions
  Optical access typically includes absorption and emission diagnostics
  Temporal and spatial resolution are coupled
  Valuable for studying flow around test geometries
  Access to high enthalpy gas with long test times
  Flow can introduce non-uniform lines of sight
  Nozzles can freeze species in nonequilibrium quantities
Many types of ground tests are needed for validating nonequilibrium models
Background
Theory
Results
Conclusions

## Slide 3: Motivation
  EAST is an established, high-enthalpy facility using emission spectroscopy.
  Project Goal: Combine Stanford absorbance diagnostic expertise with EAST facility and emission diagnostic capabilities to investigate nonequilibrium in low-speed air.
  Develop an IR-based laser absorption diagnostic for hypersonic flight conditions
        Provide direct, quantitative measurements of state-specific populations
        Refine and validate theoretical models
Background
Theory
Results
Conclusions
Stanford
  Absorption Diagnostics: CN, O*, N*, NO, T, ne
  Spectroscopy: fast-scanned infrared absorption to infer T and n
  Kinetics: vibrational relaxation, electronic excitation, ionization, and chemical reactions
NASA
  EAST Facility: Very fast incident shock speeds provides wide range of test conditions
  Emission diagnostics: very large spectral range for many species simultaneously
  Radiation models: excited state nonequilibrium

## Slide 4
https://www.nasa.gov/ames/thermophysics-facilities/electric-arc-shock-tube
EAST Facilities
Background
Theory
Results
Conclusions
Electric Arc Driver
Test Section
Emission Spectrometers
Dump Tank
Expansion Cone (Optional)
HVST, 10 cm diameter
9 m driven section
Overview
~400 m2 footprint
Shock speeds 1.3 – 46 km/s
Pressures 10-4 – 100 atm
40-kV high voltage DC power supply
1.25 MJ capacitor bank
Circular ports for pressure, line-of-sight optical diagnostics
Slot windows for emission diagnostics

## Slide 5: Interest in Low-Speed Air
    Previous EAST tests focused on lunar return conditions [1].  Velocities generally in excess of 10 km/s
     Lowest velocity considered ~7 km/s
    Interest in shock layer kinetics at lower velocities
    OES infers high-lying excited states
     Challenging to infer information on low-lying states
Background
Theory
Results
Conclusions
https://www.nasa.gov/ames/thermophysics-facilities/electric-arc-shock-tube
[1] Brandis, A., et al., 43rd AIAA Thermophysics Conference (2012).
There is an opportunity for absorption-based experimental data.
Low-Speed Air (NO)
Low-Speed Air (O*,N*)

## Slide 6: Laser Absorption Spectroscopy
Absorption is a function of fundamental, quantum-mechanical properties of the absorbing species and the number density in the absorbing state.
Beer-Lambert Relation
Rewriting with spectroscopic constants
Uniform Test Gas
(T, P, )
I0
It
Detector
Monochromatic light source
at wavelength ()
Background
Theory
Results
Conclusions
L
Assuming independent rotational and vibrational distributions

## Slide 7: Nitric Oxide (NO)
Excellent indicator of non-equilibrium behavior
Formation described by Zeldovich reactions
Strongly coupled with T
Presence at high-T can be used to measure gas properties using TDLAS
Results
Conclusions
Theory
Background

## Slide 8: Line Selection (NO)
Background
Theory
Results
Conclusions
Line selection is optimized for
Spectral isolation from interfering species
Sufficient absorbance (>0.1)
Large sweep of v” and J”
Multiple features captured in a single scan, by a single laser at >500 kHz scan rates.
Wavelength selection covers
9 features at ~5.2 um
v” = 0-3, J” = 9.5-59.5

## Slide 9: Excited Atomic Species (O*, N*)
At >10000 K, N2 and O2 break down into N and O
Radiation originates from ionized species or electronically excited quantum states of neutral species
N*(868 nm), 3s 4P 3p 4D°
Lowest lying, easily accessible states
Background
Theory
Results
Conclusions

## Slide 10: Absorption-Based Diagnostic
Background
Theory
Results
Conclusions
Mitigate non-ideal effects, fiber-couple for ease of use and safety.

## Slide 11: Low Velocity, High Pressure (NO)
Three kinetics models considered
Stanford
  Incident shock code
  Park + various sources
    Experimental rates for NO, O2
  No ionized species
Stanford P93
  Incident shock code
  Park93 solely
    Includes ionized species
DPLR
  Stagnation line, flow around sphere
  Park + Cruden et al. corrections
Background
Theory
Results
Conclusions
TDLAS measurements
  (1) Trend well with models; (2) Converge to equilibrium (w/ models), as expected.
  ** Note that Stanford models provide Tvib,NO vs DPLR Tvib
TDLAS measurements
(1) Trend well with Stanford model.
  At long times all 3 models converge to equilibrium.

## Slide 12: Low Velocity, High Pressure (NO)
NO measurements at a glance:
TDLAS measurements track models closely in both temperature and number density.
Experimental temperatures agree within 15%. (No emission-inferred number density currently available.)
There exists a 10% offset between measurements and models.
Model discrepancies may be attributed to differing and expressions in each model, vibrational energy handling.
Background
Theory
Results
Conclusions
TDLAS measurements
(1) Track models closely.
(2) Converge to equilibrium (w/ models), as expected.
** Disagreement between models in NO formation

## Slide 13: High Velocity Temperature Number Density (O* 5P)
Background
Theory
Results
Conclusions
Experimental temperatures agree within 5-10%.
Measurements suggest a lower number density than models predict.
Large scatter and uncertainty due to low population.

## Slide 14: High Velocity Number Densities (O* 5S, N* 4P)
Background
Theory
Results
Conclusions
Measurements in agreement with models.

## Slide 15: Collisional-Radiative Considerations
De-excitation through spontaneous emission can be estimated via the Einstein-A coefficient
Background
Theory
Results
Conclusions
Radiative processes can play a significant role in the kinetics of atomic species electronic excitation.
Term | [s-1] |  | [s-1]
3s 5S0 | 5.6E+03 |  | 
3p 5P3 | 3.7E+07 | 1 | 
3s 4P | 4.0E+08 | 1E-05 | 
Term |  |  | 
3s 5S0 | 5.6E+03 |  | 
3p 5P3 | 3.7E+07 |  | 
3s 4P | 4.0E+08 |  | 
Oxygen Atom (O)

## Slide 16: Impact of Collisional-Radiative Corrections
Updated figures
Background
Results
Conclusions
Theory
Original figures
Additional uncertainty from EAST reported Uis values (~1%).

## Slide 17: Summary
Seven fast-scanning TDLAS-based diagnostics targeting NO in the mid-IR, and O* and N* in the near-IR have been successfully integrated and demonstrated in the NASA Ames EAST facility.
Stanford measurements have been compared with emission measurements, Stanford models, and Ames modeling (DPLR).
Temperature measurements are consistent between Stanford absorption and NASA emission diagnostics, and relatively consistent with modeling.
Temperature measurements are higher than models suggest.
NO number density measurements track well with Stanford models.
O*(5S) and N*(4P) measurements are higher than models suggest, O*(5P) measurements are lower.
  CR considerations resolve some of the disagreement between excited states.
  Uis reporting uncertainty can resolve some of the remaining disagreement between measurement and model.
These discrepancies motivate ongoing, air kinetics work to resolve the accuracy of modeling assumptions.
Background
Theory
Results
Conclusions

## Slide 18: Acknowledgements
Stanford
Efaine Chang
Dylan Drescher
Jesse Streicher
Christopher Strand
Professor Ronald K. Hanson
NASA
NSTGRO, 80NSSC21K1268
Andrea Fagnani, USRA
Brett A. Cruden, AMA
Entry Systems Modeling Project
AFOSR
FA9550-19-1-0219
FA9550-21-1-0311

## Slide 19
Thank You!