## Slide 1: Ultraviolet Laser Absorption Studies of the Vibrational Relaxation and Kinetics of High-Temperature Air
Jesse Streicher
Spencer Barnes, and Prof. Ronald Hanson
High Temperature Gasdynamics Laboratory
Stanford University
10th International Workshop on Radiation of High Temperature Gases for Space Missions Oxford, September 10, 2024
Background
Expt. Methods
Rates
Conclusions
Outline:
Time-Histories
1

## Slide 2: Ground Test Facilities to Reproduce Flight Conditions
2
Incident Shock Tube (e.g., EAST/T6)
Reflected Shock Tube (e.g., Stanford)
Shock Tunnels (e.g., T5/T6)
  Stagnated test gas provides high time resolution
  Integration of multiple UV laser diagnostics
  Low enthalpy conditions and limited test time
  High-velocity incident shocks reproduce relevant conditions
  Optical access typically includes absorption and emission diagnostics
  Temporal and spatial resolution are coupled
  Valuable for studying flow around test geometries
  Access to high enthalpy gas with long test times
  Flow can introduce non-uniform lines of sight
  Nozzles can freeze species in nonequilibrium quantities
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 3: Multi-Step Process for Inferring Reaction Rates
3
State-Specific Time-History Measurements in Shock Tubes
Results
  Measure α(t)
  Infer temperature from α ratios
  Infer number density from α magnitude
  Infer vibrational-state specific number density.
UV Laser Absorption Diagnostic Development
Results
  Leverage spectroscopic model to choose vibrational-state-specific wavelength(s)
  Measure α(t) for mixtures with well-known temperature and composition
  Infer σ(Ttr,Tvib) over wavelength and temperature sweeps
Selected Wavelengths
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 4: Multi-Step Process for Inferring Reaction Rates
4
State-Specific Time-History Measurements in Shock Tubes
Results
  Measure α(t)
  Infer temperature from α ratios
  Infer number density from α magnitude
  Infer vibrational-state specific number density.
Nonequilibrium Rate Parameter Inferences
Results
τv from Tv(t)
kdO2 from nO2(t)
kdNO and kz from nNO(t)
Fit rate parameters with known T-dependence
UV Laser Absorption Diagnostic Development
Results
  Leverage spectroscopic model to choose vibrational-state-specific wavelength(s)
  Measure α(t) for mixtures with well-known temperature and composition
  Infer σ(Ttr,Tvib) over wavelength and temperature sweeps
O2 Dissociation
NO Dissociation
Zeldovich Reaction Rates
Experiments have probed either O2 or NO, motivating an investigation of both in high-T air.
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 5: Experimental Setup – Ultraviolet Laser Diagnostics
15.24 cm
5 mm
Top View
UV-grade fused silica windows
End View
Det.
Det.
Pump
Continuous Wave Ti:Sapphire Cavity
Frequency Doubling Stages
Det.
Det.
Det.
Pump
Pellin-Broca Prism
Fourth Harmonic Generator
Det.
Pulsed Ti:Sapphire Cavity
Det.
Det.
Pump
+
Amplifier
Frequency Doubling Stages
Reflected Shock Tube
  Measured shock velocity → T0, P0
  Stagnated test gas → tpart = tlab
  Pressure gauge → P(t)
Mira Laser System
  Pulsed, broadly tunable UV
  Primarily targets O2
Sacher Laser System
  Continuous-wave, tunable UV
  Targets both O2 and NO
M-Squared Laser System
  Continuous-wave, tunable UV
  Primarily targets NO
5
Background
Conclusions
Methods
Rates
Time-Histories
Det.
Shock Wave
Beer-Lambert Relation used to quantify state-specific absorbance:

## Slide 6: Data Analysis Procedure
Note: Separation of and is informed by separate cross-section studies, and iterated in the full data analysis
αλ
6
211.2 nm
226.1 nm
246.3 nm
236.9 nm
O2 v” = 4
NO v” = 0
NO v” = 2
O2 v” = 6
224.8 nm
NO v” = 0
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 7: Data Analysis Procedure
Inferred Quantity | Method
Vibrational Temperature | 
Total O2 Number Density | 
Vibrational-State-Specific Number Density | 
O2 Dissociation Rate | 
O2 Vibrational Relaxation Times | 
Inferred Quantity | Method
Vibrational Temperature | 
Total O2 Number Density | 
Vibrational-State-Specific Number Density | 
O2 Dissociation Rate | 
O2 Vibrational Relaxation Times | 
αλ
7
Inferred Quantity | Method
Vibrational Temperature | 
Total O2 Number Density | 
Vibrational-State-Specific Number Density | 
O2 Dissociation Rate | 
O2 Vibrational Relaxation Times | 
Inferred Quantity | Method
Vibrational Temperature | 
Total O2 Number Density | 
Vibrational-State-Specific Number Density | 
O2 Dissociation Rate | 
O2 Vibrational Relaxation Times | 
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 8: Data Analysis Procedure
Inferred Quantity | Method
Translational/Rotational Temperature | 
NO Vibrational Temperature | 
Total NO Number Density | 
Vibrational-State-Specific Number Density | 
Zeldovich Reaction Rates | 
Inferred Quantity | Method
Translational/Rotational Temperature | 
NO Vibrational Temperature | 
Total NO Number Density | 
Vibrational-State-Specific Number Density | 
Zeldovich Reaction Rates | 
αλ
8
Inferred Quantity | Method
Translational/Rotational Temperature | 
NO Vibrational Temperature | 
Total NO Number Density | 
Vibrational-State-Specific Number Density | 
Zeldovich Reaction Rates | 
Inferred Quantity | Method
Translational/Rotational Temperature | 
NO Vibrational Temperature | 
Total NO Number Density | 
Vibrational-State-Specific Number Density | 
Zeldovich Reaction Rates | 
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 9: Absorbance Time-Histories
211.2 nm
223.2 nm
Absorbance noise is proportional to laser output power
Best-fit simulation captures absorbance behavior at all λ
O2 contributions at all λ, with 236.9 nm least sensitive to NO formation
Background
Conclusions
Methods
Rates
Time-Histories
9
226.1 nm
246.3 nm
236.9 nm
224.8 nm
221.6 nm
O2 v” = 4
O2 v” = 5
NO v” = 0
NO v” = 2
O2 v” = 6
NO v” = 0
O2 v” = 5

## Slide 10: Temperature Time-Histories
Simulations use separate Tv for the vibrational relaxation for O2 and N2
TvNO results suggest NO forms with Tv Ttr after delayed NO formation
TvO2 time histories agree well with previously inferred relaxation times
10
Inferred Ttr also agrees with both TvNO results and simulations
Ttr
TvO2
TvN2
TvO2 (inferred)
TvNO (inferred)
Ttr (inferred)
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 11: Number Density Time-Histories
11
nO2 and nNO simulations couple density change and chemistry
nNO increase primarily sensitive to Zeldovich reactions (esp. kzN2-O)
nO2 decrease primarily sensitive to kdO2-O2,
kdO2-N2, and kdO2-O
nv” time-histories highlight vibrational-state sensitivity of diagnostics
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 12: Features of Best-Fit Model
12
O2 wavelengths are reasonably reproduced with Jerig et al. kdO2-N2
NO formation delayed, requiring a Park 2-T correction
Background
Conclusions
Methods
Rates
Time-Histories
Early-time O2 vibrational relaxation present at all wavelengths

## Slide 13: T/P Sweeps Exhibit Consistent Behavior
13
Delay in NO formation increases at lower temperature
Onset of NO formation occurs earlier in higher pressure experiments
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 14: O2-N2 Vibrational Relaxation
Data agrees well with previous vibrational relaxation study
High-T data deviate from the Millikan and White correlation (used in Park 2-T model)
Significantly lower scatter than literature
14
Background
Conclusions
Methods
Rates
Time-Histories
Improved agreement with Andrienko and Boyd

## Slide 15: O2-N2 Dissociation Rate Inferences
15
Background
Conclusions
Methods
Rates
Time-Histories
Data agrees with previous experimental inferences, with lower scatter than literature
New O2-N2 rates are similar to previous O2-Ar
Trend agrees well with Andrienko and Boyd rate
O2-N2 dissociation ~10x slower than predicted by Park 2-T model

## Slide 16: N2-O Zeldovich Exchange Rate Inferences
16
Background
Conclusions
Methods
Rates
Time-Histories
All recent data and models differ from Park
Difference between N2O and air is also present in literature experiments
New results span predictions of QCT models with different activation energy
Notable difference between rate inferred in 21% O2/N2 and in 5% N2O/N2 at low-T

## Slide 17: Park Model Comparison
17
Park 2-T model predicts fast O2 relaxation and dissociation
Overall, Park 2-T model is insufficient to reproduced observations
Subsequent NO formation also occurring too fast
Background
Conclusions
Methods
Rates
Time-Histories

## Slide 18
Conclusions
Seven wavelengths probe O2 in
v” = 4-6 and NO in v” = 0, 2
  Optical strategies ensure low noise
  Inferred quantities include TvO2, TvNO, Ttr, nO2, nNO, and nv”
NO formation in 21% O2/N2 mixtures exhibits a delay corresponding to the N2 vibrational relaxation time
  A dependence for kzN2-O reasonably reproduces the experimental results
Combined O2 and NO results differ significantly from Park 2-T model
  O2 vibrational relaxation and dissociation both occur too fast
  NO onset is early, with formation occurring slightly too fast
18
Background
Conclusions
Methods
Rates
Time-Histories
Future work will infer kdO2-N2 and kzN2-O

## Slide 19
Stanford Colleagues
  Students: Spencer Barnes
  Principal Investigator: Prof. Ronald Hanson
Support
  AFOSR: Dr. S. Popkin and Dr. M. Berman
Collaboration:
  University of Colorado Boulder: Prof. I. Boyd, Dr. T. Aiken,
  Dr. D. Andrienko, and Dr. R. Chaudhry
… and many helpful conversations with members of the modeling and experimental community!
Acknowledgments
19
Background
Conclusions
Methods
Models
Time-Histories

## Slide 20: Questions

## Slide 21: Backup

## Slide 22: Nonequilibrium Rates Inferred with UV LAS
O2 Dissociation
O2 Vibrational Relaxation
22
NO Vibrational Relaxation
Zeldovich Reaction Rates
NO Dissociation
So far, experiments have been limited to probing either O2 or NO, motivating a full investigation of both in high-temperature air.
Background
Conclusions
Methods
Models
Time-Histories

## Slide 23: Bose and Candler Model Comparison
Background
Conclusions
Methods
Models
Time-Histories
23
Bose and Cander QCT rate provides another 2-T expression for kzN2-O
Opportunity for additional QCT investigation of 2-T behavior of kzN2-O
Caveat: a, b, and c were extrapolated to low temperature (<7000 K)

## Slide 24: Importance of O2 and NO in High-Temperature Air
7 Species Air Reactions
NO + [M] ↔ NO+ + e- + [M]
5 Species Air Reactions
[M] = O2, N2, O, N, NO
Vibrational Relaxation
  O2(v”) + [M] ↔ O2(v’) + [M]
  N2(v”) + [M] ↔ N2(v’) + [M]
Dissociation
  O2 + [M] ↔ O + O + [M]
  N2 + [M] ↔ N + N + [M]
  NO + [M] ↔ N + O + [M]
Zeldovich Exchange Reactions
  N2 + O ↔ NO + N
  O2 + N ↔ NO + O
11 Species Air Reactions
N + [M] ↔ N + + e- + [M]
O + [M] ↔ O + + e- + [M]
N2 + [M] ↔ N2 + + e- + [M]
O2 + [M] ↔ O2 + + e- + [M]
24

## Slide 25
Absorption Process – O2 in the Ultraviolet
Absorbing Gas
L
T, P, ni
Incident Intensity
Transmitted Intensity
Det.
Beer-Lambert Relation
O2
Measurements at 236.9 nm probe v” = 6
25
Continuous bound-unbound transitions pose challenges for interference-free NO sensing
Background
Conclusions
Methods
Rates
Time-Histories
TvNO Diagnostic

## Slide 26
Diagnostic wavelengths were selected to reduce O2 interference
Absorption Process – NO in the Ultraviolet
224.8155 and 246.3222 nm probe v” = 0 and 2, respectively
26
Seven diagnostics have been developed, with 246.3222 nm new to this work
Background
Conclusions
Methods
Rates
Time-Histories
TvNO Diagnostic

## Slide 27: Ultraviolet Laser Diagnostics
27
Mira Laser System
Sacher Laser System
M-Squared Laser System
Pump
Pump
Infrared Pump
Infrared
Infrared
Frequency Doubling
Frequency Quadrupling
Frequency Doubling

## Slide 28: Shock Tube Alignment for Common Mode Rejection
28
I(t) - ”Catch” Detectors
I0(t) - “Pitch” Detectors