## Slide 1
Alex B. Glenn, Justin Clarke, Peter L. Collen, Luca Di Mare and Matthew McGilvray
Osney Thermofluids Institute, University of Oxford, United Kingdom
09/09/2024
10th International Workshop on Radiation of High Temperature Gases for Space Missions
Thermochemical Characterisation of Shock Heated Flows

## Slide 2: Low Earth Orbit Return Stagnation Lines
Vehicle descends from speeds of ~8 km/s
Radiative heating negligible compared to convective
Non-equilibrium phenomena may reach vehicle surface:
  Influence heat flux via shock wave/boundary layer interactions
  Communications blackout due to excess electrons
  Convective heat load
  Forces on vehicle surface and trajectory from aerothermodynamic couple
  Visibility
Desirable to characterise the thermochemical state through vehicle stagnation line
Illustration of entry vehicle shock layer. Not to scale.
Velocity-altitude map superimposed with high temperature gas effects. Taken from Anderson.

## Slide 3: Shock Tubes
Shock tubes can re-create stagnation lines at ground level
Advantages over other impulse facilities:
We know the initial boundary conditions
No scaling required
Full thermochemical evolution
Particle times of flight differ from vehicle stagnation line due to boundary layer mass consumption…
Illustration of hock tube – stagnation line analogy. Not to scale.
Radiation emission as test slug traverses AST window

## Slide 4: Particle Time of Flight Discrepancy in Shock Tubes
Illustration of vehicle and shock tube particle time of flight trajectories

## Slide 5: Particle Time of Flight Discrepancy in Shock Tubes
Illustration of vehicle and shock tube particle time of flight trajectories
Clarke, J., Di Mare, L., and McGilvray, M., “Spatial Transformations for Reacting Gas Shock Tube Experiments,” AIAA journal, Vol. 61, No. 8, 2023, pp. 3365–3374

## Slide 6: T6 Stalker Tunnel: Aluminium Shock Tube
Large diameter (225 mm)
  Increases integration path length
  Better signal:noise
Relatively thinner boundary layer
  Less shock deceleration
  Longer test slugs
Section view of T6 Stalker tunnel in Aluminium Shock Tube mode.
Condition map of 2023 T6 AST LEO campaign.

## Slide 7: T6 Stalker Tunnel: Aluminium Shock Tube
Large diameter (225 mm)
  Increases integration path length
  Better signal:noise
Relatively thinner boundary layer
  Less shock deceleration
  Longer test slugs
Section view of T6 Stalker tunnel in Aluminium Shock Tube mode.
Condition map of 2023 T6 AST LEO campaign.

## Slide 8: Telecentric Optical Emission Spectroscopy
The Vis/NIR (upper) and UV/Vis (lower) telecentric OES systems capturing radiation from a shock layer. Not to scale.
Calibrated spatio-spectral radiance data for T6s492 (6.65km/s, 90 Pa fill in pure nitrogen). UV/Vis wavelengths on left and Vis/NIR on right.

## Slide 9: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions

## Slide 10: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN

## Slide 11: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS

## Slide 12: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS
Fitting procedure considers all species
  The more information the better

## Slide 13: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS
Fitting procedure considers all species
  The more information the better
Starts at most relaxed end of observed test slug and increments towards shock front

## Slide 14: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS
Fitting procedure considers all species
  The more information the better
Starts at most relaxed end of observed test slug and increments towards shock front
Currently only ran for UV/Vis and Vis/NIR wavelength regions (but can be expanded!)

## Slide 15: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS
Fitting procedure considers all species
  The more information the better
Starts at most relaxed end of observed test slug and increments towards shock front
Currently only ran for UV/Vis and Vis/NIR wavelength regions (but can be expanded!)
Feature | Constrained Spectral Fitting | Previous Spectral Fitting
Mass conservation |  | X
Momentum conservation |  | X
Energy conservation |  | X
Wavelengths included | As many as possible | Isolate wavelength region for specie of interest
Spatial smearing correction near shock front |  | X
Constrained spectral fitting vs previous spectral fitting.

## Slide 16: Constrained Spectral Fitting Routine
Two-temperature model and Boltzmann distributions
Conserves total enthalpy, mass and momentum by calling OCEAN
Predicts spectral traces via NEQAIR
  Results therefore dependent on the NEQAIR modelling
  Convolve by ILS
Fitting procedure considers all species
  The more information the better
Starts at most relaxed end of observed test slug and increments towards shock front
Currently only ran for UV/Vis and Vis/NIR wavelength regions (but can be expanded!)
Summary of constrained spectral fitting routine.
Constrained spectral fitting
INPUTS:
Experimental spectra
Shock speed
Tube diameter
Fill pressure and temperature
Composition
ILS functions
Relevant species
OUTPUTS:
Ttr and Tve profiles
Number density profiles for chosen species
Corresponding pressure, enthalpy and density profiles

## Slide 17: Next Steps
Validate constrained methodology against artificial data
Apply to EAST-62-40 and compare against previous spectral fitting results
Apply to new T6 AST pure nitrogen data

## Slide 18
Validation

## Slide 19: Validate Method - Generate Artificial NESS-NEQAIR Radiance Data

## Slide 20: Validate Method - Generate Artificial NESS-NEQAIR Radiance Data
In this work we constrain to the spectral wavelengths and resolutions of the T6 AST dataset, but the methodology is not limited to this!

## Slide 21: Initial Test – T6s492 (Pure Nitrogen at 6.65km/s, 90 Pa fill)
Constrained and unconstrained temperature results.

## Slide 22: Initial Test – T6s492 (Pure Nitrogen at 6.65km/s, 90 Pa fill)
Species captured well by constrained spectral fitting routine.

## Slide 23: Initial Test – T6s492 (Pure Nitrogen at 6.65km/s, 90 Pa fill)
Species not captured well by constrained spectral fitting routine.

## Slide 24: Example Spectral Fits and Physical Properties
Equilibrium
Relaxing
Immediate
post-shock
Spectral fits from constrained routine.
Physical properties of constrained and unconstrained spectral fitting, calculated via OCEAN.

## Slide 25: Experimental Artefacts: Contaminants
Repeated NESS-NEQAIR simulation but included 12 contaminants in simulation
Do they influence our ability to extract correct information for species of interest?
Timescales to run for all contaminant species will take too long…
Effect of including contaminants in equilibrium spectra
UV/Vis
Vis/NIR

## Slide 26: Experimental Artefacts: Contaminants
Ran constrained spectral fitting for N2, N, N2+, N+, E- and:
No contaminants
CN
CN, C2, C, H2, H
N2+ improved by including CN
Don’t need to include other contaminants to capture species of interest well
Tve
N2
N
N2+

## Slide 27: Experimental Artefacts: Spatial Smearing
Spatial smearing occurs from:
  Shock motion
  Camera
  Optics
Applied Spatial Resolution Functions to NESS-NEQAIR profiles
Signal removed from immediately behind the shock
Want a way to account for this…
UV/Vis radiance profiles
UV/Vis Non-Eq. Spectra
Vis/NIR radiance profiles
Vis/NIR Non-Eq. Spectra

## Slide 28: Experimental Artefacts: Spatial Smearing
Cumulative integral of the SRF function used to approximate a scale factor for spectral radiance
Spectral fitting immediately behind shock front improves
Example SRF Profile to generate weighting profile
Positioning relative to radiance profiles
Improvement in spectral fitting immediately behind shock

## Slide 29: Experimental Artefacts: Spatial Smearing
Improves Tve in first ~2/3mm behind shock
Varies with size of SRF
Simulations have shown agreement improves as the camera gate function is reduced
Profiles extracted by constrained spectral fitting with and without SRF weighting applied

## Slide 30: Side Note – Can feed the routine more data!
Results from feeding routine with the NESS E- number density profile
Opportunities to expand the code
Not limited to current dataset!
Can identify other valuable measurements from shock tube experiments

## Slide 31
EAST Data

## Slide 32: Application to Real Data: EAST-62-40
6.88 km/s, 26.6 Pa in pure nitrogen
Spectral fitting results from Tibère-Inglesse and Cruden available for comparison
EAST-62-40 shock speed profile
Comparison vibrational temperatures extracted from EAST-62-40 via alternate spectral fitting methodologies
Sample number density profiles corresponding to constrained fit results

## Slide 33
T6 AST Data

## Slide 34: Include T6 AST Data: Pure Nitrogen Shots
Shock speed profiles of selected shots
UV radiance profiles of selected shots

## Slide 35: Example Spectral Fits of Real Data: T6s492, 6.65 km/s
Reasonable fits attained through all portions of the test slug
Predictions in wavelength regions not captured possible via NEQAIR simulation
End of observed test slug (~110 us)
Relaxing test slug (~20us)
Peak non-equilibrium (~5us)

## Slide 36: Real Data: Temperatures
Tve
N2+ mole fractions through test slugs

## Slide 37: Real Data: N2 and N
N2 mole fractions through test slugs
N mole fractions through test slugs

## Slide 38: Conclusions and Further Work
Constrained spectral fitting routine developed
  Conserve mass, momentum and energy through test slug
Validated against artificial data
  Incorporated contaminants and spatial smearing correction
Applied to real shock tube data and compared to previous spectral fitting attempts
Next steps (in the very near future):
  Implement shock deceleration effects
  Trial for higher and lower resolution spectra
  Run for new synthetic air test data

## Slide 39
Thank you!