## Slide 1: Infrared FPA Detector Readout with the NIRCA MkII ASIC
AMICSA 2025, 16 – 18 June 2025, Lisbon, Portugal
Dirk.meier@ideas.no
On behalf of IDEAS team
A. Hasanbegovic, T. Ostmoe, A.Fagerland Haavik, D. Meier, B. Samadpoor Rikan, T. Nesjo, HK. Otnes Berge, A. Dadashi, S. Azman, J. Talebi, JE. Holter, P. Oya, G. Maehlum – IDEAS, Oslo, Norway –

## Slide 2: IR FPA Detectors, FEE, Camera Core and Applications in Space and on Earth
MCT, T2SL on ROIC
Cryogenic
Microbolometers, QD on ROIC
Power
Control
Analog
Video
Output
Power
Control
Digital
Video
Output
Detector
I/F
Cold
Warm
Camera
I/F
Space Science, Earth Observation
Industries, Automation, Safety

## Slide 3: NIRCA MkII Infrared FPA Controller Readout ASIC
A single-chip solution to bias, read out and control a focal plane array (FPA).
IR FPA with analog video out
Control and clocking
Biasing and supplies
Analog readout and digitization

## Slide 4: NIRCA MkII Infrared FPA Controller Readout ASIC
Programmable Sequencer Custom instruction set 16× Digital outputs 8× Digital inputs 2048 instructions (ECC-RAM) 8 nested loops, +++ Interfaces SPI serial peripheral interface 9×480 Mbps upstream LVDS (8b/10b) IRQ for exception, sequencer messages Analog Acquisition 16× 16-bit, 12 Msps ADCs Programmable gain - x1, x1.14, x1.33, x1.6, x2, x2.67, x4, x8 Analog input configurations: - Fully differential, - Pseudo differential, - Single ended Sample point adjustment (4+ ns steps) | Analog monitoring 1× 16-bit, 12 Msps ADC 3× analog inputs (muxed), Internal temperature sensor Bias and supply outputs 8× Ext. Vbias (w. 10-bit DACs) Output and ground sensing Environment SEL LETth > 118 MeV cm2/mg Good SEU tolerance -40°C to +85°C Power Less than 2W (flexible power- down scheme) Applications Earth observation missions Hybrid image sensors, IRFPA Astronomical science Space instrumentation
A single-chip solution to bias, read out and control a focal plane array (FPA).

## Slide 5: NIRCA MkII Process, IP and Floorplan (WS CIS 2022, ESTEC)
Fabricated in the UMC180
Using DARE 180U PLL, RAM (non-protected), CORE and IO library by IMEC
Otherwise, design IP by IDEAS

## Slide 6: Qualification – Electrical Tests (WS CIS 2024, Toulouse)
Environmental test conditions:
  [VTYP -10%, VTYP, VTYP +10%], [-40°C, 25°C, 85°C]
Test parameters:
  Input range, DNL, INL, Gain, Digital functionality, IO-tests, References, Current consumption, Rates ….
Data collection
  Test result database, PDF report generation
  Channel offset and gain tuning parameters
Tuning for target applications
  E.g., temperature range, input range, gain, offset

## Slide 7: Test Results – Flight Package (WS CIS 2024, Toulouse)
Package design and assembly successful
  ADC input noise 2.9 LSBRMS – 3.2 LSBRMS
  DNL < ± 0.3 LSB , INL < ± 1.5 LSB
  Max sampling frequency: 12 Msps
  Reference output noise: 10 µVRMS – 30 µVRMS
  Power 2W (16 ADCs @ 12 Msps)

## Slide 8: Test Results – ADC Channel Equalization (WS CIS 2024, Toulouse)
Preliminary channel equalizations using on-chip offset- and gain calibration
±1 LSB offset mismatch
±10 LSB gain mismatch
Ongoing work to further improve gain mismatch
Target is ±1 LSB gain mismatch
Vin = +1.5 V
Vin = -1.5 V

## Slide 9: Radiation Tolerance of NIRCA MkII ASIC
SEE
  Heavy ions, UCL:
    3.3 and 72.17 MeVcm2/mg
  3 devices
  => SEE rates =============>
  => No SEL detected
TID
  Co-60, ESTEC
    LDR to 76 krad (Si)
  5 biased, 5 unbiased, 1 reference
  => 5% drift in current consumption
  => No performance parameter drift
1 SEU with ±40 LSB error every 32000 frames for 1k x 1k @ 180 fps.
1 SEU with 1 ±150 LSB error every 1536000 frames for 1k x 1k @ 180 fps.
Shielding: 1 mm Al equivalent,
CREME96 (peak 5-minutes) solar particles (H – U) AP-8 MIN trapped protons

## Slide 10: IR FPA Detector Readout System DevKit
Step 1 (A): Make a harness to interface to the sensor
Step 1 (B): Make a proximity electronics board to interface to the sensor
Step 2: Use one of the provided examples as baseline for
sensor power and bias sequencing
control
readout
frame size, frame segmentation, number of frames
Step 3: Connect your monitoring devices to observe response
Step 4: Perform the image acquisition
IR ROIC readout wo. MCT. Laser pointer on die.

## Slide 11: IR FPA Detector Readout Emulation
Cooled IR FPA Detectors are expensive and non-trivial to operate. Detector interface details are under NDA.
Goal: Demonstrate NIRCA MkII and FEE performance with electronics only (no detector)
  Settling accuracy
  Crosstalk
  Dynamic range (def. signal/noiseRMS)
How: Proximity board used for generating fast switching levels (i.e., detector output emulation)
  Voltage levels between 0V – 3.3V
  Fully differential
  Pseudo differential
  Single ended

## Slide 12: Fully Differential Input – Settling
Key parameters | 
Gain | x1
Internal offset | Internal VCM
AIN+ | 0.6V - 2.25V
AIN- | 2.25V – 0.6V
Full-scale input | 3.3 Vpp, i.e.,2x1.65 Vpp
Sampling frequency | 12 Msps
Observations
  Excellent settling at 12 Msps
  Dynamic range can be > 20000:1 (> 86 dB) when full-scale input is above 4 Vpp
  Activating multiple simultaneously sampling ADCs of identical signals does not impact settling accuracy
Fully differential (FDIFF)
Results | 
High data noise | 3.48 LSBRMS
Low data noise | 3.52 LSBRMS
Dynamic range | 18561:1, 85.3 dB

## Slide 13: Fully Differential Input – Crosstalk
Key parameters | 
Gain | x1
Internal offset | Internal VCM
AIN+ | 0.6V - 2.25V
AIN- | 2.25V – 0.6V
Full-scale input | 3.3 Vpp
Sampling frequency | 12 Msps
Driven input victims | 3
Floating input victims | 5
Aggressors | 8
Aggressor full-scale input | 0-100%, with some taper
Observations
  Noise not impacted by 8 aggressors
  Averaging 1024 samples shows < 2 LSB impact, but no evident crosstalk pattern
Driven input victims
Floating input victims
Aggressors
Visualizing only a part of the 1024x1024 frame
Observe driven input victims only, non-driven are non-relevant
Average to “look into” the noise for crosstalk patterns
VADC0
VADC1
VADC2
VADC0
VADC1
VADC2
Readout direction
Notes: 8 aggressors acting on 8 victims

## Slide 14: Pseudo Differential Input – Settling
Key parameters | 
Gain | x1.6
Internal offset | srefp= 255, srefn = 85
AIN+ | 1V - 3.3V
AIN- | 1V
Full-scale input | 2.3 Vpp
Sampling frequency | 12 Msps
Observations
  Excellent settling at 12 Msps
  Larger full-scale input gives higher dynamic range
  Above results are with 7 aggressors active
Pseudo differential (PDIFF)
Results | 
High data noise | 5.5 LSBRMS
Low data noise | 4.5 LSBRMS
Dynamic range | 11214:1, 81 dB

## Slide 15: Pseudo Differential Input – Crosstalk
Key parameters | 
Gain | x1.6
Internal offset | srefp= 255, srefn = 85
AIN+ | 1V - 3.3V
AIN- | 1V
Full-scale input | 2.3 Vpp
Sampling frequency | 12 Msps
Driven input victims | 3
Floating input victims | 6
Aggressors | 7
Aggressor full-scale input | 0-100%
Observations
  Noise (single sample) slightly impacted by 7 aggressors
  Averaging 1024 samples shows ~ 8 LSB crosstalk patterns
  Signal conditioning and sample rate affects crosstalk.
Notes: 8 aggressors acting on 8 victims

## Slide 16: Pseudo Differential Input – Crosstalk
Key parameters | 
Gain | x1.6
Internal offset | srefp= 255, srefn = 85
AIN+ | 1V - 3.3V
AIN- | 1V
Full-scale input | 2.3 Vpp
Sampling frequency | 10 Msps
Driven input victims | 3
Floating input victims | 6
Aggressors | 7
Aggressor full-scale input | 0-100%
Observations
  Noise (single sample) not impacted by 7 aggressors
  Averaging 1024 samples shows ~ 8 LSB crosstalk patterns
  Signal conditioning and sample rate affects crosstalk. E.g., at 10 Msps, < 3 LSB crosstalk patterns are observed
Notes: 8 aggressors acting on 8 victims

## Slide 17: Single Ended Input – Settling
Key parameters | 
Gain | x1.33
Internal offset | srefp= 255, srefn = 32
AIN+ | 0V - 3V
AIN- | GND
Full-scale input | 3 Vpp
Sampling frequency | 12 Msps
Observations
  Good settling at 12 Msps, better at lower sampling rates
  Above results are with 7 aggressors active
  Single ended settling is sensitive to local ground shifts, therefore signal conditioning is beneficial (e.g., small cap between ADC inputs)
Single ended (SE)
Results | 
High data noise | 4.6 LSBRMS
Low data noise | 6.3 LSBRMS
Dynamic range | 10518:1, 80.4 dB

## Slide 18: Single Ended Input – Crosstalk
Key parameters | 
Gain | x1.33
Internal offset | srefp= 255, srefn = 32
AIN+ | 0V - 3V
AIN- | GND
Full-scale input | 3 Vpp
Sampling frequency | 12 Msps
Driven input victims | 3
Floating input victims | 6
Aggressors | 7
Aggressor full-scale input | 3x 0-100%, 4x 0-80%
Observations
  Noise (single sample) impacted by 7 aggressors – crosstalk pattern visible
  Averaging 1024 samples shows ~ 8 LSB crosstalk patterns
  Signal conditioning and sample rate affects crosstalk and care must be taken to avoid noise coupling to the input
Notes: 8 aggressors acting on 8 victims

## Slide 19: Front-End Electronics with NIRCA MkII
Front-End Electronics Breadboard
  32-channel readout
  Space-grade power management
  SpaceWire TM/TC
  Detector SEL protection
Detector Emulator
  8-channel emulation
  14-bit DACs
  Configurable output signal conditioning
Front-End Electronics EM
  In development, available in H1 2026
Front-End Electronics Breadboard
Detector Emulator

## Slide 20: Packaging and Qualification of NIRCA MkII
IDE8420X
Ceramic package for terrestrial applications
IDE8420E/S
Ceramic package for space applications
IDE8420, Chip-on-board
Aluminum lid, or molded
Radiation test
Wafer lot acceptance
Early EMs
Evaluation
Qualification ESCC9000 Q1 2026
FMs Q1 2026
completed
Planned and Ongoing

## Slide 21: Thank you
And thank you
… to ESA for supporting the NIRCA MkII related activities
… to industry partners for the collaboration