## Slide 1: Project Report NORM Norwegian Radiation Monitor for a long-term mission in highly-elliptical orbit
ESA Contract: 4000128542/19/NL/AS 2024-06-11 TEC-EPS Final Presentation Days

## Slide 2: Why NORM?
The need for more radiation data
Norwegian interest in research
Flight opportunity: Space Norway's Arctic Satellite Broadband Mission
At IDEAS, gain experience with designing and testing of space electronics in order to support our customers including ESA better
Advance the capabilities of this technology

## Slide 3: Project Objectives
To develop the Norwegian Radiation Monitor.
It produces data from which differential and integral flux data for energetic protons and electrons with low cross species contamination can be derived, as well as optional LET spectra.
Shall be suitable for use on many satellites, but in particular the ASBM mission with its unique TAP orbit.
At IDEAS, we planned to
reuse frontend readout electronics that were developed for the RADEM instrument on JUICE,
Make improvements in cost and detector noise thresholds,
Gain knowledge to support future customers better, by understanding the issues in the design of space electronics ans systems in more depth.

## Slide 4: At IDEAS, we develop and manufacture electronics for radiation detection
Radiation Imaging Systems
Frontend ICs for Radiation Detectors
Custom Mixed-Signal ASIC Development
For use in Industry, Scientific Research
Founded in 1992, we are based in Oslo, Norway.

## Slide 5: Integrated Detector Electronics AS
IDEAS SME in operation since 1992.
integrated circuits for image sensors (x-rays, gamma rays, charged particles, IR, thermal).
Systems for radiation imaging in space and on earth.
SWIFT | NASA | 2004 | BAT gamma-ray telescope and spectrometer
CREAM | NASA | 2004-2010 | High energy particle spectrometer onboard several balloon flights
AMS/AMS02 | NASA | 1997 / 2011 | Charged particle tracker
PAMELA | INFN | 2006 | Charged particle tracker
STEREO | NASA | 2006 | PLASTIC, Particle and ion Spectrometer
Super AGILE | INAF-IASF INFN | 2007 | Gamma-ray spectrometer
Chandrayaan-1 | ISRO | 2008 | HEX, High Energy gamma and X-ray spectrometer
FOXSI | NASA | 2014 | X-ray telescope/spectrometer
CALET | JAXA | 2015 | CALorimetric Electron Telescope
DAMPE | CAS | 2015 | DArk Matter Particle Explorer. High energy calorimeter and tracker.
ASTRO-H | JAXA | 2016 | SDG Soft Gamma-ray Imager HXI Hard X-ray Imager
Tiangong 2 | CAS | 2016 | POLAR gamma-ray spectrometer/polarimeter
ARASE/ERG | JAXA | 2016 | Electron spectrometer
ISS-CREAM | NASA | 2017 | High energy particle spectrometer attached to the International Space Station
ASIM | DNSC | 2018 | MXGS, Miniature X- and Gamma-Ray Sensor.
BepiColombo | ESA/JAXA | 2018 | MPPE instrument on MMO, BERM radiation monitor ELENA instrument
EDRS-C | ESA | 2019 | NGRM, Next Generation Radiation Monitor, electron and proton spectrometer.
SRG | SRI/VNIIEF/NASA | 2019 | ART-XC – Astronomical Roentgen Telescope – X-ray Concentrator.
JUICE | ESA | 2023 | RADEM Electron and proton spectrometer.
ASBM | Space Norway | 2024 | NORM Norwegian Radiation Monitor
Applications:
Radiation monitoring.
Particle and cosmic ray detection.
Gamma and x-ray astronomy.
Infrared astronomy.
Planetary science.
SWIFT Chandrayaan-1 AMS BepiColombo JUICE

## Slide 6: Project Partners

## Slide 7: NORM Specifications
Application Measuring kinetic energy for energetic charged particle radiation
Energy range Electrons: 0.5 - 7 MeV, 9 log bins Protons: 7 - 200 MeV, 9 log bins
Power consumption < 3W (target)
Weight 3 kg
Data interfaces MIL-STD-1553B, (CAN, others)
Radiation hardness 100 krad TID, 60+ MeV cm2/mg SEL
In orbit lifetime 5+ years in HEO
Input voltage range 25V – 37V (adaptable)
Credit for radiation belt: NASA Goddard
Credit for radiation belt: NASA Goddard

## Slide 8: Electronics Unit DHU + PSU
EM Detector stack + Readout PCB (ASIC) + EM housing
Model
Detector Unit DGU / Sensor
SAMV71-Evalboard + ASIC shield + Lab-PSU, SAMV71RH Eng. Board + 1553 Test HW
breadboard
Detector Diodes + 7085 FrontEnd Board
SAMV71RH, PSU, 1553 Bus on Design PCB, Eng. Components, Housing to Flight Design
EM
FM Detector stack
+ FM housing
EM with FM footprint RH components, non-certified, FM housing
EQM
As EQM with certified components, FM housing
FM
Test and Verification
Development on Breadboard Prototypes
Electronics Testing, MIL-STD-1553-BUS Testing Sensor Functional Test Mechanics (Vibration/Shock) and Noise-Testing Calibration (“Beam-Test”)
Thermal Vacuum, Vibration Testing, EMC/EMI Environment and Mechanics Design Verification Calibration (“Beam-Test”)
Flight Model Functional Testing Environment and Mechanics Acceptance Testing
PDR Jan 2020
CDR July 2020
QAR Jan 2021
Delivery May 2021
Phase B
Phase C1
Phase C2
Phase D
Kick-Off Summer 2019
FM Detector stack
+ FM housing

## Slide 9: Detector Unit
9x 500um Si detector diodes with 2 different active area diameters (8 and 12 mm)
Aluminum and tantulum absorbers.
Stack design based on simulation with GRAS/GEANT4

## Slide 10: NORM instrument hardware
Front face, detector stack
Data Handling Unit
Detector Unit
Image credit: IDEAS

## Slide 11: Detector Readout ASIC
IDE3466 ASIC [1]
Features:
  Radiation-hard 16 x 16 mm2 chip
  36 input channels (for Si detectors)
  Energy spectroscopy capability
  Pattern unit (coincidence)
  High-speed counters
  On-board calibration circuit
  SPI interface
Image credit: IDEAS
IDEAS IDE3466 chip.
IDE3466 block diagram.
Image credit: IDEAS
[1] T. A. Stein, et al., “Front-end readout ASIC for charged particle counting with the RADEM instrument on the ESA JUICE mission,” Proc. SPIE 9905, Space Telescopes and Instrumentation 2016: Ultraviolet to Gamma Ray, 990546 (19 July 2016). DOI: 10.1117/12.2231901

## Slide 12: Detection Scheme
Read out Electronics using the IDE3466 ASIC (as used in RADEM)
Discriminator with two threshold settings
Electron detection uses low threshold trigger in the coincidence patterns.
Proton detection uses both high and low threshold trigger in the coincidence patterns.
Counter sampled every 60 seconds.
Histogram for 9 electron and 9 proton bins.
Event rate 100k events/s per channel

## Slide 13: Readout
Counter Readout through the IDE3466 ASIC SPI interface
We also use an analog output for pulse-height spectroscopy and for calibration.
Notes: This uses the ADC to read the data
It is triggered by low thresholds

## Slide 14: ASBM Artic Satellite Broadband Mission
Norwegian communication satellites
  Full coverage of area above 65°N
  Operated by Space Norway
  15-year mission
  5 years nominal NORM operation
  Viasat communication payload
  On each orbit they cross the outer radiation belt
  NORM on one of the two satellites
Launch scheduled on July 15th, 2024, on a SpaceX Falcon 9 from Vandenberg SFB.
Credit: Northrop Grumman

## Slide 15: ASBM Artic Satellite Broadband Mission
HEO: Three-Apogee Orbit, TAP
16h, 8746 km × 42878 km, 62.3°

## Slide 16: Radiation Environment
Protons > 10 MeV
Electrons > 1 MeV

## Slide 17: Project Timeline
Preliminary Design
Summer 2019 – January 2020
EM Design and Manufacturing
Feb. 2020 – Nov. 2020 Testing Dec. 2020.
CDR in Feb. 2021
What had happened?
  A few unanticipated problems
  COVID

## Slide 18
PCB Manufacturing
Mechanics Manufacturing
PCB assembly EQM
EQM AIT
FM Thermal, Vibration, EMC/EMI, Communication Test
QAR
Delivery
EQM Functional and Calibration (“Beam-Test”)
PCB assembly FM
FM AIT
One PCB rerun
June 2021
Dec 2021
Jan 2022
FM Functional and Calibration (“Beam-Test”)
Feb 2022
April 2022
EQM TVAC, Vibration Communication Testing
Sept. 2022
Sept. 2021
EQM EMC Test
August 2022

## Slide 19: Manufacturing
PCBs manufactured by Invotec
PCB assembly done by Spur, UK
Mechanics manufactured in Norway by FFI

## Slide 20: AIT

## Slide 21
Calibration at PSI

## Slide 22: Vibration testing

## Slide 23: EMC Test @ESTEC

## Slide 24: Test results: thresholds, muons

## Slide 25: Simulation of the Test

## Slide 26: Test results (2)
Beam testing shows instrument is working as expected.
51.2 MeV protons

## Slide 27: Test results (3)

## Slide 28: Results
Designed and manufactured the instrument
3 Models in < 3 years
During COVID
Preparation of final reports took longer
Launch of ASBM planned for July 15th
Usable in other missions as well
Detector stack is tunable if needed
(we are working on follow-on)
Photo: Northrop Grumman

## Slide 29: Flight on ASBM
Launch not part of the ESA contract
We set up a system to decode the telemetry and encode telecommands to the instrument.
With SPARC we developed software to provide Level 1 data
Data to be made available upon request
Example: Bow-tie analysis: integral electron fluxes (FEIO)
Launch next month

## Slide 30: Any Questions
Image: JWST/NASA,ESA,JAXA

## Slide 31: Thank You
Team behind NORM (alphabetical order):
Codin Gheorghe, Anja Kohfeldt, Gunnar Maehlum, Dirk Meier, Anders Olsen, Torbjørn Østmoe, Petter Øya, Christophe Plaissy, Timo Stein
Contact: sebastian.benoit@ideas.no