## Slide 1: ResNet50-based testbench development for the SEE evaluation of the AMD Versal SoC AIEngines
S. Achaq1,2, V. Pouget2, L. Artola1, J. Boch2
1, ONERA, Toulouse, France. 2, IES, Univ. Montpellier, CNRS, Montpellier, France.

## Slide 2: Context & motivation
Technological context
Are AI based embedded systems reliable in space radiation environments ?
Reliability ?
The rapid rise of embedded artificial intelligence (AI) systems
  Artificial Neural Networks (ANNs)
New generation of System-on-Chips (SoCs) for edge-AI
  AMD-Xilinx Versal: Programmable SoC including AI-accelerator cores
Evolution of embedded systems computation capabilities
  Autonomous decision, on-board data processing…
7nm FinFET technology
Space Radiation Environment
Radiation-induced Single event effects
(SEE)
SEU, MCU, SEFI

## Slide 3: Context & motivation
SEE test of an embedded-AI application on the AMD-Xilinx Versal AICore series 7nm FinFET SoC:
  ResNet50 convolutional Neural network (CNN) as a case study
  Laser testing of adaptive intelligence engines (AIEs)
    Investigate the sensitivity of AIE resources running a CNN
    Study the impact of SEE in a CNN hardware accelerator

## Slide 4: Outline
Target device
AIEngine resources
ResNet50 CNN
  Principles
  Implementation in Versal
  Test challenges
  Test methodology
Summary

## Slide 5: Target device
Application processing unit (APU)
Dual-core
Arm Cortex-A72
Real-Time Processing unit (RPU)
Dual-Core
Arm
Cortex-R5F
Platform management Controller (PMC)
Programmable logic
(PL)
AI Engines
Programmable Network on Chip (NoC)
Scalar Engines
AMD Xilinx Versal AICore SoC
Versal AI-Core System-on-Chip
  7nm FinFET technology
  Complex monolithic SoC, embedding:
    Multiple processing cores (PS)
    Configurable FPGA-like logic (PL)
    Network-on-Chip (NoC)
    AI dedicated engines: array of 400 cores, each with local dedicated memory
      GMIO interface to NoC/DDR
Notes: Nm processThe device under cores suited for intensive computations

## Slide 6: Target device
PS
AIEngines
PL
25.4mm
17.7mm
Versal AI-Core System-on-Chip
  7nm FinFET technology
  Complex monolithic SoC, embedding:
    Multiple processing cores (PS)
    Configurable FPGA-like logic (PL)
    Network-on-Chip (NoC)
    AI dedicated engines: array of 400 cores, each with local dedicated memory
      GMIO interface to NoC/DDR

## Slide 7: Target device
AIEngines
Ultra-RAM
PL
PS
AI Engine tile
Versal AI-Core System-on-Chip
  7nm FinFET technology
  Complex monolithic SoC, embedding:
    Multiple processing cores (PS)
    Configurable FPGA-like logic (PL)
    Network-on-Chip (NoC)
    AI dedicated engines: array of 400 cores, each with local dedicated memory
      GMIO interface to NoC/DDR

## Slide 8: AIEngine resources
AI Engine Tile:
  AI Engine core
    VLIW processor
    16 KB program memory
  Integrated data memory
    32 KB local memory
      8 memory banks
  Interfaces
    Memory interface
    AXI4 stream interface
465μm
502μm
Bank 3
Bank 1
Bank 0 (ECC)
Bank 2
Instruction memory
Memory blocks in the manufacturer tool
Instruction memory - 16KB
Memory Bank 0 - 8KB
DMA
Control
Switch
Memory Bank 1 - 8KB
Memory Bank 2 - 8KB
Memory Bank 3 - 8KB
Hardware architecture of an AIEngine
AI Engine Tile
Memory module
AXI4 interconnects
AI Engine core
DMA
8 Memory banks
4KB
4KB
4KB
4KB
4KB
4KB
4KB
4KB
Program Memory
16KB
Memory interface
North
South
East
West
Scalar unit
Vector unit
VLIW processor

## Slide 9: ResNet50 CNN - Principles
Key features of ResNet50 Convolution Neural Network (CNN):
  Designed to efficiently train very deep models using residual connections
  Strong performance in image classification tasks
  Based on convolution operations
Architecture overview:
  Consists of 4 stages
  Each stage contains between 3 and 6 residual blocks
  Each residual block consists of convolutions and a skip connection
8.78 106 2D-convolution operations
Batch_norm
Batch_norm
Residual block input
CONV
CONV
CONV
RELU
CONV
RELU
RELU
RELU
Residual block
Residual block output
Batch_norm
Batch_norm
Batch_norm
Batch_norm
Residual connections
Stage 1
Stage 2
Stage 3
Stage 4
Each stage contains between 1 and 6 residual blocks.

## Slide 10: Embedded ResNet50 - Implementation in Versal
Our objectives:
  Testability, observability and AIE workload modularity
  Not performance!
Design choices
  Bare-metal code running on PS
  Using float32 data
    Weights : 80 MB
  Mostly software-based bench
    No use of PL (no proprietary IP)
  Acceleration of the most computation intensive operations
    ResNet50 convolutions layers and additions delegated to AIEngines
    Data segmentation and parallelizing of operations in an AIEngine graph with multiple identical branches
Embedded ResNet50 application
PS
AIEs
Conv + add operations
Running ResNet50
Delegating Conv operations to AIEs

## Slide 11: Embedded ResNet50 - Implementation in Versal
AIEs hardware configuration:
  Custom AIE graph architecture
Data dispatch AIEs
Conv AIEs
Addition AIEs
D
D
D
C
A
A
A
GMIO IN
GMIO OUT
1
2
4
8
4
2
1
Data flow
One branch of the AIE Graph
22 AIEs used

## Slide 12: Embedded ResNet50 - Implementation in Versal
Customizable AIEs occupancy
  Up to 16 branches can be implemented, using 352 AIEs out of the 400 available
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT
D
A
GMIO IN
GMIO OUT

## Slide 13: Embedded ResNet50 - Implementation in Versal
Customizable AIEs occupancy
  Up to 16 branches can be implemented, using 352 AIEs out of the 400 available

## Slide 14: Embedded ResNet50 - Implementation in Versal
AIEs software configuration
  Each used AIE executes a C++ kernel
    Dispatch kernel
      Dispatch input data including header of parameters needed by conv+add operations
    Convolution kernel
      Read convolution loop parameters from the header
      Calculate convolutions on data
    Addition kernels
      Calculate post-convolution additions
D
C
A

## Slide 15: Embedded ResNet50 - Software application overview
ResNet50 application
Convolution layer operations
x N data segments
x N layers
Pooling functions
Activation functions
Batch normalization
Delegation to AIEs
Input data transfer
AIE graph execution
Output data transfer
Fully connected layer calculations
CLASSIFICATION RESULT
Network construction
Weights & bias loading
Input images loading
Executed by one of the PS APU cores

## Slide 16: Embedded ResNet50 - Software bench overview
Test bench:
  Self test approach
  ResNet50 application is executed
  Outputs gold data is generated during the first execution
    Saved to the SD card
  Outputs are verified at:
    Layer level
    Classification results level
bench
ResNet50 application
Intermediary outputs verification
Classification outputs verification
Outputs gold data generation
First test iteration?
Yes
Send error reports
Send error reports
No
X N test iterations

## Slide 17: Embedded ResNet50 - Software bench overview
The main test-loop is executed by one of the CortexA72 cores In the PS APU
One CortexR5 core is in charge of reporting AIE errors
The other CortexR5 core collects the error reports generated by the XilSEM
All status and error reports are transmitted to the test computer by a TCP/IP stack running on one of the CortexA72 cores.
The AIE graph is executed by AIEngines array
A python script to:
  Initialize the DUT configuration through JTAG
  Log DUT reports
  Detect high current events, freezes and communication losses
VCK190 Development board
AMD Xilinx Versal AI Core
PS
PL
SysMon
CortexA72-0
Ethernet communications
CortexA72-1
ResNet50 application
CortexR5-0
XilSEM reports
CortexR5-1
AIE reports
AI Engines
AIE graph
DUT test script (python)
Watchdogs
Power supply current
Communication flow
Data logging
DUT config

## Slide 18: Embedded ResNet50 – Test challenges
Sample backside preparation:
  Heatsink removed
  Substrate backside polished
  Substrate thickness: 690 µm
Dissipation of DUT self-heating during test operations using:
  A constant air flow at ambient T°
    Thermal runaway
Test Board
Dev Board

## Slide 19: Embedded ResNet50 – Test challenges
Implemented Solution:
  Custom heatsink adapted for AIEs laser test
    Opening on AIEs
  Temperature stabilized at 80 °C
    No thermal runaway during test
Test board with custom heatsink

## Slide 20: Embedded ResNet50 – Test methodology
VCK190 Development board
AMD Xilinx Versal AI Core
PULSWORKS (laser scanning software)
Events mapping
Scan execution
Device under test
Laser tests performed at IES
  Single-Photon Absorption (SPA)
  Through the substrate backside
The implemented graph consists of 176 AIEs
  8 branches
Test script (python)
Events reporting & scan control
DUT test
Board Power Supply
Laser parameters:
wavelength: 1064nm (SPA)
pulse duration: 30ps
spot size ( 1/e²): 1.1µm

## Slide 21: Embedded ResNet50 – First logs
Logs examples:
Intermediary errors logs
Classification errors logs

## Slide 22: Summary
Versal implementation methodology of a SEE test-oriented embedded ResNet50 application is detailed
ResNet50 application integration in a ResNet50 test bench is presented
  Delegation of operations to AIEs
  Bench modularity
Laser tests in progress:
  Testbench validated experimentally for laser testing
  First convolution and classification errors observed
  More results to be submitted to RADECS