## Slide 1: Ultra-Fast, Low-Overhead SpaceFibre Communication for System-on-Chips
Dave Gibson, Andrew MacLennan, Stuart Mills, Steve Parkes, Albert Ferrer Florit and Alberto Gonzalez Villafranca
STAR-Dundee
European Data Handling & Data Processing Conference 2025

## Slide 2: SpaceFibre
Very high-performance:
  6.25 Gbit/s per lane and higher depending on the SerDes
Multi-lane capability:
  For example, a quad-lane link at 6.25 Gbit/s per lane gives 25 Gbit/s
  Maximum of 16 lanes
  Graceful degradation on lane failure
  Asymmetric traffic supported with unidirectional lanes

## Slide 3: SpaceFibre
Runs over electrical or optical cables:
  Few m electrical
  100 m fibre optic
Low-latency broadcast messages:
  Time-distribution
  Synchronisation
  Event signalling
  Error notification
STAR-Tiger 10-Port SpaceFibre Routing Switch
100 Gbit/s bi-sectional bandwidth

## Slide 4: SpaceFibre
Novel quality-of-service:
  Up to 32 virtual channels
  Bandwidth reservation, priority and scheduling
Virtual networks:
  Constructed with virtual channels
  Acting as independent networks over a single physical network
Inbuilt fault detection, isolation and recovery:
  At the link level enabling rapid error recovery
  Babbling node / virtual channel protection
  Graceful degradation of multi-lane links
Image from Airbus Pléiades Neo 3 transferred using SpaceFibre

## Slide 5: SpaceFibre
Small footprint:
  Taking a few percent of a recent radiation-tolerant FPGA
Straight forward to integrate with existing SpaceWire equipment
Flying on at least 6 operational satellites
Being designed into around 60 others
Image from Airbus Pléiades Neo 3 transferred using SpaceFibre

## Slide 6: RDMA Over SpaceFibre
Remote Direct Memory Access (RDMA) Over SpaceFibre:
  Demonstration running on AMD Zynq UltraScale+ SoC and PetaLinux
  Over 20 Gbit/s with < 1% CPU
25 Gbit/s
0 Gbit/s
Data Rate
CPU Utilisation
0 %
10 %

## Slide 7: RDMA Over SpaceFibre Demo
RDMA Target
RDMA Initiator
Graphics System
Frame Buffers
Application
FB 0 / MR 0
FB 1 / MR 1
DisplayPort Interface
DisplayPort Monitor
RDMA Controller
SpaceFibre Interface
Image 0
Image 1
Image 2
Image 3
Image 4
Image 5
…
Image 581
Graphics Demo (PetaLinux)

## Slide 9: SpaceWire and SpaceFibre Processor Endpoint
Kernel-Space
Uses similar techniques to RDMA Over SpaceFibre:
  Hardware-acceleration
  Minimal CPU overhead
Simple and rapid integration for software-based systems
Supports any packet format
User-Space
SoC PL / FPGA
SpaceWire Port
SpaceWire Port
SpaceFibre VC
SpaceFibre VC
SpaceFibre VC
Data Transfer
Processor Endpoint IP
STAR-Core Drivers (Platform and PCIe)
STAR-Core APIs

## Slide 10: SpaceWire and SpaceFibre Processor Endpoint
Support for SoCs:
  Linux platform driver and PS-to-PL interface
Support for FPGAs:
  Linux PCIe driver and PCIe interface
Kernel-Space
User-Space
SoC PL / FPGA
SpaceWire Port
SpaceWire Port
SpaceFibre VC
SpaceFibre VC
SpaceFibre VC
Data Transfer
Processor Endpoint IP
STAR-Core Drivers (Platform and PCIe)
STAR-Core APIs

## Slide 11: SpaceWire and SpaceFibre Processor Endpoint
PolarFire (MPF300 Eval Kit)
SpaceFibre Processor Endpoint
1 x SpFi (1L, 6.25 Gbit/s)
SFP+
Intel i5-9600 CPU
Linux Mint
Example of PCIe-based endpoint:
  Processor Endpoint in standalone FPGA (Microchip PolarFire MPF300)
  Connected to software in external processor using PCIe driver (Intel i5-9600 CPU)
  SFP+ connected to SpaceFibre network
PCIe

## Slide 12: SpaceWire and SpaceFibre Processor Endpoint
Zynq UltraScale+ MPSoC (ZCU102)
PL
SpaceFibre Processor Endpoint
1 x SpFi (4L, 7.5 Gbit/s)
4xSFP+
Example of SoC-based endpoint:
  Processor Endpoint in SoC PL (AMD Zynq UltraScale+ ZCU102)
  Connected to software in SoC PS using platform driver (ARM Cortex-A53 CPU)
  4xSFP+ connected to SpaceFibre network
PS
ARM Cortex-A53 CPU
(PetaLinux 2022.1)
Test PC
STAR-Ultra PCIe
QSFP+

## Slide 13: Performance Testing (Setup)
Processor endpoint:
  AMD ZCU102
  ARM Cortex-A53 CPU
  PetaLinux 2022.1
Test PC:
  STAR-Ultra PCIe
  Intel i9-9900 CPU
  Windows 11 Pro
SpaceFibre:
  4 x 7.5 Gbit/s lanes
  30 Gbit/s link

## Slide 14: Performance Testing (Procedures)
Send performance tests:
  Send packets from Processor Endpoint (ZCU102)
  Receive packets on STAR-Ultra PCIe
Receive performance tests:
  Send packets from STAR-Ultra PCIe
  Receive packets on Processor Endpoint (ZCU102)
Packet sizes from 1 KB to 256 KB
Perform 10 iterations of 10 seconds for each size
Measure data rate and CPU utilisation

## Slide 15: Send Performance (Single Packets)

## Slide 16: Send Performance (Grouped Packets)

## Slide 17: Receive Performance (Single Packets)

## Slide 18: Receive Performance (Grouped Packets)

## Slide 19: Future Testing
Performance testing of SpaceFibre Processor Endpoint on AMD Versal SoC to support 100 Gbit/s+ SpaceFibre
A. Gonzalez Villafranca, A. Ferrer Florit, M. Farras Casas and S. Parkes,
“SpaceFibre IP Cores for Fast Adoption of Next-Gen FPGA Communication Architectures”,
IEEE Aerospace Conference, Big Sky, USA, March 2025

## Slide 20
Thank you for your attention Any questions?
https://www.star-dundee.com/