## Slide 1: 100 Gbps SpaceFibre on Space-Qualified FPGAs Albert Ferrer, Alberto Gonzalez, Marti Farras Steve Parkes STAR-Barcelona SL STAR-Dundee Ltd
EDHPC 2025
STAR-Dundee © - EDHPC 2025

## Slide 2
Current SpaceFibre links, using 8b/10b encoding, reach practical limits around 10 Gbit/s per lane
Some next-generation missions demand even higher onboard data rates
Modern FPGAs like Versal offer up to 25 Gbit/s per lane (112 Gbit/s commercial), enabling faster links
Objective is to upgrade SpaceFibre encoding to support >6.25 Gbps lane with minimum changes to the standard
  Existing implementations can be easily adapted to operate at both legacy and enhanced speeds
  Scrambling-based schemes (e.g. 64b/66b) reduce encoding overhead and improve spectral balance
Motivation
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
SpFi Link
8b10b
Encoding
New
Encoding
<10 Gbps
>10 Gbps

## Slide 3
High performance
  Runs without SW intervention
  Virtual channels handle multiple data flows
  Any packet size / No segmentation required
Why SpaceFibre?
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
OSI Data Link Layer protocols
High reliability
  Reliable link with link-level flow control
    Link-layer error recovery in 2us
  Multi-lane redundancy
    Graceful BW degradation on lane failure
    Hot and warm redundant lane
  Quality of service
    Bandwidth reservation, priority and scheduling
Designed for Space Applications
  SW compatible with SpaceWire
  Multi-lane with unidirectional lanes
  Efficient implementation on radiation tolerant FPGAs
9xSpW
1xSpFi

## Slide 4
Use of scrambling-based encoding schemes
  Bit streams are statistically DC balanced
  Uniform spectral properties facilitate adaptive equalization at higher rates
64b/66b encoding was selected among other options (e.g. 128b/130b, 256b/257b)
  Encoding overhead reduction from 20% down to 3.125%
  Low latency with a small 66-bit block size
  Explicit 2-bit header
    Faster block alignment than using periodic alignment patterns
    Guaranteed bit transition every 66 bits (run length)
  Native transceiver support in radiation tolerant FPGAs
Line Encoding
STAR-Dundee © - EDHPC 2025
1 0
D0 D1D2 D3D4 D5D6 D7
Control Block
scrambled
0 1
D0 D1D2 D3D4 D5D6 D7
Data Block
scrambled

## Slide 5
8b/10b encoding detects all single-bit errors and a subset of multi-bit errors
64b/66b provides no built-in error detection capability
  Additional integrity check is required
A 32-bit CRC is added to each 32-bit SpFi control word covering previous data words since the preceding CRC.
Error Detection
Control Word
Data Word
Data Word
Data Word
Data Word
Control Word
32-bit SpFi words
Data Word
Data Word
Data Word
Data Word
Control Word
64-bit blocks
32-bit CRC
Control Word
32-bit CRC
CRC coverage

## Slide 6
Block Diagram

## Slide 7
SpFi words have four characters
  Can be Data or Control characters
  Control characters have the 8b/10b K-flag set
SpFi control words
  First character is a Control character
SpFi data words
  Have control characters (EEP, EEP, FILL) at the end of a packet
  The end of a packet can start at any of the four characters
SpaceFibre Words
C
D
D
D
F
E
F
D
D
D
F
D
F
D
E
F
E
D
D
F
D
D
D
E
K-Flags
Data Bytes

## Slide 8
Transcoder TX
End of Packet ?
No
Data Block
Data Word
Data Word
Control Word
Control Block with
Control Word and CRC
Control Block with Data Words
First byte describe the type of packet ending (EOP/EEP/FILL)

## Slide 9
Transcoder RX
Data Block
Data Word
Data Word
Control block
Control Word
Data Word
Data Word
First two bits indicates if is a control word or a data word with end of packet

## Slide 10
CRC Block
32-bit CRC field appended to each control block that contains a SpFi control word
CRC-32 polynomial defined in IEEE 802.3
CRC-32 detects
  All one-bit, two-bit, and three-bit errors
  All burst up to 32 bits in length
  Any pair of burst errors up to eight bits each
CRC does not cover the 2-bit sync header
  Invalid control blocks have random invalid CRC
  Invalid data blocks will be detected in the CRC of the next control word

## Slide 11
Block Sync
The block synchronizer detects where the header is located in the incoming 66-bit stream
Two consecutive bits are checked
  Header bits can only be “01” or “10”.
  Scrambled bits can be “01” or “10” or “11” or “00”
If “11” or “00” is found, check next bit position
After 64 consecutive “01” or “10”, block lock is considered correct
scrambled
scrambled
scrambled
Check two consecutive bits here
Shift until lock found

## Slide 12
Hardware Validation
Implementation in radiation-tolerant Versal and PolarFire
Resource usage of the new encoding blocks at maximum transceiver lane rates
Heavy-ion radiation testing of 4-lane 100 Gbps links with VCK190 Evaluation Kit

## Slide 13
Conclusions
SpaceFibre updated to 64b/66b to achieve higher data rates (e.g. 100G)
  Limited modifications to the standard enables backwards compatibility
  Transcoding block maps SpaceFibre 8b/10b codes into 64b/66b blocks
    With minimal logic and power overhead
  Validation in HW with radiation testing on Versal
SpaceFibre advantages
  No limit on packet length -> No segmentation required
  Reliable link -> mitigates high BER and SEEs
  Can work without software -> Simpler, more robust
  QoS with multiple Virtual Channels -> Simple decoupling of data flows
  Link flow control -> Transmit reacts to dynamic receiver behaviour
Future work focus on forward error correction (FEC) for >25 Gbps per lane