## Slide 1: Effective, Robust TCP/IP over SpaceFibre Albert Ferrer, Marti Farras Steve Parkes STAR-Barcelona SL STAR-Dundee Ltd
EDHPC 2025
STAR-Dundee © - EDHPC 2025

## Slide 2: Overview

## Slide 3
SpaceFibre designed for space applications
  Reliable
    Link layer error recovery
    Multilane redundancy
  Flexible
    Arbitrary lane rate, packet format and size
    Virtual Networks with QoS decouple different data flows
    Works without software
    Implemented in multiple radiation-tolerant FPGAs
Leverage commercial HW and SW in space applications
  Use COTS processors with Ethernet interfaces
  Use standard OS network stack and related applications (e.g. FTP)
Motivation
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 4
Use COTS SW and HW with the development of:
Virtual Network Interface that handles:
  IP traffic (e.g. TCP/UDP)
    Carried by Ethernet Frames
  SpFi native traffic (e.g. RMAP)
    Using UDP sockets
SpaceFibre Router with Ethernet ports
  Bridges SpaceFibre and Ethernet at link layer
    Simpler, no IP layer processing required
    Support raw Ethernet frames and TCP/IP
Proposed Solution
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 5: SpaceFibre Router with Ethernet ports

## Slide 6
The Ethernet frames from the COTS processor are encapsulated into SpFi packets by the Ethernet port of the SpFi Router
IP Traffic: COTS Processor to SoC FPGA
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
At the destination, the virtual network interface of the SoC FPGA decapsulates them into Ethernet frames, which are then processed by the standard OS network stack

## Slide 7
The network interface of the SoC FPGA sends SpaceFibre packets containing Ethernet frames
IP Traffic: SoC Processor to COTS FPGA
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
The SpFi packets are routed to the Ethernet port, which decapsulates the Ethernet frames, so they can be forwarded to the COTS Processor

## Slide 8
The virtual network interface of the COTS Processor encapsulates the SpFi packets into Ethernet frames
SpaceFibre Traffic: COTS Processor to Standalone FPGA
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
The Ethernet Frames are then decapsulated by the Ethernet port and routed to the destination FPGA

## Slide 9
The SpaceFibre packets arrive at the Ethernet port, which encapsulates them into Ethernet frames
SpaceFibre Traffic: Standalone FPGA to COTS Processor
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
The network interface of the COTS processor obtains the application data, e.g., RMAP read reply, from the encapsulated SpFi packets

## Slide 10
“Start Flags” and “Sequence” fields detect if an Ethernet frame was lost
  Provides data integrity by truncating an outgoing SpFi packet with an EEP
“Length” field used only when there is Ethernet frame padding
  When payload length being smaller than the minimum (48 bytes)
SpaceFibre Packet Fragment within Ethernet Frame
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 11
Direct mapping between a MAC address byte to the SpFi address byte
  If MAC values can not be configured, then a look up table is necessary
MAC Format: 02:00:XX:XX:LA
  02: unicast traffic and locally administered MAC
  00: Ethernet port identifier
  XX: Don’t care
  LA: SpaceFibre Logical Address
A MAC address is assigned to each Ethernet port of the SpFi Router
  Sets the source MAC address of Ethernet frames created to encapsulate SpFi packets
MAC Address Translation
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 12
Ethernet port bridging logic implemented on a radiation-tolerant PolarFire FPGA (RTPF500ZT) without including an Ethernet MAC IP
Implementation Results
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
Performance test on a SpFi Router implemented in a Versal
  The Ethernet MAC IP was replaced with a loopback logic
  STAR-Ultra is sending at 5 Gbps:
    SpFi packets with 3 KB of raw data
    SpFi packets carrying Ethernet frames

## Slide 13: Virtual Network Interfaces

## Slide 14
Allows user applications to exchange both IP-based traffic and native SpaceFibre packets through standard TCP/UDP sockets
When an application opens a TCP or UDP socket, the OS stack generates the corresponding IP packets and forwards them to the appropriate virtual interface, depending on the source and destination IP address of the socket configuration
Each virtual interface is configured with an IP address (or subnet) and a maximum transmission unit (MTU)
  The MTU defines the maximum packet size supported by the interface
    OS network stack handles fragmentation
Received packets from SpFi or Ethernet are decapsulated, reconstructed as IP packets, and injected back into the OS stack
Virtual Network Interface
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 15
Unified Network Stack
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
IP traffic and SpFi traffic have different IP subnets and associated network interfaces
IP traffic is always encapsulated in an Ethernet frame
SpFi Traffic applications use the UDP protocol
QoS: each SpFi Virtual Channel or Ethernet PCP can be assigned to a different Virtual Network Interface
A network interface use a particular HW Device Driver (SpFi or Ethernet)

## Slide 16: Evaluation

## Slide 17
Virtual network interfaces are implemented as TUN interfaces
  TUN kernel driver exposes IP packets from the network stack through R/W file descriptors
  The functionality is implemented in a user-space process using these file descriptors
Hardware and Software Setup
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
PC with Ethernet
PC with SpFi STAR-Ultra
Router config port
Versal
Flexible HW setup
  SpFi Router implemented in a Versal
  SW-based endpoints are Linux PCs with SpFi and Ethernet interfaces
  Router Configuration port used to test RMAP commands

## Slide 18
Direct translation is used between IP, MAC and SpFi logical addresses
  Simple and easy to use
    <VN> is the SpFi virtual network number (similar to Ethernet VLAN)
    <LA> is the SpFi destination logical address
IP traffic: 10.100.<VN>.<LA>
SpFi traffic: 10.100.<VN+128>.<LA>
Each SpFi or Ethernet endpoint is assigned a unique SpFi LA
  Common identifier across all network layers (SpFi, MAC, IP)
IP Adress Translation
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 19
Example Results: IP Traffic over SpFi/Ethernet
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
IP packet received from a SpFi link
  SpFi protocol ID is 0xEE (Ethernet Frame)
  IP payload after Ethernet and IP headers (0x00, 0x01, 0x2…)
File transfer with FTP between two endpoints, across a network with both SpFi and Ethernet links

## Slide 20
Example Results: SpFi Traffic over SpFi/Ethernet
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.
Python script sends RMAP read command with a UDP socket
RMAP reply received over Ethernet as seen by Wireshark software

## Slide 21
COTS Processors with Ethernet links are easily integrated into a SpaceFibre network
  HW-based bridge logic integrated in the SpaceFibre Router
TCP/IP and related commercial SW can use SpaceFibre links
Solution is based on:
  SpaceFibre Router upgraded with Ethernet ports
  Virtual Network Interfaces handles both IP and native SpFi traffic
Get the best of both worlds
  Commercial technology can leverage SpaceFibre capabilities for Space Applications
    Reliable link and lane redundancy handles radiation events
    Flexible packet length and format avoids segmentation and header parsing
    Link level flow control allows transmitter to react to dynamic receiver without loss
    Virtual Networks with QoS make system integration simpler
    Broadcast messages natively support redundant topologies
Conclusions
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.

## Slide 22
Visit our booth
and see our demo!
STAR-Dundee © - EDHPC 2025
Next-generation missions with complex payloads demand much higher data rates.