## Slide 1
ESA’s Distributed Space weather Sensor System (D3S)
Melanie Heil,
Space Weather Space Segment Coordinator,
ESA/ESOC
Spacemon 2025, ESA/ESTEC
11/06/2025

## Slide 2
Space Weather protection for Europe
Space weather monitoring system
Resilient society
Tailored space weather services
Early warnings with actionable information
Developments
Ground & space measurements
Impact studies
Cost Benefit Analysis
Focussed tools and apps
Awareness and user engagement
Space Weather @ ESA

## Slide 3
L5
L1
Missions to solar wind
NGRM on EDRS-C
SOSMAG on GK-2A
Aurora
NanoSats
ICARE-NG on GEO-Sat
Impact & state
monitoring
Ground based measurements
+
D3S:
Hosted Payloads
Small missions
Forecasting
&
Event detection
ESA’s Enhanced Space Weather
Monitoring System

## Slide 4
Distributed Space weather Sensor System (D3S)
GOES-West
Himawari
MTG
Objective
Monitoring of the ”Earth space” environment
Near-real time data for operational applications
Cost effective implementation through small missions and data buy from commercial actors
Missions Overview:
Aurora
Nanosat constellations
SWORD
SHIELD
Hosted Payloads
ERSA, Lunar Pathfinder

## Slide 5: Active hosted payload missions
SOSMAG on GK2A:
Launched end 2018
near-real time magnetic field measurement in GEO
GOES-West
Himawari
MTG
https://swe.ssa.esa.int/sosmag
Continuation through SOSMAG-II on GK5 in planning!

## Slide 6: Active hosted payload missions
NGRM on EDRS-C:
Launched mid 2019
Near-real time energetic particle flux measurements (electrons: 0.15-3 MeV, protons: 4-200 MeV) in GEO
https://swe.ssa.esa.int/ngrm
GOES-West
Himawari
MTG
142.5 E
MTG-I1 data to be released this summer!

## Slide 7: Active hosted payload missions
ICARE-NG on HOTBIRDs:
Launched fall 2022
Near-real time energetic particle flux measurements (electrons: 0.5-2.5 MeV, protons: 10-200 MeV)
GOES-West
Himawari
MTG
https://swe.ssa.esa.int/icare-ng

## Slide 8: D3S: Cislunar Hosted Payload Missions
MiniRMU on Lunar Pathfinder
  Monitoring of high energy electrons and protons (sensors identical to NGRM)
  Planned launch in late 2026
ERSA on Lunar Gateway
  Comprised of several radiation monitors (NGRM, ICARE-NG, SREM), dosimeters (Hardpix, EADs) and magnetometers (MAGIC)
  Close collaboration with NASA solar physics HERMES payload
  Planned launch NET 2027
Notes: (sensors identical to NGRM)

## Slide 9
Space Weather – D3S – Hosted Payloads
Several hosted payload missions ongoing and additional in implementation
Many HP missions in intern. collaboration coming up: radiation monitors on all Meteorological missions (6xMTG, 6xMetop-SG)
Level 1 data provided through space weather portal
Future plans:
  Continued cooperation with KMA on GEO space weather suite: SOSMAG-II to fly on GK5 in 2029/30
  High energy particle instrument for NOAA L1 mission
  Potential collaboration on Korean L4 mission and
  In-orbit demonstrations of new instruments on commercial missions
Instrument | Hosting flight | Orbit (altitude in km / longitude in º) | Launch Date | Mission Lifetime
SOSMAG | GK-2A | GEO (128° East) | 2018 | 10 years
NGRM | EDRS-C | GEO (31° East) | 2019 | 10 years
NGRM | Sentinel-6-A | LEO (1336 km, 66° incl) | 2020 | 7 years
ICARE-NG | HB 13F | GEO (13° East) | 2022 | 10 years
ICARE-NG | HB 13G | GEO (13° East) | 2022 | 10 years
NGRM | MTG-I1 | GEO (0°) | 2022 | 8.5 years
NGRM | MTG-S1 | GEO (0°) | 2025 (planned) | 8.5 years
NGRM | MOS A1 | LEO (~830 km, SSO) | 2025 (planned) | 7 years
NGRM | MOS B1 | LEO (~830 km, SSO) | 2026 (planned) | 7 years
NGRM | MTG-I2 | GEO (0°) | 2026 (planned) | 8.5 years
NGRM | Sentinel-6-B | LEO (1336 km, 66˚ incl) | 2026 (planned) | 7 years
MiniRMU | Lunar Pathfinder | Lunar (elliptical) | 2026 (planned) | 8 years
ERSA | Lunar Gateway | Lunar (NRHO) | 2027 (planned) | 5+ years
SOSMAG-II, next ICARE-NG, NGRMs… | GK5, MTGs, MOSs, and TBDs | GEO, LEO, and TBDs | 2026+ | 

## Slide 10: Aurora-D main characteristics
Continuous monitoring of the Auroral Oval Small Satellite demonstration mission (Aurora-D) in preparation of constellation (Aurora-C) Aurora-C: 4-satellites with 90 degree phasing Aurora-D: single satellite launch planned in 2031 Mission orbit & satellites Medium Earth Orbit @ ~6500 km, circular, drifting ~210 kg incl. instrument ~350 W nominal operation (TBC) S-band communication, ~360 kbps downlink rate Instruments Auroral Optical Spectral Imager (AOSI) Aurora far UV Imager (AUI) Radiation Monitor and Magnetometer (RadMag) Launch Vehicle & Launch date Micro-launcher baselined Flight Operators and payload data processing Operation, ground segment and launch service managed by mission prime Level 1 processing at ESOC SWE PDC
https://site.uit.no/spaceweather/aurora-borealis/

## Slide 11: Aurora Data
Refreshed image every 20-30min
SSD 30km at nadir, 200km at edge
“wide” FoV
Optical Imaging:
Intensities of multiple lines (6) between 350-1100nm
Far UV Imaging:
1 (2) spectral bands within Oxygen lines or LBH-L and LBH-S
Imagery of Auroral Oval
In-Situ Measurements
Radiation monitors: (2 directions TBC)
Energy distribution proton flux (2-500 MeV)
Energy distribution electron flux (0.3-5 MeV)
Heavy ions particle count
Fluxgate magnetometer:
Magnetic field vector

## Slide 12: D3S: Space Weather Nanosatellites
Objective:
  Cost effective implementation of D3S measurement requirements (see SWE PSD)
  To demonstrate the capability of very small platforms to provide data with sufficient reliability, availability and low latency for use in operational applications
  To assess potential business case of a commercial constellation
Two Nanosatellite missions were funded in 2022/23

## Slide 13
Space Weather – D3S – 1st Nanosat - SWING
Under French lead (platform, instruments, mission operations) with FI, NO contributing instruments and IT supporting the ground segment
  Prime: Hemeria (FR),
  sub-cos: Eidel (NO), Isaware (FI), Syntony (FR), Planetek (IT)
Addressing the needs of ionospheric space weather services
Mission design:
Business case demonstration for a commercial constellation with ESA as anchor customer
  LEO SSO (~550 km), local time TBD, 3 years lifetime, high reliability & availability, low latency
  Instruments: Radiation monitor - DREAM, Langmuir probe - mNLP, GNSS radio occultation - Aquila, X-ray flux monitor – XFM-NS
  Service to become available early 2027
  First year of service contracted, then possible yearly extensions

## Slide 14
Space Weather – D3S – 2nd Nanosatellite - SAWA
Enabled by additional Polish subscription
Phase 0/A1 study contract signed:
  Prime: Creotech Instruments SA (PL)
  Subs: CBK PAN (PL), WUST (PL)
Addressing space weather data complementary to 1st mission, e.g.:
  LEO magnetic field,
  Radiowaves
  Neutrals density (atomic oxygen)
  Optional: Medium energy particle fluxes
Instrument baseline proposed, but still to be consolidated!
Planned schedule: launch in 2028

## Slide 15: D3S: SWORD (Space Weather Orbital Radiation Detector)
Comprehensive instrument suite covering particles of all energies (electrons 1 keV to 8 MeV, protons 0.1 keV to 1 GeV)
Small OTS satellite <200 kg, 3 years lifetime, piggy-back launch with GEO satellite, targeted launch in 2031
ESA CDF completed, parallel pre-Phase A study with industry on going, Phase A ITT planned in September – parallel contracts including instrument providers
Objective: Radiation belt monitoring from “GTO”:
  Cross-section of inner and outer belt at least every 5 hours (constellation of two satellites)
  Spinning satellite for determination of pitch angle distribution allowing extrapolation to all Earth orbits
  Latency of <60 minutes, goal of 5 minutes

## Slide 16: D3S: SHIELD
Objective: 2 hours advanced warning time for CME arrival
Shield mission shall provide low latency (5-10 min) in-situ observations of solar wind and interplanetary magnetic field ahead of Earth enabling final Earth impact prediction with a lead time equaling or exceeding 2 hours* before the CME arrival. * for CMEs up to 2000km/s
Shield mission shall provide in-situ solar wind observations for space weather modelling and scientific research
Shield mission shall measure high energy solar particles allowing detection of Solar Energetic Particle events
Image: O.C.St. Cyr et al, https://doi.org/10.1016/S1364-6826(00)00069-9
Payloads:
Plasma Analyser
Magnetometer
Radiation Monitor
ESA CDF study started June 3rd!

## Slide 17: Goal: End-to-end Space Weather Monitoring
L5 Vigil
∂
Solar disc: PMI, JEDI
(-4d - T0)
Middle corona: JEDI
(T0 – T0+30 min)
Outer corona: CCOR
(T0+15 min – T0+2h)
CME propagation: HI
(T0+2h - T0+14h)
Shield: CME shock, IMF, SPE (TI-120 min)
L1 missions: CME shock, IMF, SPE
(TI-12 min)
Earth magnetic field: GEO/LEO hosted payloads
Radiation belts, SEP impacts: SWORD
Auroral oval, electron precipitation: AURORA
Thermosphere, ionosphere: Nanosat constellations
In-situ measurements of solar wind and IMF are mandatory for final prediction of the impact on Earth

## Slide 18: Space Weather services to end users
Space Weather Payload Data Centre
MOC
D3S
Collaborating missions
Ground based observations
Ground stations
Notes: animations

## Slide 19: Thank you!

## Slide 20: Aurora ConOps
Observations
  Imagers: 90min per hemisphere
  RadMag: all the time
Latency Requirements (defined at L0):
  Imagers data latency: < 20 minutes
  In-situ data latency: < 60 minutes
Constellation:
  4 satellites, equally spaced, repeating cycle every ~60min
Ground Stations:
  Polar stations: Svalbard and Troll
  Other stations: TBC time from lower-latitude stations to meet latency/refresh rate requirements

## Slide 21: Preliminary architecture of D3S
Observational Requirements
Measurements in GEO
Measurements in LEO
Measurements in MEO & HEO
Hosted Payloads & International Collaboration
Dedicated Satellites
Ground Segment (Data Download), ESA or collaborating ground stations, L1 Data processing
Further Processing @ ESCs, Service Provision (ESA SWE Portal)