## Slide 1
<number>
EREMS
16th - 18th September 2014
PRESENTATION
SANDRINE ZAOUCHE & REMI SARRERE
Notes: 18th September 2014 – Workshop FPGA
<number>

## Slide 2
<number>
1 / INTRODUCTION
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
● Feedback about flight FPGA based on project examples
● Table of contents
- 1 / Introduction
- 2 / EREMS presentation
- 3 / Choice of FPGA target
- 4 / Prototypes
- 5 / Design
- 6 / Performance
- 7 / Programming
- 8 / Conclusion
PROJECT NAME: FPGA USED – Main feature, main functions
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 3
● EREMS, French SME near Toulouse (since 1979)
- specialized in the design & manufacture of space flight electronics
● Means & facilities
- 62 employees (36 engineers)
- Clean room facilities
- Space Qualified processes
- Space Certified operators & controllers
● Development / supply of space electronic equipments
- power supplies and power distribution units
- control/command electronics
- onboard computers, data handling equipment
- front end electronics, video acquisition equipment
● References
- R&T: CPUGEN (Leon3 OnBoard Computing Module)
- Scientific programs: BEPICOLOMBO/PHEBUS, JASON-3/CARMEN, TARANIS
- Observation satellites: SPOT 6 & SPOT 7, PHASE B STUDY / PVL
- Telecom programs: EUROSTAR 3000, IRIDIUM-Next
<number>
2 / EREMS PRESENTATION
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 4
<number>
3 / CHOICE OF FPGA TARGET
TARANIS: 1 RTAX1000 + 2 RTAX2000 – PHOTOMETRE analyzer, triggering
CPUGEN: 1 ATF280  1 ATFS450 – ITAR free Leon3 computing board
● Requirements identification
- analysis of function (sequencing, signal treatment)
- implementation of existing/developing IPs:
microcontroller: 8051 computing: PID, divider
compressor: Elias, FELICS, RLE EDAC: Hamming, Reed-Solomon
communication: SpaceWire, 1553, UART
- space available on the board
● Resources estimation
- FPGA size + IO number
● FPGA selection
● Feedback : 2 helpful criteria
- PIN compatibility for 1 FPGA family
RTSX32/72
RTAX250/1000/2000 (TARANIS)
ATF280/S450 (CPUGEN)
- QFP package preferred to CCGA
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 5
<number>
4 / PROTOTYPES
● One Time Programmable FPGA (OTP) : 3 or 4 steps
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 6
<number>
4 / PROTOTYPES
● One Time Programmable FPGA (OTP): 3 or 4 steps
CARMEN: 2 RTSX – Data processing, including microprocessor
PHEBUS: 1 RTAX1000 – Data processing, imaging, IPprocessor
PVL: 1 RTAX2000 D – Filtering, interpolation
CPUGEN: 1 ATF280  1 ATFS450 – ITAR free Leon3 computing board
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
● Programmable FPGA: 2 steps
Some prototypes of programmable flight FPGA are quite expensive Prototype ATF280 vs. Flight ATF280 cost ratio ≈ 1/3
- Does the same package follow the whole flow? Most of programmable FPGA and OTP FPGA have different packages adapter layout to have the programmable fit the OTP (CARMEN) double-prints on the same board (PHEBUS) - Does a low-cost FPGA exist with the same matrix technology? No FPGA exists with DSP blocks to prototype RTAX2000D (PVL) Xilinx prototype + adapter layout or socket to fit with the final package
Prototype RTAX2000D vs. Flight RTAX2000D cost ratio ≈ 1/10
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 7
<number>
5 / DESIGN
TARANIS: 1 RTAX1000 + 2 RTAX2000 – PHOTOMETRE analyzer, triggering
CPUGEN: 1 ATF280  1 ATFS450 – ITAR free board including microprocessor
● LIBERO
- 6 updates between 01/2011 and 02/2012 for the version 9.1
+ updates of Simplify + CN1410 (TARANIS)
- several warnings before the last version 9.2 SP1
relatively new version to be used for current flight FPGA
● PRECISION (version 2012c.14 OEM_ATMEL)
- LPM_MUX (ATF280) was not properly synthesized by the software (CPUGEN)
comparison between functional & post synthesis simulations
- short license validity for significant cost
● FIGARO
- unintuitive handling despite the good reactivity of the customer support
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 8
<number>
6 / PERFORMANCE
Project |  |  | FPGA Matrix | Working Frequency |  | Occupancy rate | Main Functions
 |  |  |  | Expected | Reached |  | 
JASON 2 |  | T2L2 | RTSX72 | 100 MHz | 105 MHz | 99% FF; 47% Cb; 100% IO | Time Transfer by Laser Link
CARMEN (Icare-NG) |  | Micro | RTSX72 | 32 MHz | 42 MHz | 82% FF; 45% Cb; 96% IO | Micro-processor companion
 |  | Exper. | RTSX72 | 32 MHz | 39 MHz | 91% FF; 87% Cb; 95% IO | Test of components in radiative environment
PHEBUS (Bepi-Colombo) |  |  | RTAX1000 | 40 MHz 10 MHz 10 MHz | 51 MHz 15 MHz 102 MHz | 82% FF; 80% Cb; 92% IO; 58% RAM | 8051µC (IP MICROSEMI), image processing, image compressions (coordinate, binary, Elias)
TARANIS | PHA |  | RTAX1000 | 20 MHz | 61 MHz | 59% FF; 26% Cb; 66% IO; 86% RAM | Analog signal acquisition, event trigger (ration algorithm)
 | MCA |  | RTAX2000 | 50 MHz 20 MHz | 57 MHz 70 MHz | 91% FF; 83% Cb; 95% IO; 77% RAM | Image compressions (FELICS, RLE), PID Thermal control
 | XGRE |  | RTAX2000 | 50 MHz 3x 20 MHz | 63 MHz 134 MHz | 69 % FF; 51% Cb; 97%IO; 82% RAM | Spectrum generation, event trigger
PVL (study) |  |  | RTAX2000D | 100 MHz | 99 MHz | 44% FF; 28% Cb; 0% RAM; 97% DSP | Signal demodulation, filtering and interpolation
CPUGEN (R&T) |  |  | ATF280 Compatible ATFS450 | 20 MHz | 21 MHz | 8% Cells; 7% Nets; 65% IO; 1% RAM | Leon3 boot and board management 90% cells free for user applications
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 9
<number>
7 / PROGRAMMING
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
● Equipment needed
- OTP FPGA 1 programmer + (1 socket / package)
- Programmable FPGA 1 probe
● Feedback about Microsemi FPGA
- 224 OTP flight FPGA programmed
- 3.13% failed
mature process
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 10
<number>
8 / CONCLUSION
● Expectations for future flight FPGA:
- free from exportation restrictions
- member of a pin compatible FPGA family
- low cost flow for prototypes
- integration of hard IPs:
communication modules (SpaceWire, 1553 bus, CAN bus, Ethernet, SPI)
multiplier-accumulator blocs
RAM blocs
LVDS compatibility
microprocessor core
- user friendly development tools for:
synthesis / placement routing
timing verifications
optimization (retiming)
manual placement constraints
limited versions for space implementation
- libraries of soft IPs:
communication protocols
computing modules (filters, EDAC, compressor, PID, FFT)
microprocessor core
- package technology easy to use (QFP)
1/ Introduction - 2/ EREMS presentation - 3/ Choice of FPGA target - 4/ Prototypes - 5/ Design - 6/ Performance - 7/ Programming - 8/ Conclusion
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 11
<number>
● ESA – Mr. David Merodio Codinachs
● CNES – Mr. David Dangla
SPECIAL THANKS TO
Notes: <number>
18th September 2014 – Workshop FPGA

## Slide 12
<number>
EREMS CONTACTS
● Gérard Dejonghe ● Nicolas Poiraudeau
Chief Executive Officer Head of FPGA Department
Email : gerard.dejonghe@erems.fr Email : nicolas.poiraudeau@erems.fr
Phone: +33 - 5 61 36 06 06
www.erems.fr
Notes: <number>
18th September 2014 – Workshop FPGA