## Slide 1
Entry modelling and instrumentation: impacts to aerothermal research Aaron Brandis,1 and Tom West2
1NASA Ames Research Center
2NASA Langley Research Center RHTG | Sep 24th, 2026

## Slide 2: NASA RTMD Entry Modeling & Instrumentation Portfolio (EM&I)
Entry System Instrumentation
Entry Systems Modeling
Flight Test and Instrumentation
EM&I is the only NASA portfolio that builds and validates the cross‑cutting flight technologies, models, and tools needed for EDL across missions
Delivers ground‑to‑flight traceability with quantified uncertainty
Reducing mission risk and facilitating faster design iteration
Enabling new entry and descent system architectures
EM&I provides EDL capabilities and expertise resulting from decades of mission-focused development – there is no viable industry counterpart

## Slide 3: Capability Outline by Mission
EM&I modeling impacts on Dragonfly (Titan) will be used to highlight modeling capabilities generally useful for EDL missions:
  Aeroheating of Detailed Geometries
  Capsule Dynamics
  Parachute Dynamics
Capability infusion plans for new and emerging missions will also be discussed:
  DAVINCI (Venus)
  Outer Planets (Uranus and Saturn)

## Slide 4
Highlighting EM&I Capability Infusion for Dragonfly
EM&I partnered with Dragonfly to infuse and demonstrate new capabilities for mission design – mitigation efforts for 5 of 10 major EDL mission risks supported using these developments
Dynamics under Drogue
DrEAM Instrumentation Suite
Dynamic Stability Characterization
Improved Aeroheating Tools

## Slide 5: Aeroheating of Detailed Geometries
‘PICA-tooth’ Shoulder Heating with Coupled Radiation, Flow, and Material Response (Ares Code)
Dragonfly aeroshell has detailed structural features – capabilities for efficient, multiphysics aeroheating analyses reduced design complexity and mitigated aeroheating risks
POC: Olivia Schroeder, Amal Sahai, Joey Schulz, Kyle Thompson, Prakash Shrestha
Design Impact: Coupled flow-material-radiation analyses mitigated need to protect main seal with complex, protective heatshield ‘tooth’
Risk Mitigation: Improved efficiency radiation and CFD algorithms mitigated aeroheating concerns for backshell low-gain antenna (LGA)
LGA Impact on Heating of Full Aeroshell (HyperSolve CFD Solver)
LGA Heating with Coupled Tools (NERO Radiation Code)

## Slide 6: Vehicle Dynamics
Dragonfly poses unique challenges for vehicle dynamics that have not been faced by previous missions – efforts underway to drive down mission risk
Titan atmosphere reaches a higher altitude, is colder, and denser near the surface compared to Mars
Disk-gap-band supersonic drogue parachute 6 minutes after entering the atmosphere at a target Mach number of 1.4 to 1.5
Vehicle will decelerate under drogue for unprecedented > 100 minutes!
Genesis heritage aeroshell (basis for Dragonfly) is known to be dynamically unstable in certain conditions
Genesis Impact and CFD of Dragonfly Capsule

## Slide 7: Vehicle Dynamics - DAWG
POCs: Quincy McKown, Mark Schoenenberger, Ben Libben, Hannah Alpert
The Dynamic Analysis Working Group (DAWG) is working to fuse theoretical, computational, and experimental approaches for dynamics to better predict stability
Current work to fill key missing low-supersonic data – LaRC wind tunnels, SPEED drop tests, Aberdeen testing – to reduce into improved model description near drogue deploy
Longer term aim is to reformulate dynamic stability equations for improved accuracy
Three-pronged DAWG Approach to Stability
SPEED Concept of Operations (Stratospheric Projective Experiment in Entry Dynamics)
Collaborative Dragonfly-NESC-DAWG Aberdeen Ballistic Range Testing

## Slide 8: Parachute Dynamics
Capabilities to simulate coupled drogue deploy and aeroshell dynamics in development
POCs: Francois Cadieux, Michael Barad
Animation showing Mach number on a slice, where the aeroshell and parachute surfaces are shown in gray, and the parachute lines in black.
Simulation of Dragonfly Drogue Deployment (LAVA solver)

## Slide 9: Dragonfly Entry Aerosciences Measurements (DrEAM) Instrumentation Suite
POCs: Helen Hwang & Aaron Brandis
DrEAM Instrumentation Bridges Aeroheating and Dynamics
Notes: Update figure….

## Slide 10
Mission Infusion: DAVINCI (Venus)
Comparison to Flight Data
EM&I will provide entry instrumentation for the DAVINCI capsule through the VISTA project to improve entry modeling in CO2 environments.
Uncoated
Roughness Heating Augmentation
Models for roughness heating are important for Venus entry and largely empirical. EM&I is developing roughness heating augmentation models for both tiled and monolithic TPS.
4000
3000
2000
W/cm2
Venus offers several challenges for EDL, the entry conditions are extreme, leading to the development of new and novel EDL technologies.
Capsule Dynamic Behavior
Free-flight CFD can be used to estimate drag as a function of the trajectory to minimize descent time for Venus descent. (ADEPT shown)
Benchmark Radiative Heating
Radiative heat flux may be dominant for Venus entry. Shock tube data for CO2 atmospheric entry is being generated for model validation.

## Slide 11
Missions to outer planets pose several EDL challenges including the largest heat fluxes of our solar system, multi-destinations within one mission, and new TPS materials.
Mission Infusion: Outer Planets (Saturn, Neptune, Uranus)
Launch to Landing GN&C
Coupled GNC (POST2) and trajectory (MONTE) solver provides insights to multiple mission concepts.
Fracture & Failure of Woven TPS
Developing models for TPS fracture and failure modes to improve reliability prediction and risk reduction for extreme entries.
Advancing Woven TPS Thermal Models
EM&I is developing woven TPS (e.g., HEEET) material models to quantify thermal uncertainties and aid design.
Radiative Heating & Kinetics
Radiative heat flux has large uncertainties for H2/He atmospheres. Shock tube data for H2/He atmospheric entry is being generated for model refinement.
Notes: Tom

## Slide 12: Summary
EM&I seeks to develop new modeling and simulation capabilities for EDL, validated through ground and flight testing
Value of incorporating improved capabilities into missions demonstrated through partnership with Dragonfly
Future activities will be planned as the mission landscape evolves:
  Mars, Outer Planets, Sample Returns, Venus missions

## Slide 13: ESM Capability Development Mission Transition and Infusion
Artemis Backshell Design
ESM research highlighted wake radiation as a significant (often dominant) contributor to afterbody heating, and this was included in the Artemis-1 backshell TPS design for first time. Flight measurements confirmed the significance of this heating.
Augmented heating measured
Mission Roughness for Artemis
Tools and techniques developed for ESM roughness testing in LAL applied to Artemis-I post flight study to look at char-loss induced "roughness"
Excellent agreement with Orion DFI
GN&C
Dragonfly using ESM improved version of POST2. Algorithm development useful for UOP trade studies. Coupling with Copernicus (and Monte) for improved mission design through-put.
POST2 parallel optimization for lunar ascent & orbit
Detailed Geometry Simulation
A multi-physics simulation capability developed to model complex Dragonfly aeroshell features such as cavities, domes and seals.

## Slide 14: ESM Capability Development Mission Transition and Infusion
Parachute Modeling
Excellent agreement shown with ASPIRE parachute flight test (MSR-SRL). Increased confidence prompting work to begin on a drogue-aeroshell simulation for Dragonfly. Will provide insights into dynamics and anchor lower-fidelity simulations.
Titan Aerothermal Environments
ESM anticipated need in advance of a Titan mission with EAST shock tube test. Enabled informed margin policy and improved models to be used by Dragonfly – neither would have been possible without this data.
Dynamic stability
Free-Flight simulation capability a critical tool used to understand the passive entry vehicle dynamic stability of MSR-EES & Dragonfly.
LAVA ASPIRE FSI simulation
Dragonfly Free-Flight simulation
FSI flow visualization
Dragonfly aerothermal flowfield
EAST Shock Tube
3D Ares simulation of recessing Arc Jet coupon
Multi-Dimensional Response
Dragonfly & MSR-EES have some complicated geometries that cannot be modeled with traditional 1-D approach. Coupled multi-dimensional material response tools developed within ESM being utilized.

## Slide 15
For more details, please refer to:
F. Cadieux and M. F. Barad. "Fluid-Structure Interaction Simulations Of Supersonic Parachute Inflation: Model Sensitivities”, AIAA 2024-4225. AIAA AVIATION FORUM AND ASCEND 2024. July 2024.
F. Cadieux and M. F. Barad. “Wall-Modeled Large-Eddy Simulations Of Supersonic Parachute Inflation”, Twelfth International Conference on Computational Fluid Dynamics (ICCFD12). July 2024.

## Slide 16: Qualitative Comparison to ASPIRE SR03
Rendering of FSI parachute system meant to mimic the high-speed video from flight (right).
Notes: Here we compare the view of the parachute system (without the payload) from FSI on the left to what was recorded during the SR03 flight test on the right.
Notice that the parachute is barely distinguishable from the lines at line-stretch on the right, but once it starts to inflate we see a lot of similarities between FSI and the flight test.
Both inflations show the disk getting taut first and tugging the band along, creating a multi-lobed shape until the band is pressurized.

## Slide 17: ESM Capability Development Mission Transition and Infusion
Radiative Heating In Flight
ESM responsible for characterization, calibration and analysis of the Orion radiometer and spectrometer. Tools showed excellent agreement with observation of Hayabusa-2 return.
NuSil coated PICA
MEDLI2 Deep Dive (NuSil) detailed analysis provided supporting evidence to inform change of MSR-SRL TPS design process.
(* SRL design decisions made by them, not ESM)
TPS Cert for Orion
TPS Certification tools have shown so much promise, already being infused by MSR-EES to characterize the new class of woven TPS materials and provide insights into the Orion/Artemis-1 heatshield performance.
Developing woven TPS models
Simulation of tiled MSL heatshield
Excellent comparison with MEDLI2 TC data
Augmented heating measured
Hayabusa-2 entry simulated
Roughness Margin for EES
MSR-EES margin & nominal environment due to TPS roughness augmented heat flux derived from need-anticipating ESM testing.
HEEET Engineering Test Unit & range model

## Slide 18: Jupiter: Galileo Probe
Jovian entry on 7 December 1995 traveling at 47 km/s!
Previous attempts at post-flight comparisons did not predict the measured forebody recession well
Increasing model fidelity improved agreement significantly
  3-D radiation (i.e., ray-tracing)
  Detailed multicomponent diffusion modeling
  Modeling TPS recession
Surface Recession Modeling
Diffusion Modeling

## Slide 19: Summary of Tools
Icarus | Material Response | Limited Distribution
Ares | Multi-physics Coupling | US Distribution
PATO | Material Response | Open Source
PuMA | Micro-Material Response | Open Source
arcjetCV | Arc Jet In Situ Analyses | Open Source
SPARTA | Gas-Surface Interactions | Open Source
NEQAIR | Radiation | NASA Software
NERO | Radiation | To Be Released
HARA | Radiation | NASA Software
MPEC | Quantum Chemistry | NASA Software
LAURA | CFD | NASA Software
HyperSolve | CFD | NASA Software
NASA Software: https://software.nasa.gov/
Contact for More Info: justin.b.haskins@nasa.gov, aaron.m.brandis@nasa.gov
Notes: BEAST… TOMATO… facilities… EAST, ARCTRON,

## Slide 21: Entry, Descent, and Landing (EDL) Challenges
EDL is small portion of mission timeline but among the largest risks
Entry Heating
Aerodynamic Heating
Radiative Heating
Thermal Protection System (TPS) Response
Hypersonic Aero-Maneuvering
Vehicle Dynamics Stability
Guidance, Navigation & Control
Parachute Deployment & Descent
Parachute Stability & Dynamics
Guidance, Navigation & Control
Mars2020 Simplified Entry & Descent
EDL is a multi-stage process unique to mission and destination
Each stage presents challenges – high velocity, large thermal gradients, and complex maneuvers
Test-as-you-fly is usually not feasible – validated models required for ground-to-flight traceability

## Slide 22: Vehicle Dynamics - SPEED
POCs: Ben Libben, Hannah Alpert, Kenny McAfee
The Stratospheric Projectile Experiment of Entry Dynamics (SPEED) is low-cost flight test platform to provide free flight dynamics
SPEED allows testing at Transonic Mach where ground facilities have no mutual overlap – verification of ground tests
First flight test with Dragonfly-like capsules is slated for later this summer - data will be leveraged in DAWG activities to complement existing databased
SPEED Projectile and Mach Span

## Slide 23
Sample returns involve Earth re-entries that require robust TPS materials and understanding of air environments at high-velocity. Weave/GN&C development needs overlap with Outer Planets.
Mission Infusion: Sample Returns (Earth)
Launch to Landing GN&C
Coupled GNC (POST2) and trajectory (MONTE) solver provides insights to multiple mission concepts.
Fracture & Failure of Woven TPS
Developing models for TPS fracture and failure modes to improve reliability prediction and risk reduction for extreme entries.
Advancing Woven TPS Thermal Models
EM&I is developing woven TPS (e.g., HEEET) material models to quantify thermal uncertainties and aid design.
High-Speed Air Radiation
First of their kind databases for backshells and high velocity radiation have been developed. Radiation validated with shock tube data.
Mars Sample Return – Earth Entry System
Notes: Tom

## Slide 24: EM&I Stakeholder Capability Infusion
External Collaborators
EM&I collaborates extensively to accelerate capability development and infusion
Science, human exploration, and commercial space missions
30+ Major Academic Partners
Multiple NASA Centers and OGAS
NASA Project and Government Team
Spaceflight Projects and Missions
DLR (German Aerospace Center)
Ecole CentraleSupelec
Von Karman Institute
University of Queensland
Oxford University
Instituto Superior Tecnico
European Space Agency
JAXA (partnered with Orion)
Various International Partners

## Slide 25: Mission Infusion and Transition
 | Orion/Artemis | ESM: TPS Tools, Models, and Experiments for Char Loss Investigation ESM: Backshell radiative environment models and co-funded spectrometer Artemis I-III FTI: Spectrometer on SciFil for Artemis II imaging
 | Mars Sample Return Earth Entry System (EES) Sample Retrieval Lander (SRL) | ESM: Co-funded TPS material response models for woven TPS and TPS coatings ESM: Vehicle dynamic stability model development ESM: Aerothermal environments and multi-physics design tools FTI: SPEED data on capsule dynamic stability
 | Dragonfly | ESI: DrEAM providing EDL instrumentation for Dragonfly ESM: Multi-physics TPS design tools, Titan aerothermal environments ESM: Vehicle dynamics models development and co-funded ballistic range tests FTI: SPEED data on capsule dynamic stability
 | DAVINCI | ESI: VISTA providing EDL instrumentation for DAVINCI
 | SMD and HEO Futures: Ice Giants and Mars | ESM: Human-Mars will benefit from activities in all capability elements ESM: Uranus-Orbiter Probe aerothermal environments and TPS response
 | Commercial Space | ESM: ULA/Vera HIAD data products through LOFTID Deep Dive ESM: SpaceX and Blue Origin tool infusion for TPS design FTI: SciFli ACO SpaceX Starship Re-entry Observation FTI: SPEED Blue Origin Partnership on testing FTI: OSPREE ARFL Spectrometer Reconstruction from Varda flight
25

## Slide 26: Other Capabilities from EM&I Infused into Dragonfly
Benchmark Radiative Heating
The benchmark experimental data for Titan entry, along with validated models performed and developed within ESM
New Radiative Heating
New low density shock tube (LDST) online in the Electric Arc Shock Tube (EAST) at NASA Ames
Heatshield Coating Behavior
Improved models for behavior of NuSil coated Phenolic Impregnated Carbon Ablator (PICA)
Convective Cooling
Scale resolved convective cooling conducted to understand temperatures during descent
POCs: Brett Cruden, Aaron Brandis, Brody Bessire, Francois Cadieux
Capabilities have led to reduced radiative aeroheating baselines and margins – changing TPS sizing, mitigating heatshield thermostructural risk, and mitigating internal temperature exceedance risks