## Slide 1: Unpacking the Millikan and White Relaxation Fits
RHTG 2026
Kaelan B. Hansson, Eric C. Geistfeld
Analytical Mechanics Associates, NASA Ames

## Slide 2: Thermochemistry Model
Conservatives
[, u, E]
Primitives
[, u, T]
Reactions
[, 0,]
Relaxation
[0, 0, ]
Chemical Source Term
[, u, E]

## Slide 3: Two Primary Problems
Vectorization
  Software is faster if it is given repeated calls to the same function.
  If all reactions and relaxation processes can be cast as the same functional form. There is a possible speedup
Uncertainty Analysis
  Relaxation processes are usually parameterized using the Millikan and White fit, using two parameters, a and b (plus the high temperature correction parameters). We are not sure what the uncertainties are on these numbers.

## Slide 4: Millikan and White Relaxation Times
“Time based”
“Frequency
based”
Note: I am using as a molar density
The molar weighted relaxation frequency averaging is important
Note: None of this works with the US3D style mixture averaged
Note 2: Harmonic oscillator is used for all in this analysis

## Slide 5: Some Algebra
Algebra
Standard Millikan and White
Even though we say P is the total pressure, the mixing rule converts it to a partial pressure of the collider

## Slide 6: Millikan and White Source Term
Multiply by the two molar densities to get the true source term
This is what is currently in DPLR
A DMS study from 2017

## Slide 7: Reaction Energy Source Terms
Three Energy Moving Processes:
Move the average modal energy at the mixture temperature (
Move some ratio of the heat of formation into a particular mode ()
Move and extra RT out of a move ()
The change in energy of mode m
: The stochiometric coefficient of the species
Static Parameters
Standard modified Arrhenius

## Slide 8: Consider a “Relaxation Reaction”
This is very close to the form found for Millikan and White

## Slide 9: Comparing
Chemical Reaction
Millikan and White Relaxation
Can we find reaction parameters that fit the relaxation process source term?

## Slide 10: Making the Fits
Minimization on the RMS of the relative error
Use a genetic algorithm to find the global minima
The choice of fit points always matters: We use a “band” around T = Tv.
You don’t want to include T=Tv because you’ll have a zero divided by zero error
Prefactor | Exponent | Activation Temperature | Vibrational Weighting
2.7331·103 m3/(s mol) | 2.543 | 9538 K | 0.3184
Tt
Tv

## Slide 11: Adiabatic Reactor Comparison
Millikan White:
Reaction Fit:
Pure N2 at 15000K

## Slide 12: Space Marching Comparison
7 km/s, 0.1 Torr, 100% N2

## Slide 13: Torres QCT/DMS Data (2025)
This data is collected from DMS data;
i.e., it is “averaged” over a range of vibrational temperatures

## Slide 14: Fitting Torres QCT Data
Reaction fits seem to work reasonably well for ab initio data
This provides a path to incorporate new data into heritage models

## Slide 15: The High Temperature Correction
Park’s Version
X
Cannot separate into per-processes relaxation times

## Slide 16: Plots of process specific relaxation times are misleading
These curves do not really exist in Park because there is no way to separate the processes

## Slide 17: Simply Accept the Separation
Proposed Version

## Slide 18: Comparisons
Proposed correction to high temperature correction yields results in family with original calculation
7 km/s, 0.1 Torr, 100% N2
Note: There are no reaction fits here. This just compares relaxation time parameterization

## Slide 19: Reaction fitting does not agree
7 km/s, 0.1 Torr, 100% N2

## Slide 20: Fit itself is poor
N2 – N: Grover with High Temperature Correction Source Term

## Slide 21: Quasi Classical Trajectories: Possible Vindication
This analysis begs the question: What data is truly “correct.”
We wrote a new QCT code (mostly to handle electronic transitions)
Using the Minnesota N3 Surface we will inspect the N2-N relaxation

## Slide 22: Orientation for Following Plots
At each point:
Run three million trajectories
Collect all processes that do not dissociate
Capture total change in vibrational energy
Capture cross-section/collision frequency

## Slide 23: Translational Temperature: 5000K

## Slide 24: Translational Temperature: 5000K
Dashed – Solid Divergence: Poor Fitting
Energy Transfer at Tt=Tv

## Slide 25: Translational Temperature: 1000K

## Slide 26: Translational Temperature: 15000K
Fits with some sort of high temperature dependence diverge more

## Slide 27: Thoughts
QCT rates are generally larger than other data
  Likely a result of sampling at a pure Boltzmann distribution
  Caveats:
    QCT does not follow detailed balance a priori
      Continuous classical distribution has quantization errors when converting to rovibronic levels
      Unclear if dynamic equilibrium matches the thermal equilibrium
Reaction Fits can diverge from fits at high T-Tv difference
  This is likely a result of the choice of of the fitting points.
  Overall, the result is to speed up the relaxation rate.
The N2-N relaxation rate in DPLR is the fastest of present data
The harmonic oscillator approximation will affect these results

## Slide 28: Conclusions
Millikan and White Relaxation Processes can be recast as reactions.
We cannot exactly reproduce DPLR because the high temperature correction is inseparable.
Fitting the high temperature correction can lead to unacceptable errors
We can successfully fit master equation/DMS data directly.
There are a lot of subtleties that should be checked before proposing a final reaction list
The obvious question: How much better could you do if you had a more sophisticated reaction parameterization?

## Slide 30: Translational Temperature: 1000K

## Slide 31: Translational Temperature: 1500K