## Slide 1: Characterization of Spectral Radiance Uncertainties for Ice Giant Entry Simulations and Experiments
Cate Leszcz and Iain D. Boyd
Ann and H.J. Smead Department of Aerospace Engineering Sciences
University of Colorado Boulder, Boulder, CO
International Workshop on Radiation of High Temperature Gases for Space Missions
Mola di Bari, Italy
September 22, 2026

## Slide 2: Mission to Ice Giant Planets
Planetary Science Decadal Survey has deemed mission to Ice Giant planets high priority [1]
  Least explored planets in our solar system
  Next NASA Flagship Mission: Uranus Orbiter & Probe
    Mission could take 13-14 years from launch to atmospheric entry
We want to accurately predict the aerothermal environment for heat shield design
[1] “Vision and Voyages for Planetary Science in the Decade 2013-2022,” National Academies Press, 2011. https://doi.org/10.17226/13117.
Image Credit: Rebrickable
Notes: Also mention that you don’t want the heat shield to be too thick so that we can take a payload

## Slide 3: Aerothermal Environment of Ice Giant Planets
Hydrogen/helium/methane atmospheres [2]
Entry velocity 20+ km/s [3]
Thermochemical nonequilibrium behind detached bow shock
We use computational modeling tools to predict the aerothermal environment
  Uncertainties in chemical kinetics models
Shock tube experiments also have uncertainties
  T6 Stalker Tunnel at University of Oxford
  EAST Facility at NASA Ames Research Center
Image Credit: boltzplatz
[2] Moses, J. I., Cavali, T., Fletcher, L. N., and Roman, M. T., “Atmospheric chemistry on Uranus and Neptune,” Philosophical Transactions of the Royal Society A, 2020. https://doi.org/10.1098/rsta.2019.0477.
[3] Monk, J., Prabhu, D., Jr, G. A., Thornton, J. M., Hwang, H., Pensado, A., and Dutta, S., “Uranus Probe Entry and Descent Mission Concept,” In Situ Exploration of the Giant Planets II, 2022.

## Slide 4: Nonequilibrium Chemical Kinetics Solver
Toolkit for Excitation, Reactions, and Radiation with Applications (TERRA)
1D incident shock simulations
Multi-temperature chemical kinetics model
Newly implemented 12-species H2/He/CH4 database
  Equilibrium properties match NASA CEA within 5%
  Validated with the literature [4]
[4] Furudate, M., Chang, K.-S., and Jeung, I.-S., “Calculation of H2-He Flow with Nonequilibrium Ionization and Radiation,” 43rd AIAA Aerospace Sciences Meeting and Exhibit, American Institute of Aeronautics and Astronautics, Reno, Nevada, 2005. https://doi.org/10.2514/6.2005-586.

## Slide 5: Nonequilibrium Chemical Kinetics + Radiation Solver
TERRA
NEQAIR v15.3 [5]
Position
Temperature
(translational-rotational, vibrational-electronic)
Species number densities
Spectral Radiance
[5] Brandis, A. M., and Cruden, B., “Neqair v15. 0 release notes: Nonequilibrium and equilibrium radiative transport and spectra program,” Technical report, 2020.

## Slide 6: Experimental Data from Oxford T6 Stalker Tunnel
T6 Condition B:
84.5% H2 / 15% He / 0.5% CH4
12.9 Pa, 16.4 km/s
T6 Condition C:
80% H2 / 15% He / 5% CH4
13.0 Pa, 16.3 km/s
[6] Steer, J., Collen, P., Glenn, A., Hambidge, C., Doherty, L. J., McGilvray, M., Sopek, T., Loehle, S., and Walpot, L., “Commissioning of Upgrades to T6 to Study Giant Planet Entry,” Journal of Spacecraft and Rockets, Vol. 61, No. 6, 2024, p. 1545–1562. https://doi.org/10.2514/1.A35893.

## Slide 7: Peak Nonequilibrium Spectral Radiance
T6 Condition B:
84.5% H2 / 15% He / 0.5% CH4
12.9 Pa, 16.4 km/s
T6 Condition C:
80% H2 / 15% He / 5% CH4
13.0 Pa, 16.3 km/s

## Slide 8: Peak Nonequilibrium Spectral Radiance
T6 Condition B:
84.5% H2 / 15% He / 0.5% CH4
12.9 Pa, 16.4 km/s
T6 Condition C:
80% H2 / 15% He / 5% CH4
13.0 Pa, 16.3 km/s
Research Question: Can an uncertainty quantification (UQ) analysis that includes uncertainties from both simulations and experiments close the existing gap between modeling and testing for H2/He/CH4 systems?

## Slide 9: Mixed UQ Framework

## Slide 10: Uncertain Parameters
Epistemic Uncertainty
Aleatory Uncertainty
Due to lack of knowledge of variable
Result of inadequate understanding of physics model in numerical tool
Reducible if increase in physics knowledge
Due to uncontrollable factors
  Instrument noise in experiments
Generally considered irreducible [7]
Chemical kinetic rate parameters:
Fluctuations in experimental freestream conditions:
Velocity, Pressure
[7] West, T. K., and Hosder, S., “Uncertainty Quantification of Hypersonic Reentry Flows with Sparse Sampling and Stochastic Expansions,” Journal of Spacecraft and Rockets, Vol. 52, No. 1, 2015, p. 120–133. https://doi.org/10.2514/1.A32947.

## Slide 11: Epistemic Uncertain Parameters
Chemical kinetic rate parameters
[8] Leibowitz, L. P., “Measurements of the Structure of an Ionizing Shock Wave in a Hydrogen-Helium Mixture,” Physics of Fluids, Vol. 16, No. 1, 1973, pp. 59–68.
[9] da Silva, M. L., and Vargas, J., “A Physically-Consistent Chemical Dataset for the Simulation of N2-CH4 Shocked Flows Up to T 100; 000 K,” arXiv: 2212.09911 [physics], 2022.
[10] Carroll, A. T., Blanquart, G., Brandis, A. M., and Cruden, B. A., “Kinetic and Transport Modeling for Entry Flows in Hydrogen-Helium Atmospheres,” AIAA AVIATION 2023 Forum, AIAA Paper 2023-3728, 2023.
[11] Leibowitz, L. P., and Kuo, T.-J., “Ionizational Nonequilibrium Heating During Outer Planetary Entries,” AIAA Journal, Vol. 14, No. 9, 1976, pp. 1324–1329.

## Slide 12: Aleatory Uncertain Parameters
Velocity
[6] Steer, J., Collen, P., Glenn, A., Hambidge, C., Doherty, L. J., McGilvray, M., Sopek, T., Loehle, S., and Walpot, L., “Commissioning of Upgrades to T6 to Study Giant Planet Entry,” Journal of Spacecraft and Rockets, Vol. 61, No. 6, 2024, p. 1545–1562. https://doi.org/10.2514/1.A35893.

## Slide 13: Mixed UQ Nested Loop
Epistemic Outer Loop
Aleatory Inner Loop
TERRA
NEQAIR
x, Tt, Tv, Tr, Te, ns
L(,y)
Chemical kinetic rate parameters
V, P, Xs
V, P, Xs
Chemical kinetic rate parameters

## Slide 14: Polynomial Chaos Expansion
: multivariate polynomials that are orthogonal with respect to probability distribution of inputs
: PCE coefficients
Polynomial chaos expansion (PCE):
Used to represent uncertain system as sum of orthogonal polynomials and is used to form a surrogate model.
With Ordinary Least Squares (OLS) Regression

## Slide 15: Sobol’ Indices
Total Sobol’ indices:
Quantifies how much uncertainty in input parameter affects QoI on a normalized scale from 0 to 1
= : first-order Sobol’ index
D: total variance of Sobol’ decomposition

## Slide 16: Mixed UQ Problem Setup
Number of samples required for total order expansion:
p: polynomial order
n: number of uncertain parameters
p = 2
20 epistemic uncertain parameters
OSR = 2, Ne = 462
2 aleatory uncertain parameters
OSR = 2, Na = 12
Nt = Ne*Na
Nt = 5544

## Slide 17: Baseline Case Results

## Slide 18: Baseline Case Temperatures
T6 Condition B:
84.5% H2 / 15% He / 0.5% CH4
12.9 Pa, 16.4 km/s
T6 Condition C:
80% H2 / 15% He / 5% CH4
13.0 Pa, 16.3 km/s

## Slide 19: T6 B Baseline Case
Condition | Test gas composition (%v/v) | P (Pa) | Ushock (km/s)
T6 B | 84.5% H2 / 15% He / 0.5% CH4 | 12.9 | 16.4

## Slide 20: T6 C Baseline Case
Condition | Test gas composition (%v/v) | P (Pa) | Ushock (km/s)
T6 C | 80% H2 / 15% He / 5% CH4 | 13.0 | 16.3

## Slide 21: Spectral Features

## Slide 22: Spectral Features
Radiation bands in 350 – 570 nm range:
CH(A-X)
H Balmer -
C, C+ Atomic Lines
C2 Swan

## Slide 23: Spectral Features
Radiation bands in 350 – 570 nm range:
C Atomic Lines
C2 Swan

## Slide 24: Spectral Features
Radiation bands in 350 – 570 nm range:
C Atomic Lines
C2 Swan

## Slide 25: Spectral Features
Radiation bands in 350 – 570 nm range:
C2 Swan

## Slide 26: Spectral Features
Radiation bands in 350 – 570 nm range:
C2 Swan
C Atomic Lines
C2 Swan
CH(A-X)
H Balmer -
C, C+ Atomic Lines
C2 Swan
Strongest radiators: CH, C2

## Slide 27: Mixed UQ Results

## Slide 28: Peak Spectral Radiance Comparisons for T6 B

## Slide 29: Sobol’ Indices for Integrated Radiance (T6 B)
Integrated radiance uncertainty is dominated by uncertainty in experimentally measured velocity
Processes that form CH and C2 as well as H2 dissociation also contribute to uncertainty in integrated radiance

## Slide 30: Peak Spectral Radiance Comparisons for T6 B
CH(A-X)
H Balmer -
C, C+ Atomic Lines
C2 Swan

## Slide 31: Sobol’ Indices for Spectral Radiance at 430 nm (T6 B)
Spectral radiance uncertainty at 430 nm is dominated by uncertainty in experimentally measured velocity

## Slide 32: Peak Spectral Radiance Comparisons for T6 C

## Slide 33: Sobol’ Indices for Integrated Radiance for T6 C
Integrated radiance uncertainty is dominated by uncertainty in experimentally measured velocity
CH3 dissociation has a much larger effect on integrated spectral radiance than condition B

## Slide 34: Peak Spectral Radiance Comparisons for T6 C
CH(A-X)
H Balmer -
C, C+ Atomic Lines
C2 Swan

## Slide 35: Sobol’ Indices for Spectral Radiance at 430 nm for T6 C
Spectral radiance uncertainty at 430 nm is still dominated by uncertainty in velocity, but the contribution is less than for Condition B

## Slide 36: Peak Spectral Radiance Comparisons for T6 C
C Atomic Lines
C2 Swan

## Slide 37: Sobol’ Indices for Spectral Radiance at 514 nm for T6 C
Spectral radiance uncertainty at 514 nm is dominated by formation of CH, and formation of C2 also plays a role

## Slide 38: Data from NASA EAST Facility

## Slide 39: Experimental Data from EAST Facility: Shot 56 - 22
Condition | Test gas composition (%v/v) | P (Pa) | Ushock (km/s)
EAST 56 - 22 | 89% H2 / 11% He / 0% CH4 | 68 | 27.66

## Slide 40: EAST Shot 56 – 22 Visible
Condition | Test gas composition (%v/v) | P (Pa) | Ushock (km/s)
EAST 56 - 22 | 89% H2 / 11% He / 0% CH4 | 68 | 27.66
[12] Cruden, B.A. and Bogdanoff, D.W, “Shock Radiation Tests for Saturn and Uranus Entry Probes,” Journal of Spacecraft and Rockets, Vol. 54, No. 6, 2017, p. 1246-1257. https://doi.org/10.2514/1.A33891.

## Slide 41: EAST Shot 56 – 22 VUV and IR
Condition | Test gas composition (%v/v) | P (Pa) | Ushock (km/s)
EAST 56 - 22 | 89% H2 / 11% He / 0% CH4 | 68 | 27.66
[12] Cruden, B.A. and Bogdanoff, D.W, “Shock Radiation Tests for Saturn and Uranus Entry Probes,” Journal of Spacecraft and Rockets, Vol. 54, No. 6, 2017, p. 1246-1257. https://doi.org/10.2514/1.A33891.

## Slide 42: Spectral Features

## Slide 43: EAST Shot 56 – 22 Visible
H Balmer-
H Balmer-
H Balmer-
H Balmer-
H Balmer-
H Balmer-
H Balmer-
Blue
Red

## Slide 44: EAST Shot 56 – 22 VUV and IR
H Lyman-
H Paschen-
H Paschen-
H2 Lyman-Werner
VUV
IR

## Slide 45: UQ Results for Visible Regions
Blue
Red

## Slide 46: UQ Results for VUV and IR Regions
VUV
IR

## Slide 47: Sobol’ Indices for Integrated Radiance Visible Region
Blue
Red

## Slide 48: Sobol’ Indices for Integrated Radiance VUV & IR Regions
VUV
IR

## Slide 49: Summary
There is an existing gap in simulations and experiments for predicting the aerothermal environment for H2/He/CH4 systems
Mixed UQ framework is presented to investigate this gap that includes:
  Epistemic uncertainties from chemical kinetic rate parameters within computational modeling tools
  Aleatory uncertainties from experimental conditions in shock tube experiments
    T6 Stalker Tunnel at the University of Oxford
    EAST Facility at NASA Ames Research Center
Sobol’ indices are computed which help identify which parameters most contribute to uncertainty in QoIs (integrated radiance and spectral radiance at certain spectral features)

## Slide 50: Conclusions
T6 Stalker Tunnel:
  Uncertainty in spectral radiance predictions are mostly dominated by experimentally measured velocity
  Formation of CH and C2 also contribute to uncertainty
    Formation of C2 contribution is higher at spectral features from C2 Swan band
NASA EAST Facility:
  Uncertainty is dominated by hydrogen ionization reactions
    No CH4 in the freestream for this condition
  Experimental uncertainty is not the dominant effect on uncertainty
    Well-suited to solve the inverse problem

## Slide 51: Future Work
Reduce uncertainty in parameters with highest Sobol’ indices
  Statistical calibration of kinetic rate uncertainty
Mixed UQ framework can be applied to many experimental facilities/conditions
  Can help identify which data is suitable for Bayesian inference
  Can be used to identify critical facility uncertainties that may limit utility of existing data
Helps investigate existing gap between simulations and experiments for H2/He/CH4 systems

## Slide 52
Questions?
Email: cate.leszcz@colorado.edu
Acknowledgments
Funding:
NSF GRFP
The Smead Program
Helpful Conversations:
Dr. Tim Aiken

## Slide 53
Backup Slides

## Slide 54: Electronic Energy Data