## Slide 1: Modeling and simulation of thermochemical nonequilibrium flows during Titan atmospheric entry
Antonio Narracci, Francesco Bonelli, Davide Ninni, Gianpiero Colonna, Annarita Laricchiuta, Giuseppe Pascazio

## Slide 2
Dense nitrogen-methane atmosphere
Organic compounds
Hypersonic approach at Mach 22
Non-equilibrium
Titan atmospheric entry
Dragonfly octocopter concept
dragonfly.jhuapl.edu/

## Slide 3
Finite volume Navier-Stokes equations
Perfect-gas equation of state
Time integration splitting
3rd order Runge-Kutta
Gauss-Seidel
Mixture-specific transport properties
Wilke’s rule
Fick’s law
Catalytic wall model
Methodology: the solver

## Slide 4
Multi-temperature
Modeling of internal energy
Different temperatures
Computational efficiency
State-to-State
Definition of pseudo-species
Accuracy
Huge computational cost
Methodology: non-equilibrium modeling

## Slide 5
Test case
Freestream composition (volume) | N2 (95%), CH4 (5%)
Altitude, km | 269
Velocity, m/s | 5761
Density, kg/m3 | 1.491x10-4
Pressure, Pa | 6.91
Temperature, K | 152.7
Mach | 22.7
*N. Takashima, B. Hollis, E. Zoby, K. Sutton, J. Olejniczak, M. Wright, D. Prabhu, Preliminary Aerothermodynamics of Titan Aerocapture Aeroshell. 2006. https://doi.org/10.2514/6.2003-4952
Capsule design*
12 species: CH4, CH3, CH2, CH, NH, CN, C2, H2, N2, C, H, N
18 species: 12 species mixture plus CN+, N2+, N+, C+, H+, e-

## Slide 6
Computational domain
Capsule max diameter: 3.75m
Nodes: 141x141
Wall refinement: 5.0 x10-7 m
Shock wave refinement: 5.0 x10-4 m
Shock position (stagnation line): ~ 0.12 m
Reference discretization

## Slide 7
Temperature contour (Park, 18-species)
Model verification
*N. Takashima, B. Hollis, E. Zoby, K. Sutton, J. Olejniczak, M. Wright, D. Prabhu, Preliminary Aerothermodynamics of Titan Aerocapture Aeroshell. 2006. https://doi.org/10.2514/6.2003-4952
Comparison with literature data*
Ionization effects assessment
Park and Nelson multi-temperature models
Catalytic wall analysis
StS vs Park model comparison

## Slide 8
Reference comparison
18-species multi-temperature Park model verification with reference data

## Slide 9
Ionization analysis
18-species Park model and 12-species Park and Nelson models comparison

## Slide 10
Catalysis effects
12-species Park simulations under fully catalytic ( γc = 1 ) and non-catalytic ( γc = 0 ) wall
Wall reactions: N + N = N2
C + 4H = CH4

## Slide 11
Twelve vs two analysis
12 species: CH4, CH3, CH2, CH, NH,
CN, C2, H2, N2, C, H, N
Freestream composition (volume): N2 = 95%
CH4 = 5%
2 species: N2, N
Freestream composition (volume): N2 = 100%
Park simulations of the 12-species and 2-species mixtures

## Slide 12
Stagnation line species mass fraction with Park model
State-to-State analysis
N2:
68 vibrational levels
4 electronic levels
CN:
44 vibrational levels
2 electronic levels
Other species:
1 vibro-electronic (ground) level

## Slide 13
State-to-State analysis
12-species mixture simulation using Park and StS models (non catalytic wall)

## Slide 14
Conclusions…
successful development and verification
model comparison and selection
…and future work
extended State-to-State model
3D simulations

## Slide 15
Thank you for your attention!