## Slide 1
An Overview of Innovative Optical Observation Techniques Applied to Daytime and Cislunar Orbits and Real-Time Tracking

## Slide 2
Reference scenario
Earth orbit is no longer sparse
The operational baseline for SST/SSA is shifting from catalogue maintenance to continuous monitoring of a rapidly growing population.
Current debris environment
≈44’870
objects regularly tracked by space surveillance networks
≈15’200
functioning satellites still in space
≈1.2M
objects estimated between 1–10 cm
Detection, tracking, and cataloguing are becoming coupled problems across crowded LEO, high-altitude Earth orbits, and the emerging cislunar domain.
more objects and crowded orbitals regimes → more conjunctions, re-entry, fragmentations events → need innovative observation techniques → improve the tracking and the observability capabilities of the optical systems
Sources: ESA Space Environment Statistics, last updated 21 Apr 2026; ESA Space Environment Report 2025. Images: ESA Space Safety / ESA Multimedia.

## Slide 3
Index
Innovative optical observation techniques
Daylight observation, high-altitude detection, and real-time tracking address complementary gaps in current SSA/SST operations. Expand the capability of detection and monitoring with innovative optical observation techniques
Daylight optical observations
Extend optical data acquisition beyond the night-time window and test astrometric extraction under adverse sky-background conditions.
Cislunar detection
Assess the feasibility of observing faint objects above the GEO ring and toward lunar distances with 25 cm–1 m class sensors.
Real-time Stare-and-Chase tracking
Move from survey-only detections toward sufficient arcs for orbit determination and cataloguing of uncatalogued targets.
Contribution to the SSA/SST scenario
The contribution is not just “more observations”: it is extending the operational envelope of optical SST from nighttime cataloguing to robust acquisition in difficult visibility, geometry, and knowledge conditions.

## Slide 4
Daytime observations
Stars visibility during daytime, up to 2.5 J mag
El Sun 30°
El Sun 12°
El Sun 60°
El Sun 30°
El Sun 30°
El Sun 12°
El Sun 60°
El Sun 30°
Stars observed
Stars observed

## Slide 5
Daytime observations
Target observation test
OBSERVED OBJECTS VISIBLE EVEN AT LOCAL NOON:
  ISS
  Sl-16
  Bluewalker-3
  Bluewalker-6 / Spacemobile-006
Satellites Can be Detected during most of their passages.
NORAD ID: 25544
ISS at 13:13 UTC
10/12/2025
NORAD ID : 67232
Spacemobile-006 at 07:40 UTC
10/04/2026

## Slide 6
Daytime observations
SL-16 Campaign
Object parameters | 
Dry mass | 8.9 tons
Diameter | 3.90 m
Length | 11.047 m
Orbit parameters | 
Apogee | 850.0 km
Inclination | 71.0 °
Period | 101.7 minutes
SL-16 observed passages during daytime

## Slide 7
Cislunar observations
Reference scenario
The monitoring perimeter is expanding with lunar infrastructure, commercial services, and international exploration architectures.
What changes for SST/SSA
Objects are fainter and farther: over GEO orbits, highly eccentric and lunar-orbit regimes. Classical radar contribution decreases as range increases; optical assets become central. Tracking cannot rely only on precise a priori ephemerides: discovery-to-cataloguing pipelines are needed.
Artemis II completed a crewed lunar flyby on 1–10 Apr 2026.
Artemis III is scheduled for 2027; Artemis IV is targeted for early 2028.
NASA has already awarded 11 Commercial Lunar Payload Services (CLPS) lunar deliveries to 5 vendors, carrying >50 payloads through Nov 2028.
Current scenario

## Slide 8
Cislunar observations
Selected targets for observations tests
CISLUNAR OBJECTS |  |  |  |  |  |  |  |  | 
Object | TYPE | STATUS | COSPAR ID | NORAD ID | ID Horizons | TLE | Horizons Ephemerides | Observed | Observatory
ATLAS 5 CENTAUR R/B | Rocket Body | Uncontrolled | 2009-017B | 34714 |  | UPDATED | Not Available |  | GALHASSIN
ARIANE 5 R/B | Rocket Body | Uncontrolled | 199-9066B | 25990 |  | UPDATED | Not Available |  | SCUDO
CLUSTER II-FM5 | Scientific Payload | Re-entry October 2025 | 2000-045A | 26463 |  | OLD | Not Available |  | SCUDO
ARIANE 44P+3 R/B | Rocket Body | Uncontrolled | 1995-062B | 23716 |  | UPDATED | Not Available |  | GALHASSIN
CZ-38 R/B | Rocket Body | Uncontrolled | 2013-070B | 39459 |  | OLD | Not available 2021-05-31 21:36:00.001 |  | 
CXO (Chandra Observatory) | X-Ray telescope | Active | 1999-040B | 25867 | -151 | UPDATED | Available until 2026-10-08 12:01:09.182 |  | GALHASSIN
CLUSTER II-FM7 | Scientific Payload | End of life re-entry August 2026 | 2000-041A | 26410 |  | MID | Not Available |  | 
TESS (CICERO 10) | 6U CubeSat | Re-entry 2024 | 2018-088A | 43690 |  | OLD | Not Available |  | 
GEOTAIL | Scientific Payload | Deactivated 2022 | 1992-044A | 22049 |  | MID | Not Available |  | 
MMS-1 | Scientific Payload | Active | 2015-011A | 40482 | -140482 | UPDATED | Available until 2026-05-14 04:01:11.184 |  | 
INTEGRAL | Gamma-Ray telescope | Active | 2002-048A | 27540 | -198 | MID | Available until 2026-05-12 08:14:13.262 |  | 
CAPSTONE | 25Kg CubeSat | Active | 2022-070A | 52914 | -1176 | OLD | Available until 2026-04-17 00:01:09.186 |  | 
DANURI (KPLO) | Lunar Orbiter | Active | 2022-094A | 53365 | -155 | OLD | Available until 2026-10-31 20:05:53.142 |  | 
Chandrayaan 2 | Lunar Orbiter | Active | 2019-042A | 44441 | -153 -152 | VERY OLD | Available until 2019-09-06 20:28:00.000 |  | 
LRO | Lunar Orbiter | Active | 2009-031A | // | -85 |  | Available until 2027-10-11 00:01:09.182 |  | 
TESS | Telescope | Active | 2018-038A | 43435 | -95 | MID | Available until 2027-10-06 13:01:09.182 |  | 
ARTEMIS II – Orion Integrity | Multi-Purpose Crew Vehicle | Re-entry April 2026 | 2026-069A | 68538 | -1024 | OLD | Available until 2026-04-10 23:54:22.858 |  | SCUDO, GALHASSIN

## Slide 9
25990 - ARIANE 5 R/B
Observations - 2025-06-04 SCUDO: Sapienza Coupled University Debris Observatory Collepardo, Italy
Exp: 4s
Bin: 3x3
Observation:
            Observed: Descending to the perigee
            El = 27°-30°
            Lunar Elong = 130°
            Range = 50’000 Km
            Mean Magnitude = 13.5
            Phase Angle = 50°
Last stage of the Ariane 5 Rocket
Uncontrolled object

## Slide 10
26463 - CLUSTER II-FM5
Observations - 2025-07-21 SCUDO: Sapienza Coupled University Debris Observatory Collepardo, Italy
Exp: 15s
Bin: 2x2
Observation:
            Observed: Ascending to the apogee
            El = 30°-38°
            Lunar Elong = 86°
            Range = 56’000 Km
            Mean Magnitude = 15
            Phase Angle = 60°
Magnetospheric research project
Active @ observation time Re-Entry October 2025

## Slide 11
Artemis 2 Mission – Integrity Observations
Observations
SCUDO: Sapienza Coupled University Debris Observatory Collepardo (FR), Italy
Observed: 2026-04-10
Time: 03:04-04:00 UTC
Telescope: 1°x1° FoV 1200mm f4,8
Stacked: 128 frame @ 10s, clear
Sidereal Tracking
Horizon JPL ephemerides
Orion Integrity Artemis II
Elong = 28 °
Distance = 180’000Km
El = 14°
2 m
19 m
7,3 m

## Slide 12
Real Time Tracking
State-of-the-art
STARE: the system remains fixed in an initial pointing direction waiting for the object to cross the field of view.
CHASE: the system follows the object using the real time data acquired and integrate it in a control law to improve the tracking or follow the object without any a-priori orbital information.
The state of the art in real-time tracking orbital object with optical systems is refers mostly by the Stare and Chase strategy. The name of the stare and chase was coined after the merge of two observation strategies used in passive-optical systems namely survey and follow-up.

## Slide 13
Real Time Tracking Pipeline
Linear-Tracking

## Slide 14
Real time tracking
Real time detections and tracking
Stare phase based on a survey method. First rea-time detection of uncatalogued object initialize the chase phase.
STARE
CHASE
Chase phase start the real time follow up of the uncatalogued object. The video show the linear-tracking method based on a linear estimation for the next pointing.

## Slide 15
1
2
3
Real time tracking
Tracking maintenance
During the chasing phase, the measurements must be filtered to preserve track continuity, as other objects may enter the field of view together with the target. In addition, the target may be temporarily lost due to clouds or other external factors that degrade real-time detection performance. detection.
For this chasing phase we can see three different uncatalogued target chased during the night. The maximum tracking time for each follow-up it is fixed to 2 hours.
For the 1st and 2nd tracking we can see different lost of the target and the attempt procedure that try to spot again the target, due to high clouds in the FoV. The 3rd tracking instead it is maintain without problem for over the length of the visibility.
Lost detection due to high clouds in the FoV.
Outlier detection very elongated galaxy. Discarded by measurements filtering

## Slide 16
Real time tracking
Real time data acquisition: light curve
Tumbling uncatalogued object

## Slide 17
Thank you for your attention
Matteo Rossetti
Andrea Ederle
Lorenzo Cimino
Lorenzo Mariani
Fabrizio Piergentili