## Slide 1: A Performance-Based Orbital Slotting Framework for Long-Term Space Sustainability
Pietro Russo1, Giorgio Isoletta1, Roberto Opromolla1, Giancarmine Fasano1
1Department of Industrial Engineering, University of Naples Federico II
2nd Space Capacity Allocation for the Sustainability of Space Activities Workshop
Milan 3-5 Jun 2026

## Slide 2: Outline
Context and Problem Statement
Conclusions and Future Works
Test Cases and Results
2
3
4
5
1
Required Navigation Performance in aviation
Required Navigation Performance for STM

## Slide 3: Context and Problem Statement
1

## Slide 4
In recent years, the growing interest in space is leading to an increasing number of satellites and space debris in Earth’s orbit.
Chapter I: Context
54000 | Objects larger than 10 cm
1.2 mln | Objects from 1 cm to 10 cm
130 mln | Objects from 1 mm to 1 cm
ESA Space Environment Report (2025)
This poses significant challenges to the long-term sustainability of space. The increasing risks of overexploitation and collisions are shifting the attention on Space Traffic Management (STM) and cooperative Space Situational Awareness (cooperative SSA).
Space Environment. Credits: ESA

## Slide 5
The problem of space environment congestion is currently addressed through active coordination among all the operators, who manually handle conjunctions.
Chapter I: Context
Conjunction Events statistics for a set of representative targets (ESA Space Environment Report 2025)
As the space population grows, this approach can become unsustainable and ineffective. An integration of active and passive coordination is needed.

## Slide 6
An alternative and scalable approach is based on orbital coordination which enables the use of designated slots, optimizing orbital capacity, and minimizing the risk of conjunction and the operational burden associated with coordinating collision avoidance maneuvers.
Chapter I: Context
Pietro Russo, et al. “Analysis of Satellite Performance Requirements for Orbital slot maintenance”
Orbital Slotting Techniques
Inter-Shell Orbital Slotting
Intra-Shell Orbital Slotting
David Arnas, et al. “Definition of Low Earth Orbit slotting architectures using 2D lattice flower constellations”

## Slide 7
Chapter I: Problem Statement
In this context, there is a need to define the operational capabilities required at the STM system level to ensure safe orbital coordination.
Extending the Required Navigation Performance (RNP) concept from Air Traffic Management (ATM) and Unmanned Aircraft System Traffic Management (UTM) to STM enables a performance-based framework which can facilitate orbital coordination among diverse operators.

## Slide 8: Required Navigation Performance in aviation
2

## Slide 9
Chapter II: Required Navigation Performance in aviation
In ATM and UTM the Required Navigation Performance (RNP) is a Performance-Based Navigation (PBN) specification that enables aircraft operations along a desired flight path within the coverage of ground- or space-based navigation aids, or self-contained onboard navigation systems1.
RNP
(ATM & UTM)
Navigation System Error
Path Definition Error
Flight Technical Error
1International Civil Aviation Organization, “Performance-based Navigation Manual”
2International Civil Aviation Organization, “Unmanned Aircraft Systems Traffic Management (UTM) - A Common Framework with Core Principles for Global Harmonization”
True
Position
NSE
Estimated
Position
FTE
Defined
Path
PDE
Desired
Path
TSE (Total System Error)

## Slide 10: Required Navigation Performance for STM
3

## Slide 11
Chapter III: Required Navigation Performance for STM
Analogous to RNP criteria used in aviation, RNP for STM establishes a containment limit that must be met for a specified percentage of the spacecraft operational lifetime.
CONTROL: capability of the satellite to maintain the nominal trajectory.
TRACKING-NAVIGATION UNCERTAINTY: uncertainty in the satellite’s estimated position with respect to its true position. It depends on the performance of SST systems.
RNP
(STM)
Tracking-Navigation Uncertainty
(Navigation System Error)
Control
(Flight Technical
Error)

## Slide 12
Chapter III: Required Navigation Performance for STM
Under the assumption that control and tracking-navigation uncertainty are independent and Gaussian distributed, the RNP along each axis of the RSW reference frame is mathematically defined as:
= maximum allowable deviation from a nominal path that must be maintained for 95% of the operational flight time.
= non-zero mean error due to station-keeping strategy
= position standard deviation error due to station-keeping strategy
= tracking-navigation uncertainty (resulting from linear covariance propagation)
The proposed RNP definition establishes a link between satellite’s required performance and orbital slot size, transforming the latter from a static geometric allocation into a performance-based metric.
Russo, P., Isoletta, G., Opromolla, R., Fasano, G., “Satellite Required Navigation Performance for Space Traffic Management”, In: Proceedings of the 5th IAA Conference on Space Situational Awareness (ICSSA), Madrid (Spain), 7-9 April 2026

## Slide 13
Chapter III: Required Navigation Performance for STM
According to the shared information about the nominal trajectory and the required level of coordination, three levels of RNP can be proposed:
LEVEL 1 | ORBITAL SHELL
Coordination: Radial
Parameters:
RNP Definition: (95%)
LEVEL 2 | ORBITAL PLANE
Coordination: Radial + Cross-Track
Parameters: :
RNP Definition: (95%)
LEVEL 3 | FULL TRAJECTORY
Coordination: 4D (R, S, W, Time)
Parameters:
RNP Definition: (95%)
Legend: SMA: Semi-Major Axis | e: Eccentricity | i: Inclination | ω: Argument of Perigee | Ω: RAAN | M: Mean Anomaly | t₀: reference epoch
Russo, P., Isoletta, G., Opromolla, R., Fasano, G., “Satellite Required Navigation Performance for Space Traffic Management”, In: Proceedings of the 5th IAA Conference on Space Situational Awareness (ICSSA), Madrid (Spain), 7-9 April 2026

## Slide 14: Test Case and Results
4

## Slide 15
Chapter IV: Test Case and Results
Test Case | 
Orbital Regime | Low Earth Orbit ()
Orbit Type | Frozen Orbit
Ballistic Coefficient | 
Perturbation modelling | Atmospheric Drag, Solar Radiation Pressure, Third Body, J2-J3 gravity
Orbital Elements Theory | Brouwer-Lyddane
Tracking-Navigation Architectures | GNSS & Ground-Based Sensors (Radar and Telescope)
Test Case | 
Orbital Regime | 
Orbit Type | Frozen Orbit
Ballistic Coefficient | 
Perturbation modelling | Atmospheric Drag, Solar Radiation Pressure, Third Body, J2-J3 gravity
Orbital Elements Theory | Brouwer-Lyddane
Tracking-Navigation Architectures | GNSS & Ground-Based Sensors (Radar and Telescope)
Control Strategy | 
Level 1 | maintenance
Level 2 | maintenance
Level 3 | Full trajectory maintenance (drag make-up maneuvers)
Control Strategy | 
Level 1 | 
Level 2 | 
Level 3 | Full trajectory maintenance (drag make-up maneuvers)
The RNP concept is applied to a LEO satellite to quantify the relation between required performance and slot size.
Tracking Architecture |  | 
Orbital State Accuracy (Earth-Centered Inertial Frame) | GNSS | Ground-Based Sensor
X | 1 m | 150 m
Y | 1 m | 150 m
Z | 1 m | 150 m
VX | 0.001 m/s | 0.1 m/s
VY | 0.001 m/s | 0.1 m/s
VZ | 0.001 m/s | 0.1 m/s
Precise Orbit Determination Accuracy

## Slide 16
Chapter IV: Test Case and Results
Level 1 (Orbital Shell) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Level 1 (Orbital Shell) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Orbital Slot Size |  | 
RNP Level 1 | GNSS Scenario | Ground Based Scenario
Orbital Slot Size |  | 
RNP Level 1 | GNSS Scenario | Ground Based Scenario
Control Analysis
Tracking-Navigation Uncertainty Analysis

## Slide 17
Chapter IV: Test Case and Results
Level 2 (Orbital Plane) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Level 2 (Orbital Plane) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Control Analysis
Tracking-Navigation Uncertainty Analysis
Orbital Slot Size |  | 
RNP Level 2 | GNSS Scenario | Ground Based Scenario
Orbital Slot Size |  | 
RNP Level 2 | GNSS Scenario | Ground Based Scenario

## Slide 18
Chapter IV: Test Case and Results
Level 3 (Full Trajectory) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Level 3 (Full Trajectory) | 
Reference Epoch (UTC) | 2025-01-01T00:00:00.000
Orbital Slot Size |  | 
RNP Level 3 | GNSS Scenario | Ground Based Scenario
Orbital Slot Size |  | 
RNP Level 3 | GNSS Scenario | Ground Based Scenario
Control Analysis
Tracking-Navigation Uncertainty Analysis

## Slide 19: Conclusions and Future Works
5

## Slide 20: Conclusions
Chapter V: Conclusions and Future Works
Adaptation of the aviation-derived concept of Required Navigation Performance to Space Traffic Management
RNP classification based on the required level of coordination among operators
Establishment of a link between RNP and slot size, which enables a transition from static geometric allocations to performance-based orbital slots and provides a metric to determine an asset eligibility for operation within high-density environments
Future Work
Acknowledgments
This work has been developed within the project “Attività tecnico scientifiche di support a C-SSA/ISOC e simulazione di architetture di sensori per SST” funded by the Italian Space Agency (ASI).
Integration of safety margins for Collision Avoidance Maneuvers (CAM) into the RNP definition
Analysis of the impact of RNP on orbital capacity
Simulation of high-density scenarios to analyse how performance-based slotting can streamline conjunction analysis and enhance the efficiency of in-orbit deconfliction

## Slide 21: THANK YOU FOR YOUR ATTENTION
Contacts: pietro.russo2@unina.it
LinkedIn:
2nd Space Capacity Allocation for the Sustainability of Space Activities Workshop
Milan 3-5 Jun 2026