## Slide 1: GREEN SPECIES: Active control of the space debris population to define optimal mitigation policies to target a sustainable development of space activities
Second Space Capacity Allocation For The Sustainability of Space Activities Workshop
3–5 Jun 2026, Politecnico di Milano
Camilla Colombo, Martina Rusconi, Wiebke Retagne, Achraf Mizmizi, Juan Felipe Cabrera, Giacomo Borelli, Elisa Boccolari, Francesco De Bortoli

## Slide 2: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 3: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 4
The space debris problem
Space for humankind
The long-term sustainability of space activities will be possible if a change of behaviour is put in place.
Image credits: European Space Agency and Copernicus EU
Orbital environment trend: space debris tracked by space surveillance networks. Source: ESA’s Space Environment Report 2022.
[1] Maury T., Loubet P., Trisolini M., Gallice A., Sonnemann G., Colombo C., ”Assessing the impact of space debris on orbital resource in Life Cycle Assessment”, Science of the Total Environment, 2019.
Earth system trends: environmental stressors.
Notes: Space missions offer services of social and economic benefit for humankind and enable monitoring the condition of our planet. As recognised by the UN, space missions contribute to the achievement of the Sustainable Development Goals.
As our lives become more interconnected thanks to satellites, Space can be seen as the extension of our planet biosphere. As such, the long-term sustainability of space activities will be possible only if a change of behaviour is put in place by space operators.
Indeed, the growth of space debris is following an exponential trend, which is typical of many other Earth system trends. Immediate actions are needed to mitigate the increasing risk of collisions and enable the future use of Space as a common.

## Slide 5
CO2 emission. © Picture alliance/dpa
Ocean acidification. © University of Plymouth
Amazon rainforest deforestation. © REUTERS/Bruno Kelly
Space debris simulation. COMPASS Virtual Reality game. Actual space debris orbits. Larger object dimensions.
Number of fragments for explosion of CZ-6A rocket body happened on 13 Nov 2022 in low Earth orbit. Giudici L., Colombo C. 2022.
Spatial density of fragments for Cosmos-2251 collision.
Frey S. Colombo C. 2020.
Raise awareness of the space debris problem as an environmental issue.
Notes: The long-term impact of the project will hopefully reach other environmental sciences, as it will raise awareness of the space debris problem as an environmental issue.

## Slide 6: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 7
M1: Space debris model
Space debris environmental model
Aleatory and epistemic uncertainties
Economic forecasts
Space objects sources and sinks
Space object population control
Indexes
Policies and regulations
Orbital dynamics
Environment drivers
Environmental control and management
WP1
WP2
WP4
WP5
WP7
WP6
Uncertainty models
WP3
Methodology
Notes: I will develop a probabilistic space debris environmental model that includes all uncertainties. To predict the development of the New Space activities and compliance to mitigation guidelines, I will devise economic forecasts including expert opinions.

## Slide 8
Several debris evolutionary models exists
Statistical vs deterministic models
Cross-validated within the Inter Agency Debris Coordination Committee
Do not predict future but study possible evolution under different hypothesis on launches, post mission disposals, collisions and explosions, solar activity and density models
Results always as statistical distributions
Modelling of the space debris evolution
Space debris complex dynamics, affected by several overlapping uncertainties.
Sources
Launches
Collisions
Explosions
Sinks
Post mission disposals
Active debris removal missions
Re-entry due to atmospheric drag
Orbital mechanics
Earth gravity, Moon + Sun gravity perturbation
Non spherical mass distribution of Earth
Atmospheric drag (solar activity)
Solar radiation pressure

## Slide 9: The COMETA model
Propagate background fragments distribution
Fragments population
at time :
a, e, i, A/M
Time vector:
Compute total fragments distribution
Store density distribution
Total fragments distribution at time
NO
Fragmentation debris distributions at
For loop
Fragments distribution at times
Obtain intact objects mission profile
Intact objects population at time :
a, e, i, Ac , M, launch epoch,
activity status, species
Estimate collision and explosion probability
Fragmentation?
Trigger object breakup
YES
Objects IDs, type
Propagate fragmentation debris cloud
object at time
Objects at time
Background fragments distribution at times
Intact objects at times :
a, e, i, Ac , M, torb, activity status, species
Species launch model
[8] Giudici L., Colombo C., Horstmann A., Letizia F., Lemmens S., “Density-based evolutionary model of the space debris environment in low-Earth orbit,” Acta Astronautica, 2024.

## Slide 10: The COMETA model validation ongoing
[9] Letizia F., Bastida Virgili B., Lemmens S., “Assessment of orbital capacity thresholds through long-term simulations of the debris environment,” Advances in Space Research, 2023.
[10] Giudici L., Colombo C., Horstmann A., Lemmens S., Letizia S., “Continuity equation-based model for the assessment of the long-term effect of mitigation and remediation measures on the space debris environment,” IOC II, 2023.
Number of fragments > 10 cm over time
Cumulative number of catastrophic collisions over time

## Slide 11: Fragmentations: non trackable fragments
Effect of the impact of a 1 cm space debris onto the Sentinel-1A solar array [16].
Giudici L., Gonzalo J. L., Colombo C., “Density-based in-orbit collision risk model extension to any impact geometry”, Acta Astronautica, 2024.
Krag H., et al., “A 1 cm space debris impact onto the Sentinel-1A solar array,” Acta Astronautica, 2017.
Fragments flux in LEO as function of semi-major axis and inclination [15].
Fragments > 10 cm
Fragments > 1 cm
Fragmentations produce thousand of fragments in orbit
Non trackable fragments pose the highest risk,
  They cannot be tracked by space surveillance networks
  They are transparent to collision avoidance manoeuvres

## Slide 12: Fragmentations: evolution of clouds of fragments
Cabrera J. F., Ottoboni F., Stevenson E., Colombo C., “Fragmentation Cloud Modelling for Collision Risk Estimation in LEO”, 7th International Workshop on Key Topics in Orbit Propagation Applied to SSA, Toulon, May 27-29, 2026.
Giudici L., Trisolini M., Colombo C., “Probabilistic multi-dimensional debris cloud propagation subject to non-linear dynamics”, Advances in Space Research, 2023.
Fragments evolution in LEO, fragmentation at 800 km, 100 deg inclination, and argument of latitude equal to 0 degrees [17].
Fragments evolution in LEO, fragmentation at at 800 km, 100 deg inclination, and argument of latitude equal to 90 degrees [17].
Fragmentation cloud spread differently depending on their orbit and point of origin

## Slide 13: Fragmentations: increased collision risk
Oneweb-like fragmentation against Oneweb
  Fragmentation: 1200 km and 80 deg
  Target: 1200 km and 80 deg
Starlink-like fragmentation against Starlink
  Fragmentation: 400 km and 60 deg
  Target: 400 km and 60 deg
Cabrera J. F., Ottoboni F., Stevenson E., Colombo C., “Fragmentation Cloud Modelling for Collision Risk Estimation in LEO”, 7th International Workshop on Key Topics in Orbit Propagation Applied to SSA, Toulon, May 27-29, 2026.

## Slide 14
Modelling of the space debris evolution
Space debris complex dynamics, affected by several overlapping uncertainties.
To develop the first high-fidelity, multi-dimensional probabilistic space debris model.
To elaborate a unified approach for treating concurrently all uncertainties of physical nature.
WP1
WP2

## Slide 15
M1: Space debris model
Space debris environmental model
Aleatory and epistemic uncertainties
Economic forecasts
Space objects sources and sinks
Space object population control
Indexes
Policies and regulations
Orbital dynamics
Environment drivers
Environmental control and management
WP1
WP2
WP4
WP5
WP7
WP6
Future launch traffic
Uncertainty models
WP3
Methodology
Notes: I will develop a probabilistic space debris environmental model that includes all uncertainties. To predict the development of the New Space activities and compliance to mitigation guidelines, I will devise economic forecasts including expert opinions.

## Slide 16
Current launch traffic differ much from the past one
Economic factors need to be included in launch traffic model, to adapt to changing trends
Moving from modelling to forecasting
Launch traffic model
Space debris complex dynamics, affected by several overlapping uncertainties and factors of economic nature.
ESA - Space debris by the numbers, 21 April 2026, https://www.esa.int/Space_Safety/Space_Debris/Space_debris_by_the_numbers
Evolution of the launch traffic in number of payloads objects.

## Slide 17: Some representative large constellation programmes
Generation | Altitude | Inclination | Planned
Gen 1 | 540 km | 53.2° | 1,584
 | 550 km | 53.0° | 1,584
 | 560 km | 97.6° | 520
 | 570 km | 70.0° | 720
Gen 2 | 340 km | 53.0° | <15,000
 | 345 km | 48.0° | 
 | 350 km | 38.0° | 
 | 355 km | 43.0° | 
 | 360 km | 96.9° | 
 | 365 km | 28.0 - 32.0° | 
 | 475 km | 28.0 - 32.0° | 
 | 480 km | 53.0° | 
 | 485 km | 43.0° | 
 | 525 km | 53.0° | 
 | 530 km | 43.0° | 
 | 535 km | 33.0° | 
Constellation | In orbit [7] | Planned
Starlink | ~10,373 | ~12,000
G60 Qianfan | ~144 | ~15,000
GW Guowang | ~168 | 12,992
Amazon Leo (Kuiper) | ~304 | 3,236
OneWeb | ~656 | ~1,100
Telesat |  | ~198
IRIS2 |  | ~264+18
https://spacemapper.cn/en-us/, 10 May 2026
https://sma.nasa.gov/sma-disciplines/orbital-debris, 16 May 2026
chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://docs.fcc.gov/public/attachments/DA-26-36A1.pdf
Starlink mission architecture [8, 9].
Large constellations are injecting into orbit an unprecedented number of active spacecraft
Notes: There are already many influential large constellations (such as Starlink, G60, GW, Amazon LEO/Kuiper, and OneWeb)
e.g. over 10,000 Starlink satellites occupy different orbital shells. From 540-570 km for the first generation to 340-535 km for the second, the orbits are gradually lowering and distribution more extensive.

## Slide 18: From GEO orbital slots to LEO orbital shells
https://satellitemap.space/, 17 May 2026
A LEO large constellation occupy almost a full orbital altitude shell. Once a constellation is in place at a give altitude, it is difficult to place another constellation at the same altitude.
Notes: Thanks to the work of satellitemap, we can visualise more intuitively the space environment surrounding our planet: (Please play the animation).
This demonstrates the distribution of Starlink satellites around the Earth. And, as we outlined in the table on the previous slide, we anticipate seeing two to three more mega-constellations of this massive scale.
10373 in orbit
Screenshot obtained from https://Satellitemap.space/vis/Constellation/starlink showing the Starlink satellites currently in orbit. The night sky is increasingly affected not only by terrestrial light pollution, but also by the rapid proliferation of artificial satellites, particularly large megaconstellations composed of hundreds or even thousands of spacecraft. Among these, SpaceX’s Starlink constellation represents the most prominent and rapidly expanding example.

## Slide 19: Extrapolation of future launches: numbers
Non-constellation launches determined based on a SARIMAX based forecast including Gross Domestic Product information [11]
Mean rate launch forecast
8 constellations (5-year replenishment is assumed).
Only those constellations that have launched satellites are considered.
Retagne W., Colombo C., "Satellite launch traffic forecast based on the global Gross Domestic Product and constellation plans", Acta Astronautica, Vol. 246, 2026, pp. 717-733, https://doi.org/10.1016/j.actaastro.2026.04.046.
Historical launch traffic until 2024 and then future mean rate forecast including constellations, assuming a 5-year replenishment
Space debris complex dynamics, affected by several overlapping uncertainties and factors of economic nature.
Notes: This plot displays the historical launch traffic until 2024 and then the future mean rate forecast including constellations, assuming a 5 year replenishment. The launches are broken down by non-constellation and constellation launches. Of the 15 constellations plotted, 8 have not finished their launch plans and are projected into the future. Constellation launches make up the majority of the launches. In total it is projected to reach up to 11,000 launches per year. The main contributions are from Starlink, Guowang and Qianfan
The future forecast without constellations based on the SARIMAX model. The mean forecast predicts a steady growth with some slight variations. The confidence interval grows going further into the future. This can serve as an upper and lower bound for future launch forecasts. (For interpretation of the references to colour in this figure legend, the reader is referred to the web version of this article.)

## Slide 20: Extrapolation of future launches: orbital slots
Future launch traffic evolution distribution in orbital slots in inclination and semi-major axis
Retagne W., Colombo C., “Studies of future launch traffic effect on the space debris environment evolution”, In preparation 2026.

## Slide 21: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 22
M1: Space debris model
Space debris environmental model
Aleatory and epistemic uncertainties
Economic forecasts
Space objects sources and sinks
Space object population control
Policies and regulations
Orbital dynamics
Ideal technical mitigation solutions
Environment drivers
Environmental control and management
M2: Dynamical system theory analyses
M3: Control actions
WP1
WP2
WP4
WP5
WP7
WP6
Uncertainty models
Indexes
WP5
Methodology
Notes: A first control loop will allow dynamical analyses of the debris complex system, to define robust yet ideal control actions, acting on different time scales and orbital regions.

## Slide 23: Space debris population control
Performance function
Model of the space environment evolution
Feedback controller
Control logic
Mitigation strategy
Definition of sustainable target scenario
Orbital slots representation
How to control it?
Post mission disposal compliance
Active debris removal missions
Re-entry due to atmospheric drag
Launches
Collision avoidance maneouvres
Urgent to control the space debris population as a whole and to integrate debris mitigation in Space traffic management.

## Slide 24: Space debris population control
Fragments
Inactive objects
Propagation time 50 y
Control inputs: PMD compliance and ADR rate (maximum 30 ADR per year per shell)
Control target: keep the initial number and distribution of inactive objects and fragments.
M. Rusconi, C. Colombo., A Model-Based Control Framework for Space Debris Management. Acta Astronautica, 2025.
Notes: - 2024 population
- propagation time 50y
- categories: Active objects (AO), Inactive objects (IO), Fragments (FR). Active objects include: active Payload and Constellation (optional), with active lifetime of 8 years and 5 years respectively; Inactive objects include: inactive Payload and Constellation (optional) and large Debris.
- launch traffic: 8 year repeating cycle of historical data for Payloads; full deployment and replenishment of Constellation (based on DISCOS available data)
- control inputs: PMD compliance and ADR rate (maximum 30 ADR per year per shell --> large flexibility)
- control target: keep the initial number and distribution of Inactive objects and Fragments

## Slide 25: Space debris population control
Propagation time 50 y
Control inputs: PMD compliance and ADR rate (maximum 30 ADR per year per shell)
Control target: keep the initial number and distribution of inactive objects and fragments.
Number of fragments + Inactive objects
Post mission disposal guidelines (better if binding laws) can be used to control the overall status of the space object environment
Debris mitigation guidelines (better if binding laws) should react to the quickly evolving space ecosystem
Active debris removal is necessary to limit future fragmentation events
M. Rusconi, C. Colombo., A Model-Based Control Framework for Space Debris Management. Acta Astronautica, 2025.
Notes: - 2024 population
- propagation time 50y
- categories: Active objects (AO), Inactive objects (IO), Fragments (FR). Active objects include: active Payload and Constellation (optional), with active lifetime of 8 years and 5 years respectively; Inactive objects include: inactive Payload and Constellation (optional) and large Debris.
- launch traffic: 8 year repeating cycle of historical data for Payloads; full deployment and replenishment of Constellation (based on DISCOS available data)
- control inputs: PMD compliance and ADR rate (maximum 30 ADR per year per shell --> large flexibility)
- control target: keep the initial number and distribution of Inactive objects and Fragments

## Slide 26: Collision avoidance manoeuvres
Space more accessible
Increasing number of objects
New challenges to Space Traffic Management
Autonomous Collision Avoidance Manoeuvre
Polli E. M., Gonzalo J. L., Colombo C., “Semi-analytical model for autonomous fuel-optimal low-thrust collision avoidance with eclipse constraints”, 35th AAS/AIAA Space Flight Mechanics Meeting, Lihue, Kaua’i, Hawaii, 19-23 Jan. 2025.

## Slide 27: Collision avoidance manoeuvres design
Design of collision avoidance manoeuvres considering attitude and eclipse constraints
Minimise the probability of collision at the time of close approach
Polli E. M., Gonzalo J. L., Colombo C., “Convex Fuel-Optimal Low-Thrust Collision Avoidance with Operational Constraints”, 5th IAA Conference on Space Situational Awareness (ICSSA).

## Slide 28
Space debris population control
Modelling of the space debris evolution
Space debris complex dynamics, affected by several overlapping uncertainties.
Urgent to control the space debris population as a whole and to integrate debris mitigation in Space traffic management.
To develop the first high-fidelity, multi-dimensional probabilistic space debris model.
To elaborate a unified approach for treating concurrently all uncertainties of physical nature.
Space debris as a system of systems
A feedback controller

## Slide 29: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 30
Space debris population control
Policies and regulations
Modelling of the space debris evolution
A new interdisciplinary framework for the modelling of the space debris population, and the control of its evolution.
Space debris complex dynamics, affected by several overlapping uncertainties and factors of economic nature.
Urgent to control the space debris population as a whole and to integrate debris mitigation in Space traffic management.
Control actions to be translated into policies and regulations to allow the definition of mitigation guidelines.
To develop the first high-fidelity, multi-dimensional probabilistic space debris model.
To elaborate a unified approach for treating concurrently all uncertainties of physical, economic, and political nature.
Space debris as a system of systems
A robust time-delay feedback controller to tackle uncertainties in prediction and delays due to the implementation of debris mitigation policies.
Quantitative indexes
To measure the environmental impact and the social and economic benefit of a mission to humankind.
To define policies and regulations to control the space debris population.
WP1
WP2
WP3
WP4
WP5
WP6
WP7

## Slide 31
M1: Space debris model
Space debris environmental model
Aleatory and epistemic uncertainties
Economic forecasts
Space objects sources and sinks
Space object population control
Policies and regulations
Orbital dynamics
Ideal technical mitigation solutions
Debris mitigation guidelines
Environment drivers
Environmental control and management
M6: Policy-actuated control actions
M4: Indexes
M3: Control actions
WP1
WP2
WP3
WP4
WP7
WP6
Future launch traffic
Uncertainty models
Indexes
WP5
M2: Dynamical system theory analyses
Methodology
Notes: I will then transform these technical feedback solutions into policies and regulations that will operate as the actuator of a real controlled system to define debris mitigation guidelines.

## Slide 32: Evaluation of sustainability impact with indicators
Space debris indicator for in-orbit segment [22]
Atmosphere pollution for re-entry
Light pollution indicator [30]
Orbital resource use [31]
Social benefit of a mission [5]
Casualty risk at re-entry [31]
Zuliani C., Santoro V., Nugnes M., Colombo C., Social benefit assessment of Earth observation missions through the SDG20230, 72nd International Astronautical Congress (IAC), Dubai, United Arab Emirates, 25-29 October 2021. IAC-21-B1.5.3.
Colombo C., Muciaccia M., Giudici L., Gonzalo J. L., Masat A., Trisolini M., del Campo B., Letizia F., Lemmens F. “Tracking the health of the space debris environment with THEMIS, EUCASS-CEAS Conference 2023, 9-13 Jul. 2023, Lausanne.
Littoriano G., Colombo C., Nastasi A., Falco C., “Modelling of spacecraft apparent brightness A study on OneWeb constellation satellites”, Advances in Space Research, Vol. 74, Issue 3, 2024, pp. 1392-1409, ISSN 0273-1177.
Colombo C., Letizia F., Trisolini M., Lewis, H. G., Chanoine A., Duvernois, P.-A., Austin J., Lemmens S. (2017), “Life cycle assessment indicator for space debris”. 7th European Conference on Space Debris, , Darmstadt, Germany. 18 - 21 Apr 2017.
Borelli G., Trisolini M., Massari M., Colombo C. , “Comprehensive ranking framework for active debris removal mission candidates. Proc. 8th European Conference on Space Debris, 2021.
Active debris removal [32]

## Slide 33: Evaluation of sustainability impact with indicators
Space debris indicator for in-orbit segment

## Slide 34: THEMIS for Tracking the Health of the Environment and Missions in Space
Collision probability
Fragmentation effect
Explosion probability
Risk metric:
Index profile for a single OneWeb satellite considering several disposal options
Operational phase, including operations
Post mission disposal, including failures
Colombo C., Muciaccia M., Giudici L., Gonzalo J. L., Masat A., Trisolini M., del Campo B., Letizia F., Lemmens F. “Tracking the health of the space debris environment with THEMIS, EUCASS-CEAS Conference 2023, 9-13 Jul. 2023, Lausanne.
Over the mission time life:
Operational phase, including operations
Post mission disposal, including failures

## Slide 35: THEMIS for Tracking the Health of the Environment and Missions in Space
Mission design
Debris risk metric:
Collision/explosion probability
  Orbit
  Cross-area
  CAM reliability
  PMD
  Failures
  Fragment trackability
Effects
  Orbital region where the possible fragmentation takes place
  Mass
  Positions and area of other active spacecraft
  Relative orbit geometries
Capacity evaluation
Impact of a space mission on the space environment based on mission information
Aggregate over all objects in the population to measure the orbital capacity
Mitigation guideline
Licence procedure
Could be integrated into licencing process (e.g. ITU)
Insurance evaluation
Depending on the orbital slot the risk is very different
Drive de definition of mitigation guidelines
Colombo C., Muciaccia M., Giudici L., Gonzalo J. L., Masat A., Trisolini M., del Campo B., Letizia F., Lemmens F. “Tracking the health of the space debris environment with THEMIS, EUCASS-CEAS Conference 2023, 9-13 Jul. 2023, Lausanne.
Debris risk metrics can be used to quantitively assess the debris-generating impact of a space missions for several applications:

## Slide 36: Debris index indicators: OneWeb-like mission
Sentinel-1C assumptions:
  mass: 2185 kg, cross-sectional area: 19.7 m²
  chemical monopropellant propulsion
  collision avoidance manoeuvre reliability: 0.9
  PMD reliability: 0.9
  The mission lifetime 7 years.
The OneWeb spacecraft:
  mass: 148 kg, cross-sectional area: 3.464 m²
  electric propulsion, Ion 1 (T5)
  PMD reliability: 0.9
The OneWeb constellation is modelled with:
  656 satellites
  constellation lifetime: 50 years
  single spacecraft lifetime: 6 years
A large constellation uses a larger share of the overall capacity than a single satellite mission.
Debris index depends on orbit altitude and inclination, cross sectional area, mass, PMD
Michahelles M., Muciaccia A., Lück D., Retagne W., Colombo C., “Environmental impact of large constellations using the space debris THEMIS indicator”, 16th EASN international-conference, in preparation 2026.
Notes: Sentinel-1C assumptions
Sentinel-1C is modelled as a payload with:
- mass: 2185.253 kg
- cross-sectional area: 19.705 m²
- chemical monopropellant propulsion
- collision avoidance manoeuvre reliability: 0.9
- PMD reliability: 0.9
The mission lifetime is assumed to be 7 years.
Sentinel-1C phases
Deployment
The deployment phase includes launch and injection.
Launch is modelled from 2024-01-01 to 2024-01-02 at:
- semi-major axis: 7074 km
- eccentricity: 0.0
- inclination: 98.19 deg
Injection is modelled from 2025-01-01 to 2025-03-01 at:
- semi-major axis: 7073.89 km
- eccentricity: 0.0001314
- inclination: 98.1824 deg
Operational phase
The operational phase is modelled from 2026-01-01 to 2033-01-01 with:
- semi-major axis: 7073.69 km
- eccentricity: 0.0001314
- inclination: 98.1824 deg
Disposal phase
Two disposal branches are included:
1. PMD branch
Direct disposal starting on 2033-01-01 using the King-Hele propagator with:
- drag coefficient: 2.2
- reflectivity coefficient: 1.3
- target perigee: 580 km
- lifetime limit: 25 years
2. No-PMD branch
The spacecraft remains in orbit from 2033-01-01 and naturally evolves according to the King-Hele propagation.
OneWeb assumptions
The OneWeb spacecraft is modelled as a payload with:
- mass: 148 kg
- cross-sectional area: 3.464 m²
- electric propulsion, Ion 1 (T5)
- PMD reliability: 0.9
The OneWeb constellation is modelled with:
- 656 satellites
- constellation lifetime: 50 years
- single spacecraft lifetime: 6 years
OneWeb phases
Deployment
The deployment phase includes launch and injection.
Launch is modelled from 2019-01-01 to 2019-01-02 at:
- semi-major axis: 7375 km
- eccentricity: 0.0001
- inclination: 87.77 deg
Injection is modelled from 2020-01-01 to 2020-04-01 at:
- semi-major axis: 7580 km
- eccentricity: 0.0001
- inclination: 87.9 deg
Operational phase
The operational phase is modelled from 2021-01-01 to 2031-01-01.
The operational orbit is assumed to be:
- semi-major axis: 7580 km
- eccentricity: 0.0001
- inclination: 87.9 deg
Disposal phase
Two disposal branches are included:
1. PMD branch
The satellite performs direct disposal starting on 2031-01-01.
The disposal is propagated using the King-Hele model with:
- drag coefficient: 2.2
- reflectivity coefficient: 1.3
- target perigee: 200 km
- lifetime limit: 5 years
2. No-PMD branch
The satellite remains in the operational orbit from 2031-01-01 and naturally evolves according to the King-Hele propagation.

## Slide 37: Effect maps with constellations
Fragmentation effect:
When an object fragments in an orbital slot, the entire population of active objects is affected by the generated debris cloud as:
  A debris cloud is generated and reaches in time different orbital slots
  This causes an increased operational effort due to an increased collision risk
Muciaccia A., Giudici L., Letizia F., Trisolini M, Gonzalo J. L., Colombo C., “Evaluating the environmental impact of space missions”, Acta Astronautica, 2025-11 doi: 10.1016/j.actaastro.2025.06.024.

## Slide 38: Evaluation of sustainability impact with indicators
Light pollution indicator [30]

## Slide 39: Brightness estimation model
Brightness model can be used to quantitively assess the brightness of a satellite for:
System design
Trade-off different design solution to reduce brightness
Attitude constraint
Optimise attitude for minimisation of brightness
Brightness indicator
Define brightness indicator
Mizmizi A., Colombo C., “Satellite Brightness Model”, 2nd Space capacity allocation for the sustainability of space activities workshop, Milano, Jun 2026

## Slide 40: Evaluation of sustainability impact with indicators
Social benefit of a mission

## Slide 41: Socio-economic impact of space
Modelling approach
How well?
What?
How frequently?
Where?
The core of the modelling is made of the four performance indices focusing on the payload and orbit main characterising factors
Spectral efficiency index ISpectr (0-100)
Spatial resolution index ISR (0-100)
Earth coverage index ICov (0-100)
Temporal resolution index ITR (0-100)
[18] Zuliani C., Santoro V., Nugnes M., Colombo C., Social benefit assessment of Earth observation missions through the SDG20230, 72nd International Astronautical Congress (IAC), Dubai, United Arab Emirates, 25-29 October 2021. IAC-21-B1.5.3

## Slide 42: Socio-economic impact of space
Earth observation services contribution to the SDGs and SDG indices
EO majorly contributes to Goal 13 (Climate Action), followed by Goal 15 (Life on Land) and Goal 12 (Responsible Consumption and Production)
Major contributions from Built-up land and Limnology services
Two sets of indices:
    Relative indices: contribution of a mission to the SDGs with respect to given service maximum capability
    Absolute indices: it considers the maximum value among all the services capability
[18] Zuliani C., Santoro V., Nugnes M., Colombo C., Social benefit assessment of Earth observation missions through the SDG20230, 72nd International Astronautical Congress (IAC), Dubai, United Arab Emirates, 25-29 October 2021. IAC-21-B1.5.3

## Slide 43: Evaluation of sustainability impact with indicators
Active debris removal

## Slide 44: Active debris removal indicator
What object should we remove?
Development of an indicator to account various aspect of ADR impacts and complexity
Environmental index
Models the risk and the effect of in-orbit collisions
Measures the impact removing an object to the long-term sustainability of the orbital space
Main dependencies on object flux, mass, expected lifetime
[19] Borelli G., Trisolini M., Massari M., Colombo C. , “Comprehensive ranking framework for active debris removal mission candidates. 8th European Conference on Space Debris, 2021.
[20] Anselmo L., Pardini C., “Ranking upper stages in low Earth orbit for active removal”, Acta Astronautica, Vol. 122, June 2016, pp. 19–27.
[21] Borelli, G., Colombo, C., “Space Debris Index Definition for Multi-purpose Active Debris Removal Mission Design”, 2025, Under Review in Advances of Space Research.
Operability index
Models the complexity arising from rigid capture for removal [19,21]
Measures the feasibility of capturing the in-space object
Main dependencies on rotational state, mass, shape, illumination conditions
Economic index
Models the commercial value of the regions occupied [19,21]
Measures the interest in clearing specific orbital regions from a commercial point of view
Main dependencies on active satellites mass distribution in orbit, revenue streams generated by satellite types.

## Slide 45: Active debris removal indicator
What object should we remove?
Development of an indicator to account various aspect of ADR impacts and complexity
Generation of rankings based on user needs and priorities
Easy to integrate into mission design tools for multiple target ADR planning

## Slide 46: Outline
Introduction
Space debris model
Controlling the space object population
Integrated index approach
Conclusions

## Slide 47
M7: Revenue system for sustainable Space
M1: Space debris model
Space debris environmental model
Aleatory and epistemic uncertainties
Economic forecasts
Space objects sources and sinks
Space object population control
Indexes
Policies and regulations
Orbital dynamics
Ideal technical mitigation solutions
Environment drivers
Environmental control and management
M6: Policy-actuated control actions
M4: Indexes
M3: Control actions
M5: Revenue model for sustainable space
WP1
WP2
WP3
WP4
WP5
WP7
WP6
Future launch traffic
Uncertainty models
M2: Dynamical system theory analyses
Debris mitigation guidelines
Methodology
Notes: My project will generate the first economic model for a revenue system for Sustainable Space, by leveraging approaches from the management of the global climate.

## Slide 48: Final considerations
Great steps have been made so far to discuss space sustainability at international level: IADC mitigation guidelines, UN COPUOS mitigation guidelines, ESA zero debris charter, etc.
Operator use good practices for short term STM: post mission disposal (5 years for large constellations), collision avoidance manoeuvres, passivation
Legal framework (e.g., EU space act under discussion, French space law, Italian space law, etc.). Not yet international regulation.
Orbital slots:
  No rules so far for orbital slotting
  Slots are in some way “controlled” by the ITU licencing procedure (just telecom band licence)
  “Race” to get the perfect slot (economic competition)
  Need for other and future missions to transits through LEO occupied shells
  Even if operations are done in a very responsible way, fragmentations and explosion happen

## Slide 49: Final considerations
Discussion at IADC on space debris indicators and how to they compare in measuring the capacity.
Tools available to evaluate space debris impact of missions (e.g., ESA, ASI, CNES, DLR, JAXA, UKSA, NASA, CNSA)
Urgent need for international cooperation, discussion and coordination
  How to define orbital slotting/orbital shells rules?
  How to define threshold for shells/slot or in general?
Space as a common

## Slide 50
Camilla Colombo, Gabriella Gaias, Andrea Muciaccia, Martina Rusconi, Mathilda Bolis, Eduardo Polli, Francesca Ottoboni, Daniel Lück, Juan Felipe Cabrera, Yifan Cai, Alessandro Michelazzi, Alessandro Scalvini, Francesco De Bortoli, Wiebke Retagne, Achraf Mizmizi, Margherita Michahelles, Mara Terra Nadab, Paolo Cirrincione Pazè, Antonio Rossi, Sveva Cutino
This research received funding from the European Research Council (ERC) under the European Union’s Horizon Europe research and innovation program as part of the GREEN SPECIES project (Grant agreement No 101089265).

## Slide 51: References (1/4)
Wood L., Satellite constellation networks, pp. 13-34, https://link.springer.com/chapter/10.1007/978-1-4615-0431-3_2
Huang S., Colombo C., Bernelli-Zazzera F. , "Multi-criteria design of continuous global coverage Walker and Street-of-Coverage constellations through property assessment", Acta Astronautica, Vol. 188, 2021, pp. 151-170, https://doi.org/10.1016/j.actaastro.2021.07.002.
https://www.gsc-europa.eu/system-service-status/constellation-information
https://www.iridium.com/network
Zuliani C., Santoro V., Nugnes M., Colombo C., “Social benefit assessment of Earth observation missions through the SDG20230”, 72nd International Astronautical Congress (IAC), Dubai, United Arab Emirates, 25-29 Oct. 2021. IAC-21-B1.5.3
SpaceX Starlink Network Architecture and System Elements | RF Wireless World. https://www.rfwireless-world.com
https://spacemapper.cn/en-us/, 10 May 2026
https://sma.nasa.gov/sma-disciplines/orbital-debris, 16 May 2026
chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://docs.fcc.gov/public/attachments/DA-26-36A1.pdf
https://satellitemap.space/, 17 May 2026
Retagne W., Colombo C., "Satellite launch traffic forecast based on the global Gross Domestic Product and constellation plans", Acta Astronautica, Vol. 246, 2026, pp. 717-733, https://doi.org/10.1016/j.actaastro.2026.04.046.

## Slide 52: References (2/4)
Retagne W., Colombo C., “Studies of future launch traffic effect on the space debris environment evolution”, In preparation 2026.
ESA - Space debris by the numbers, 21 April 2026, https://www.esa.int/Space_Safety/Space_Debris/Space_debris_by_the_numbers
Maury T., Loubet P., Trisolini M., Gallice A., Sonnemann G., Colombo C., ”Assessing the impact of space debris on orbital resource in Life Cycle Assessment”, Science of the Total Environment, 2019.
Giudici L., Gonzalo J. L., Colombo C., “Density-based in-orbit collision risk model extension to any impact geometry”, Acta Astronautica, 2024.
Krag H., et al., “A 1 cm space debris impact onto the Sentinel-1A solar array,” Acta Astronautica, 2017.
Cabrera J. F., Ottoboni F., Stevenson E., Colombo C., “Fragmentation Cloud Modelling for Collision Risk Estimation in LEO”, 7th International Workshop on Key Topics in Orbit Propagation Applied to SSA, Toulon, May 27-29, 2026.
Giudici L., Trisolini M., Colombo C., “Probabilistic multi-dimensional debris cloud propagation subject to non-linear dynamics”, Advances in Space Research, 2023.
Polli E. M., Gonzalo J. L., Colombo C., “Semi-analytical model for autonomous fuel-optimal low-thrust collision avoidance with eclipse constraints”, 35th AAS/AIAA Space Flight Mechanics Meeting, Lihue, Kaua’i, Hawaii, 19-23 Jan. 2025.
Polli E. M., Gonzalo J. L., Colombo C., “Convex Fuel-Optimal Low-Thrust Collision Avoidance with Operational Constraints”, 5th IAA Conference on Space Situational Awareness (ICSSA).

## Slide 53: References (3/4)
Rusconi M., Colombo C., “Application of active feedback control for investigation of debris mitigation strategies on a density-based model of the population evolution”, 75th IAC.
Colombo C., Muciaccia M., Giudici L., Gonzalo J. L., Masat A., Trisolini M., del Campo B., Letizia F., Lemmens F. “Tracking the health of the space debris environment with THEMIS, EUCASS-CEAS Conference 2023, 9-13 Jul. 2023, Lausanne.
Michahelles M., Colombo C., Muciaccia A., Lück D., “Large constellation index evaluation with THEMIS”, In preparation, May 2026.
Muciaccia A., Giudici L., Letizia F., Trisolini M, Gonzalo J. L., Colombo C., “Evaluating the environmental impact of space missions”, Acta Astronautica, 2025-11 doi: 10.1016/j.actaastro.2025.06.024.
Letizia F., Colombo C., Rossi A., Muciaccia A., Giudici L., Harada R., Kawamoto S. Böttcher L., Ruch V., Taillan C., A comparative assessment of object-based index formulations through long-term simulations of the space debris environment in Earth orbit, Acta Astronautica, 2026-10, doi: 10.1016/j.actaastro.2026.05.005
https://apod.nasa.gov/apod/ap260427.html
Walker, C., Hall, J., Allen, L., Green, R., Seitzer, P., Tyson, T., ... & Yoachim, P. (2020). Impact of satellite constellations on optical astronomy and recommendations toward mitigations. Bulletin of the American Astronomical Society, 52 (2).
United Nations General Assembly, Report of the Committee on the Peaceful Uses of Outer Space, Sixty-fifth Session, Official Records of the General Assembly, Seventy-seventh Session, Supplement No. 20 (A/77/20), 2022.

## Slide 54: References (4/4)
Mizmizi A., Colombo C., “Satellite Brightness Model”, 2nd Space capacity allocation for the sustainability of space activities workshop, Milano, Jun 2026.
Littoriano G., Colombo C., Nastasi A., Falco C., “Modelling of spacecraft apparent brightness A study on OneWeb constellation satellites”, Advances in Space Research, Vol. 74, Issue 3, 2024, pp. 1392-1409, ISSN 0273-1177.
Colombo C., Letizia F., Trisolini M., Lewis, H. G., Chanoine A., Duvernois, P.-A., Austin J., Lemmens S. (2017), “Life cycle assessment indicator for space debris”. 7th European Conference on Space Debris, , Darmstadt, Germany. 18 - 21 Apr 2017.
Borelli G., Trisolini M., Massari M., Colombo C. , “Comprehensive ranking framework for active debris removal mission candidates. Proc. 8th European Conference on Space Debris, 2021.

## Slide 55
www.compass.polimi.it
Via La Masa, 34, 20159 Milano
Thank you for your attention
camilla.colombo@polimi.it